## Slide 1: Gemini: Rendezvous and Docking
INST 154
Apollo at 50
Gemini Flight Controller Orientation

## Slide 2: Gemini Objectives
To demonstrate endurance of humans and equipment in spaceflight for extended periods, at least eight days required for a Moon landing, to a maximum of two weeks [succeeded]
To effect rendezvous and docking with another vehicle, and to maneuver the combined spacecraft using the propulsion system of the target vehicle [succeeded]
To demonstrate Extra-Vehicular Activity (EVA), or space-"walks" outside the protection of the spacecraft, and to evaluate the astronauts' ability to perform tasks there [succeeded]
To perfect techniques of atmospheric reentry and touchdown at a pre-selected location on land [failed]

## Slide 6: Timeline
Mercury Mark II program approval December 1961
  Last Mercury mission May 1963
First uncrewed Gemini mission April 1964
First crewed Gemini mission March 1965
  First US Spacewalk June 1965
  First Rendezvous December 1965
  Last Gemini mission November 1966
Uncrewed Air Force Gemini B (MOL program) launch November 1966
  Air Force Manned Orbiting Laboratory program cancelled June 1969

## Slide 7: Rendezvous Missions (before Apollo 11)
Gemini 4 (second stage re-rendezvous) [venting, line of sight thrusting]

## Slide 8: Rendezvous Missions (before Apollo 11)
Gemini 4 (second stage re-rendezvous) [venting, line of sight thrusting]
Gemini 5 (Radar Evaluation Pod) [fuel cell problems]

## Slide 9: Rendezvous Missions (before Apollo 11)
Gemini 4 (second stage re-rendezvous) [venting, line of sight thrusting]
Gemini 5 (Radar Evaluation Pod) [fuel cell problems]
Gemini 6A (first rendezvous – with Gemini 7) [Agena fail, pad abort]

## Slide 12: Rendezvous Missions (before Apollo 11)
Gemini 4 (second stage re-rendezvous) [venting, line of sight thrusting]
Gemini 5 (Radar Evaluation Pod) [fuel cell problems]
Gemini 6A (first rendezvous – with Gemini 7) [Agena fail, pad abort]
Gemini 8 (first docking) [emergency reentry]
Gemini 9A (rendezvous from above) [backup crew, Atlas fail, ADTA fail]

## Slide 14: Rendezvous Missions (before Apollo 11)
Gemini 4 (second stage re-rendezvous) [venting, line of sight thrusting]
Gemini 5 (Radar Evaluation Pod) [fuel cell problems]
Gemini 6A (first rendezvous – with Gemini 7) [Agena fail, pad abort]
Gemini 8 (first docking) [emergency reentry]
Gemini 9A (rendezvous from above) [backup crew, Atlas fail, ADTA fail]
Gemini 10 (rendezvous with an uncooperative target)
Gemini 11 (rapid one-orbit rendezvous)
Gemini 12 (unplanned rendezvous without radar)
Apollo 9 (LM-active rendezvous)
Apollo 10 (Lunar Orbit Rendezvous)

## Slide 17: Rendezvous Missions (before Apollo 11)
Gemini 4 (second stage re-rendezvous) [venting, line of sight thrusting]
Gemini 5 (Radar Evaluation Pod) [fuel cell problems]
Gemini 6A (first rendezvous – with Gemini 7) [Agena fail, pad abort]
Gemini 8 (first docking) [emergency reentry]
Gemini 9A (rendezvous from above) [backup crew, Atlas fail, ADTA fail]
Gemini 10 (rendezvous with an uncooperative target)
Gemini 11 (rapid one-orbit rendezvous)
Gemini 12 (unplanned rendezvous without radar)
Apollo 9 (LM-active rendezvous)
Apollo 10 (Lunar Orbit Rendezvous)

## Slide 20: M=4 Rendezvous (Gemini 6A)

## Slide 21: Terminal Phase

## Slide 22: Braking Schedule
Apollo LOR:
6000 feet: -30 fps
3000 feet: -20 fps
1500 feet: -10 fps
600 feet: - 5 fps
Gemini 12 Pilot Report:
Braking was accomplished in increments, starting with a 3 ft/sec decrease to a closing rate of 45 ft/sec at the fourth midcourse correction. At a range of about 1.5 nautical miles, the closing rate had been decreased to about 17 ft/sec. The inertial indicators were used for an inertial reference during this period. The line-of-sight rates were very small throughout this portion of the braking sequence, requiring only one input correction, according to the inertial indicators. At a range of approximately one nautical mile, inertial reference was shifted to the stars.
From approximately one mile range, braking was accomplished in small increments. The analog range and range-rate indicators did not function during the braking phase. Position and closing rates were maintained by monitoring computer information and by visual observations of the target. At the completion of the rendezvous, the propellant-quantity-remaining indicator read 69 percent.

## Slide 24: Discussion Groups
Hacker chapter 12 (“Spirit of 76”)
  The story of the first rendezvous
FETM video episode 1 (“Can We Do This?”)
  NASA from the lunar landing decision through the end of Project Gemini
Summary Conference chapter 2 (“Summary of Rendezvous Operations”)
  A detailed review of Gemini rendezvous

## Slide 25: Long Duration Missions (before Shuttle/Mir)
Mercury-Atlas 9 1.4 days
Gemini 4 4.1 days
Gemini 5 7.9 days
Gemini 7 13.8 days
Skylab 2 28.0 days
Skylab 3 59.5 days
Skylab 4 84.1 days

## Slide 31: Team Project Status Reports
Due on ELMS before class this Thursday
  And a second one the Tuesday following Spring Break
Paragraph 1: What you have done so far
Paragraph 2: Problems you have encountered
  Only needed if you have had problems
  If you need help with problems, also send us an email!

## Slide 32: https://apolloinrealtime.org/11