## Slide 1: Networks
Session 1
INST 346
Technologies, Infrastructure and Architecture

## Slide 2: Goals for Today
Understand what a network is
Learn about the design of the Internet
Get an overview of the course

## Slide 3
Enrollment
Student
Course
Grade
…
Student
Student ID
First name
Last name
Department
E-mail
…
Course
Course ID
Course Name
…
Department
Department ID
Department Name
…
has
has
associated with

## Slide 4: Some Other Networks
Genealogy
Post office
Telephone
The Web
Bacon numbers

## Slide 5: The Internet

## Slide 6: The Internet
Global collection of public “IP” networks
  Private IP networks are often called “intranets”
Independent
  Each organization maintains its own network
Cooperating (e.g., ICANN)
  Internet Protocol (IP) address blocks
  Domain names

## Slide 7: A Short History of the Internet
1969: Origins in government research
  Advanced Research Projects Agency (ARPAnet)
  Key standards: UDP, TCP, DNS
1983: Design adopted by other agencies
  Created a need for inter-network connections
  Key standards: IP
Notes: Moore’s law make shift from large time sharing computer facilities to individual, small but powerful computer systems, and

## Slide 9
http://www.geog.ucl.ac.uk/casa/martin/atlas/isp_maps.html

## Slide 10: The Internet
Image from the Opte Project

## Slide 11: Types of Internet “Nodes”
Hosts
  Computers that use the network to do something
Routers
  Specialized computers that route packets
Gateway
  Routers that connect two networks
Firewall
  Gateways that pass packets selectively

## Slide 12: Types of Digital Links
“Backbone”
  Microwave
  Satellite
  Fiber
“Last mile” wired
  Telephone modem
  Cable modem
  Fiber
“Last mile” wireless
  Wi-Fi (IEEE 802.11)
  Mobile data (GSM, 4G)

## Slide 13: Layered Internmet Architecture
Link
Link
Link
Link
Link
Link
Network
Network
Network
Network
Virtual link for packets
Transport
Transport
Virtual link for end to end packets
Application
Application
Virtual network service
Link for bits
Link for bits
Link for bits

## Slide 14: Layering of airline functionality
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure
airport
arrival
airport
intermediate air-traffic
control centers
airplane routing
airplane routing
ticket (complain)
baggage (claim
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing
layers: each layer implements a service
  via its own internal-layer actions
  relying on services provided by layer below

## Slide 15: An Internet Protocol (IP) Address
IP address: 216.183.103.150
Identifies a LAN
Identifies a specific computer

## Slide 16: Hands-on: Learn About Your IP Address
Find your IP address
  Windows: “cmd” in the search box, then ipconfig /all
  Mac: open a Terminal, then ifconfig
See who “owns” that address
  Use http://remote.12dt.com/
See where in the world it (probably) is
  http://www.geobytes.com/ipLocator.htm

## Slide 17: Thinking About Speed
Two parts of moving data from here to there:
  Getting the first bit there (latency)
  Getting everything there (throughput)
Latency: Amount of time it takes data to travel from source to destination
Throughput: Amount of data that can be sent in some amount of time (e.g., 1 second)

## Slide 18: Modules
Application
Transport
Network
Link/Physical
TCP/IP "Stack"
Scenarios
Social Issues
Network Security
Overview
Exam 1
Exam 2
Final Exam

## Slide 19: Required Background
Algebra
Statistics
Programming
Database design

## Slide 20: Keys to Success
Don’t get behind
  20 pages or so of reading for every class
Use class to deepen your understanding
  You’re here to discuss it, not to listen to it!
Use homeworks and labs to gain mastery
  Work together, share ideas online
  Final submission must be written by you!
Proactively use office hours
  We can’t help if you don’t ask!

## Slide 21: Grading
No curve, no extra credit.
  90 for A-, 93 for A, etc.
No single-point failures
  50%: Best 2 of 3 exams (individual work)
  10%: Best 8 of 10 quizzes (individual work)
  20%: Best 4 of 5 homeworks (work together)
  20%: Best 4 of 5 labs (work together)
Attendance is not separately graded
  But it is strongly correlated with success

## Slide 22: Pair Up
Turn to the person next to you and discuss:
What do you most want to learn in this course?