## Slide 1: IP
Session 13
INST 346
Technologies, Infrastructure and Architecture

## Slide 2: Your Suggestions
State goals explicitly
More examples
  Animations, videos, demos
  In-class activities
  Draw more on the board
  Analogies from everyday life
Discuss every lab and homework
  Both in advance and afterwards
Provide links to supplemental sources

## Slide 3: Your Other Suggestions
Assign more homework (!)
Talk about every slide
Wake you up if you fall asleep

## Slide 4: Goals for Today
Exam results
Getting IPv4 to work
  DHCP, NAT, Fragmentation
IPv6
Getahead: Routing

## Slide 5: Network-layer functions
forwarding: move packets from router’s input to appropriate router output
data plane
control plane
Two approaches to structuring network control plane:
per-router control (traditional)
logically centralized control (software defined networking)
Recall: two network-layer functions:
routing: determine route taken by packets from source to destination

## Slide 6: Router architecture overview
high-seed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware) operttes in nanosecond timeframe
routing, management
control plane (software)
operates in millisecond
time frame
high-level view of generic router architecture:

## Slide 7: Switching via a bus
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access and enterprise routers
bus

## Slide 8: IP addressing
IP address: 32-bit identifier for host, router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 9: Longest prefix matching
Destination Address Range
11001000 00010111 00010*** *********
11001000 00010111 00011000 *********
11001000 00010111 00011*** *********
otherwise
DA: 11001000 00010111 00011000 10101010
examples:
DA: 11001000 00010111 00010110 10100001
which interface?
which interface?
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix matching
Link interface
0
1
2
3

## Slide 10: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network (more shortly)
DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg [optional]
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 11: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 12: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 13: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 14: DHCP: example
connecting laptop needs its IP address, addr of first-hop router, addr of DNS server: use DHCP
router with DHCP
server built into
router
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.1 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP

## Slide 15: DHCP: example
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulation of DHCP server, frame forwarded to client, demuxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DSN server, IP address of its first-hop router

## Slide 16: DHCP: Wireshark output (home LAN)
Message type: Boot Reply (2)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 192.168.1.101 (192.168.1.101)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 192.168.1.1 (192.168.1.1)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP ACK
Option: (t=54,l=4) Server Identifier = 192.168.1.1
Option: (t=1,l=4) Subnet Mask = 255.255.255.0
Option: (t=3,l=4) Router = 192.168.1.1
Option: (6) Domain Name Server
Length: 12; Value: 445747E2445749F244574092;
IP Address: 68.87.71.226;
IP Address: 68.87.73.242;
IP Address: 68.87.64.146
Option: (t=15,l=20) Domain Name = "hsd1.ma.comcast.net."
reply
Message type: Boot Request (1)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 0.0.0.0 (0.0.0.0)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 0.0.0.0 (0.0.0.0)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP Request
Option: (61) Client identifier
Length: 7; Value: 010016D323688A;
Hardware type: Ethernet
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Option: (t=50,l=4) Requested IP Address = 192.168.1.101
Option: (t=12,l=5) Host Name = "nomad"
Option: (55) Parameter Request List
Length: 11; Value: 010F03062C2E2F1F21F92B
1 = Subnet Mask; 15 = Domain Name
3 = Router; 6 = Domain Name Server
44 = NetBIOS over TCP/IP Name Server
……
request

## Slide 17: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,different source port numbers

## Slide 18: NAT: network address translation
motivation: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net not explicitly addressable, visible by outside world (a security plus)

## Slide 19: NAT: network address translation
implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 20: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 21: NAT: network address translation
16-bit port-number field:
  60,000 simultaneous connections with a single LAN-side address!
NAT is controversial:
  routers should only process up to layer 3
  address shortage should be solved by IPv6
  violates end-to-end argument
    NAT possibility must be taken into account by app designers, e.g., P2P applications
  NAT traversal: what if client wants to connect to server behind NAT?

## Slide 22: IP fragmentation, reassembly
network links have MTU (max.transfer size) - largest possible link-level frame
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…

## Slide 23: IP fragmentation, reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8

## Slide 24: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version
number
header length
(bytes)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
“type” of data
for
fragmentation/
reassembly
max number
remaining hops
(decremented at
each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 25: IPv6: motivation
initial motivation: 32-bit address space soon to be completely allocated.
additional motivation:
  header format helps speed processing/forwarding
  header changes to facilitate QoS
IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed

## Slide 26: IPv6 datagram format
priority: identify priority among datagrams in flow
flow Label: identify datagrams in same “flow.”
(concept of“flow” not well defined).
next header: identify upper layer protocol for data
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits

## Slide 27: Other changes from IPv4
checksum: removed entirely to reduce processing time at each hop
options: allowed, but outside of header, indicated by “Next Header” field
ICMPv6: new version of ICMP
  additional message types, e.g. “Packet Too Big”
  multicast group management functions

## Slide 28: Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  no “flag days”
  how will network operate with mixed IPv4 and IPv6 routers?
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields

## Slide 29: Tunneling
physical view:
IPv4
IPv4
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6

## Slide 30: Tunneling
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6
IPv4
IPv4

## Slide 31: IPv6: adoption
Google: 8% of clients access services via IPv6
NIST: 1/3 of all US government domains are IPv6 capable
Long (long!) time for deployment, use
  20 years and counting!
  think of application-level changes in last 20 years: WWW, Facebook, streaming media, Skype, …
  Why?

## Slide 32
Per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact with each other in control plane to compute forwarding tables
data
plane
control
plane

## Slide 33
data
plane
control
plane
Logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs) in routers to compute forwarding tables
Remote Controller
CA
CA
CA
CA
CA

## Slide 34
5.1 introduction
5.2 routing protocols
link state
distance vector
5.3 intra-AS routing in the Internet: OSPF
5.4 routing among the ISPs: BGP
5.5 The SDN control plane
5.6 ICMP: The Internet Control Message Protocol
5.7 Network management and SNMP
Chapter 5: outline

## Slide 35: Routing protocols
Routing protocol goal: determine “good” paths (equivalently, routes), from sending hosts to receiving host, through network of routers
path: sequence of routers packets will traverse in going from given initial source host to given final destination host
“good”: least “cost”, “fastest”, “least congested”
routing: a “top-10” networking challenge!

## Slide 36: Graph abstraction of the network
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
aside: graph abstraction is useful in other network contexts, e.g.,
P2P, where N is set of peers and E is set of TCP connections

## Slide 37: Graph abstraction: costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x’) = cost of link (x,x’)
e.g., c(w,z) = 5
cost could always be 1, or
inversely related to bandwidth,
or inversely related to
congestion
cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
key question: what is the least-cost path between u and z ?
routing algorithm: algorithm that finds that least cost path

## Slide 38: Routing algorithm classification
Q: global or decentralized information?
global:
all routers have complete topology, link cost info
“link state” algorithms
decentralized:
router knows physically-connected neighbors, link costs to neighbors
iterative process of computation, exchange of info with neighbors
“distance vector” algorithms
Q: static or dynamic?
static:
routes change slowly over time
dynamic:
routes change more quickly
  periodic update
  in response to link cost changes

## Slide 39: Distance vector algorithm
Dx(y) = estimate of least cost from x to y
  x maintains distance vector Dx = [Dx(y): y є N ]
node x:
  knows cost to each neighbor v: c(x,v)
  maintains its neighbors’ distance vectors. For each neighbor v, x maintains Dv = [Dv(y): y є N ]

## Slide 40: Distance vector algorithm
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
when x receives new DV estimate from neighbor, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)

## Slide 41: Distance vector algorithm
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
distributed:
each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors if necessary
wait for (change in local link cost or msg from neighbor)
recompute estimates
if DV to any dest has changed, notify neighbors
each node:

## Slide 42
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from

## Slide 43
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x
table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2
node y
table
node z
table
cost to
from

## Slide 44: Distance vector: link cost changes
link cost changes:
node detects local link cost change
updates routing info, recalculates distance vector
if DV changes, notify neighbors
“good
news
travels
fast”
x
z
1
4
50
y
1
t0 : y detects link-cost change, updates its DV, informs its neighbors.
t1 : z receives update from y, updates its table, computes new least cost to x , sends its neighbors its DV.
t2 : y receives z’s update, updates its distance table. y’s least costs do not change, so y does not send a message to z.
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 45: Distance vector: link cost changes
link cost changes:
node detects local link cost change
bad news travels slow - “count to infinity” problem!
44 iterations before algorithm stabilizes: see text
x
z
1
4
50
y
60
poisoned reverse:
If Z routes through Y to get to X :
  Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
will this completely solve count to infinity problem?

## Slide 46: Before You Go
On a sheet of paper, answer the following (ungraded) question (no names, please):
What one or two possible improvements to the way the class is being taught would make the most difference?