## Slide 1: Computing
Week 9
LBSC 671
Creating Information Infrastructures

## Slide 2: Midterm Results (Tentative)
Chart: 
 | 100 | 100 | 100 | 100 | 99 | 98 | 95 | 95 | 95 | 95 | 95 | 94 | 93 | 89 | 85 | 85 | 85 | 85 | 85 | 83 | 83 | 80 | 80 | 76 | 75 | 75 | 75 | 65

## Slide 3: Goals for Today
Understand what makes stupid computers seem smart
Understand how the Internet works

## Slide 5: A Very Brief History of Computing
Hardware
  Mechanical: essentially a big adding machine
  Analog: designed for calculus, limited accuracy
  Digital: early machines filled a room
  Microchips: designed for missile guidance
Software
  Numeric: computing gun angles
  Symbolic: code-breaking

## Slide 6: Commercial Developments
Mainframes (1960’s)
  IBM
Minicomputers(1970’s)
  DEC
Personal computers (1980’s)
  Apple, Microsoft
Networks (1990’s)
  Web
Convergence (2000’s)
  Cell phone/PDA, HDTV/Computer, …

## Slide 7
Source: Wikipedia

## Slide 8
Source: Wikipedia

## Slide 9
Source: Wikipedia

## Slide 10
Source: Wikipedia

## Slide 11
Source: Wikipedia

## Slide 12
Source: Wikipedia

## Slide 13: The Big Picture
Processor
Memory
Network

## Slide 14: Hardware Processing Cycle
Input comes from somewhere
  Keyboard, mouse, microphone, camera, …
The system does something with it
  Processor, memory, software, network, …
Output goes somewhere
  Monitor, speaker, robot controls, …

## Slide 15
Memory
Processor
Output
Input

## Slide 16: Computer Hardware
Central Processing Unit (CPU)
  Intel Xeon, Motorola Power PC, …
Communications “Bus”
  FSB, PCI, ISA, USB, Firewire, …
Storage devices
  Cache, RAM, hard drive, flash memory, …
External communications
  Modem, Ethernet, GPRS, 802.11, …

## Slide 17: “Solid-State” Memory
ROM
  Does not require power to retain content
  Used for “Basic Input/Output System” (BIOS)
Cache (Fast low-power “Static” RAM)
  Level 1 (L1) cache: small, single-purpose
  Level 2 (L2) cache: larger, shared
(“Dynamic”) RAM (Slower, power hungry)
  Reached over the “Front-Side Bus” (FSB)
Flash memory (fast read, slow write EEPROM)
  Reached over USB bus or SD socket
  Used in memory sticks (“non-volatile” storage)

## Slide 18
Extracted From Shelly Cashman Vermatt’s Discovering Computers 2004

## Slide 19: System Architecture
CPU
RAM
Hard
Drive
CD/
DVD
Cache
Motherboard
System Bus
Video
Card
Input
Controller
Keyboard
Mouse
Sound
Card
USB Port
L1
L2
Front Side Bus

## Slide 20: The Storage Hierarchy
Type | Speed | Size | Cost
Registers | ~300 ps | 256 B | Very expensive
Cache | ~1 ns | 4 MB | Expensive
RAM | ~10 ns | 1 GB | Cheap
Hard drive | ~10 ms | 1 TB | Very cheap

## Slide 21: File System
Paths specify location of files on a hard drive
Folder metaphor
  Hierarchically nested directories
  Absolute vs. relative paths
/afs/wam.umd.edu/home/wam/j/i/jimmylin/home
C:\Documents and Settings\Jimmy Lin\My Documents
../pub
..\Desktop
~/oard

## Slide 22: Directory Tree Exercise
First, visually explore the directory tree
  PC: Windows Explorer
  Mac: Finder
Then launch a shell
  PC: type cmd in search box
  Mac: Applications->Utiities->Terminal
Then navigate around
  “tree .”plots the tree from here (PC only)
  “dir” (PC) or “ls” (Mac) lists the present directory
  “cd WINDOWS” takes you “down” in the tree
  cd .. takes you “up” in the tree

## Slide 23: The Internet
Global collection of public “IP” networks
  Private networks are often called “intranets”
Independent
  Each organization maintains its own network
Cooperating
  Internet Protocol (IP) address blocks
  Domain names
  World-Wide Web Consortium (W3C)
  Computer Emergency Response Team (CERT)

## Slide 24: A Short History of the Internet
1969: Origins in government research
  Advanced Research Projects Agency (ARPAnet)
  Key standards: UDP, TCP, DNS
1983: Design adopted by other agencies
  Created a need for inter-network connections
  Key standards: IP
1991: World-Wide Web added point-and-click
  Now 908 million Internet “hosts” (July 2012)
  Key standards: HTTP, URL, HTML, XML
Notes: Moore’s law make shift from large time sharing computer facilities to individual, small but powerful computer systems, and

## Slide 25: What Changed in 1994?
Chart: 

## Slide 26: Types of Digital Channels
“Backbone”
  Microwave
  Satellite
  Fiber
“Last mile” wired
  ADSL
  Cable modem
  Fiber
“Last mile” wireless
  Wi-Fi (IEEE 802.11)
  GSM/4G

## Slide 27: A Network of Networks

## Slide 28
http://www.geog.ucl.ac.uk/casa/martin/atlas/isp_maps.html

## Slide 29: Thinking About Speed
Two parts of moving data from here to there:
  Getting the first bit there
  Getting everything there
Fundamentally, there’s no difference:
  Moving data from the processor to RAM
  Saving a file to disk
  Downloading music from a server in China

## Slide 30: Units of Time
Unit | Abbreviation | Duration (seconds)
second | sec/s | 1
millisecond | ms | 10-3 = 1/1,000
microsecond | ms | 10-6 = 1/1,000,000
nanosecond | ns | 10-9 = 1/1,000,000,000
picosecond | ps | 10-12 = 1/1,000,000,000,000
femtosecond | fs | 10-15 = 1/1,000,000,000,000,000

## Slide 31: Units of Frequency
Unit | Abbreviation | Operations per second
hertz | Hz | 1
kilohertz | KHz | 103 = 1,000
megahertz | MHz | 106 = 1,000,000
gigahertz | GHz | 109 = 1,000,000,000

## Slide 32: Units of Size
Unit | Abbreviation | Size (bytes)
bit | b | 1/8
byte | B | 1
kilobyte | KB | 210 = 1024
megabyte | MB | 220 = 1,048,576
gigabyte | GB | 230 = 1,073,741,824
terabyte | TB | 240 = 1,099,511,627,776
petabyte | PB | 250 = 1,125,899,906,842,624

## Slide 33: Some Definitions
Latency
  The amount of time it takes data to travel from source to destination
Bandwidth
  The amount of data that can be transmitted in a fixed amount of time

## Slide 34: Types of Internet “Nodes”
Hosts
  Computers that use the network to do something
Routers
  Specialized computers that route packets
Gateway
  Routers that connect two networks
Firewall
  Gateways that pass packets selectively

## Slide 35: IP Address
Every host (and every router) is identified by an “Internet Protocol” (IP) address
32 bit number, divided into four “octets”
128.8.11.33
216.239.39.99
199.181.132.250
Example: point your browser at http://128.8.237.77/

## Slide 36: An Internet Protocol (IP) Address
IP address: 216.183.103.150
Identifies a LAN
Identifies a specific computer

## Slide 37: Dynamic IP Addresses
Dynamic Host Configuration Protocol (DHCP)

## Slide 38: Hands-on: Learn About Your IP Address
Find your IP address
  Bring up a command window
    In Windows, type “cmd” in the search box!
  Type “ipconfig /all” (and press enter)
See who “owns” that address
  Use http://remote.12dt.com/
See where in the world it (probably) is
  http://www.geobytes.com/ipLocator.htm

## Slide 39: Routing Tables
IP Prefix | Next Router | Estimated Delay
216.141.xxx.xxx | 120.0.0.0 | 18 ms
216.xxx.xxx.xxx | 121.0.0.0 | 34 ms
101.42.224.xxx | 120.0.0.0 | 21 ms
xxx.xxx.xxx.xxx | 121.0.0.0 | 250 ms
45.0.2.10
120.0.0.0
121.0.0.0

## Slide 40: TraceRoute
See how packets get from South Africa to you
  http://services.truteq.com/
Look at the same data visually
  http://visualroute.visualware.com/

## Slide 41: Domain Name Service (DNS)
“Domain names” improve usability
  Easier to remember than IP addresses
  Written like a postal address: specific-to-general
Each “name server” knows one level of names
  “Top level” name servers know .edu, .com, .mil, …
  .edu name server knows umd, umbc, stanford, …
  .umd.edu name server knows wam, ischool, ttclass, …
  .wam.umd.edu name server knows rac1, rac2, …

## Slide 42: IP Addresses and Domain Names
Domain Name: wam.umd.edu
IP address: 128.8.10.142

## Slide 43: Uniform Resource Locator (URL)
Uniquely identify Web pages
http://www.glue.umd.edu:80/~oard/teaching.html
Domain name
Path
File name
Port
Protocol

## Slide 44: Ports
Well-known ports
  22 Secure Shell (for SSH and SFTP)
  25 Simple Mail Transfer Protocol (SMTP)
  53 Domain Name System (DNS)
  68 Dynamic Host Configuration Protocol (DHCP)
  80 Hypertext Transfer Protocol (HTTP)
  143 Internet Message Access Protocol (IMAP)
  554 Real-Time Streaming Protolol (RTSP)
Registered Ports
  8080 HTTP server run by ordinary users
Ephemeral Ports

## Slide 45: Port Mapping
Internet Service providers lease one IP address
  But home networks may contain many machines
Network Address Translation (NAT)
  Each internal machine gets a private IP address
  Ports on internal machines are mapped both ways
Port forwarding
  Permits public server to run in the local network

## Slide 46: The TCP/IP “Protocol Stack”
Link layer moves bits
  Ethernet, cable modem, DSL
Network layer moves packets
  IP
Transport layer provides services to applications
  UDP, TCP
Application layer uses those services
  DNS, SFTP, SSH, …

## Slide 47: TCP/IP layer architecture
Link
Link
Link
Link
Link
Link
Network
Network
Network
Network
Virtual link for packets
Transport
Transport
Virtual link for end to end packets
Application
Application
Virtual network service
Link for bits
Link for bits
Link for bits

## Slide 48: Transmission Control Protocol (TCP)
Built on the network-layer version of UDP
Guarantees delivery all data
  Retransmits missing data
Guarantees data will be delivered in order
  “Buffers” subsequent packets if necessary
No guarantee of delivery time
  Long delays may occur without warning

## Slide 49: User Datagram Protocol (UDP)
The Internet’s basic transport service
  Sends every packet immediately
  Passes received packets to the application
No delivery guarantee
  Collisions can result in packet loss
Example: sending clicks on web browser
Notes: No connection establishment. As we shall discuss in Section 3.5, TCP uses a three-way handshake before it starts to transfer data. UDP just blasts away without any formal preliminaries. Thus UDP does not introduce any delay to establish a connection. This is probably the principle reason why DNS runs over UDP rather than TCP -- DNS would be much slower if it ran over TCP. HTTP uses TCP rather than UDP, since reliability is critical for Web pages with text. But, as we briefly discussed in Section 2.2, the TCP connection establishment delay in HTTP is an important contributor to the "world wide wait".
No connection state. TCP maintains connection state in the end systems. This connection state includes receive and send buffers, congestion control parameters, and sequence and acknowledgment number parameters. We will see in Section 3.5 that this state information is needed to implement TCP's reliable data transfer service and to provide congestion control. UDP, on the other hand, does not maintain connection state and does not track any of these parameters. For this reason, a server devoted to a particular application can typically support many more active clients when the application runs over UDP rather than TCP.
Small segment header overhead. The TCP segment has 20 bytes of header overhead in every segment, whereas UDP only has 8 bytes of overhead.
Unregulated send rate. TCP has a congestion control mechanism that throttles the sender when one or more links between sender and receiver becomes excessively congested. This throttling can have a severe impact on real-time applications, which can tolerate some packet loss but require a minimum send rate. On the other hand, the speed at which UDP sends data is only constrained by the rate at which the application generates data, the capabilities of the source (CPU, clock rate, etc.) and the access bandwidth to the Internet. We should keep in mind, however, that the receiving host does not necessarily receive all the data - when the network is congested, a significant fraction of the UDP-transmitted data could be lost due to router buffer overflow. Thus, the receive rate is limited by network congestion even if the sending rate is not constrained.

## Slide 50: UDP/IP Protocol Stack

## Slide 51: File Transfer Program (FTP)
Used to move files between machines
  Upload (put) moves from client to server
  Download (get) moves files from server to client
Both visual and command line interfaces available
Normally requires an account on the server
  Userid “anonymous” provides public access

## Slide 52: Hands On: Graphical Secure FTP
SFTP to “terpconnect.umd.edu”
Change directory to “/pub/USERID”
Upload or download files
You can see these files at: http://terpconnect.umd.edu/~USERID/

## Slide 53: Network Abuse
Flooding
  Excessive activity, intended to prevent valid activity
Worms
  Like a virus, but self-propagating
Sniffing
  Monitoring network traffic (e.g., for passwords)

## Slide 54: Encryption
Secret-key systems (e.g., DES)
  Use the same key to encrypt and decrypt
Public-key systems (e.g., PGP)
  Public key: open, for encryption
  Private key: secret, for decryption
Digital signatures
  Encrypt with private key, decrypt with public key

## Slide 55: Encrypted Standards
Secure Shell (SSH)
  Replaces Telnet
Secure FTP (SFTP)/Secure Copy (SCP)
  Replaces FTP
Secure HTTP (HTTPS)
  Used for financial and other private data
Wired Equivalent Protocol (WEP)
  Used on wireless networks
Virtual Private Network (VPN)
  Not really a “standard”

## Slide 56: Virtual Private Networks
Intranet
Intranet
a secure private network over the public Internet
Public Internet
virtual “leased line”

## Slide 57: Internet  Web
Internet: collection of global networks
Web: way of managing information exchange
There are many other uses for the Internet
  File transfer (FTP)
  Email (SMTP, POP, IMAP)

## Slide 58: The World-Wide Web
Remote Sever
Send Request
Requested Page
Fetch Page
Proxy Server
Local copy of
Page requested
My Browser
Internet
Notes: A server that sits between a client application, such as a Web browser, and a real server. It intercepts all requests to the real server to see if it can fulfill the requests itself. If not, it forwards the request to the real server. Proxy servers have two main purposes:
Improve Performance: Proxy servers can dramatically improve performance for groups of users. This is because it saves the results of all requests for a certain amount of time. Consider the case where both user X and user Y access the World Wide Web through a proxy server. First user X requests a certain Web page, which we'll call Page 1. Sometime later, user Y requests the same page. Instead of forwarding the request to the Web server where Page 1 resides, which can be a time-consuming operation, the proxy server simply returns the Page 1 that it already fetched for user X. Since the proxy server is often on the same network as the user, this is a much faster operation. Real proxy servers support hundreds or thousands of users. The major online services such as Compuserve and America Online, for example, employ an array of proxy servers.
Filter Requests: Proxy servers can also be used to filter requests. For example, a company might use a proxy server to prevent its employees from accessing a specific set of Web sites.

## Slide 59
HTML
(data/display)
Internet
communication
protocols
RTSP
FTP
Email
Web
Server
HTTP
(transfer)
File System
URL
(e.g.,http://www.foo.org/snarf.html)
HTML
HTTP
URL
“The Web”

## Slide 60: Web Standards
HTML
  How to write and interpret the information
URL
  Where to find it
HTTP
  How to get it
Notes: Link this to postal service

## Slide 61: HyperText Transfer Protocol (HTTP)
Send request
  GET /path/file.html HTTP/1.0
  From: someuser@jmarshall.com
  User-Agent: HTTPTool/1.0
Server response
  HTTP/1.0 200 OK
  Date: Fri, 31 Dec 1999 23:59:59 GMT
  Content-Type: text/html
  Content-Length: 1354
  <html><body> <h1>Happy New Millennium!</h1> … </body> </html>
Notes: The Difference Between FTP and HTTP File Transfer Protocol, or FTP, is a protocol used to upload files from a workstation to a FTP server or download files from a FTP server to a workstation. It is the way that files get transferred from one device to another in order for the files to be available on the Internet. When ftp appears in a URL it means that the user is connecting to a file server and not a Web server and that some form of file transfer is going to take place. Most FTP servers require the user to log on to the server in order to transfer files. In contrast, Hyper Text Transfer Protocol, or HTTP, is a protocol used to transfer files from a Web server onto a browser in order to view a Web page that is on the Internet. Unlike FTP, where entire files are transferred from one device to another and copied into memory, HTTP only transfers the contents of a web page into a browser for viewing. FTP is a two-way system as files are transferred back and forth between server and workstation. HTTP is a one-way system as files are transported only from the server onto the workstation's browser. When http appears in a URL it means that the user is connecting to a Web server and not a file server. The files are transferred but not downloaded, therefore not copied into the memory of the receiving device.

## Slide 62: Before You Go
On a sheet of paper, answer the following (ungraded) question (no names, please):
What was the muddiest point in today’s class?