## Slide 1: ENEE446: Digital Computer Design
Uzi Vishkin
Electrical and Computer Engineering Dept

## Slide 2: Why is this course becoming more interesting?
Yesterday: Top of the line machines were parallel
Today: Parallelism is becoming the norm for all classes of machines, from mobile devices to the fastest machines
Tomorrow: Far less clear than you would expect. Documented: 1. significant displeasure with vendors’ microprocessors, 2. no agreed platform

## Slide 3: Commodity computer systems
Chapter 1 19462003: Serial. 5KHz4GHz.
Chapter 2 2004--: Parallel. #”cores”: ~dy-2005
2005: 1 core. 2015: 100 (?) cores
2020: 1000 (?) cores
Windows 7: scaled to 256 cores…
how to use the remaining 255?
Is this the role of the OS?
BIG NEWS
Clock frequency growth: flat.
If you want your program to run significantly faster … you’re going to have to parallelize it  Parallelism: only game in town
#Transistors/chip 19802010s: 29K30B!
Programmer’s IQ? Flat..
40 years of parallel computing
The world is yet to see a successful general-purpose parallel computer: Easy to program & good speedups
Intel Platform 2015, March05
Notes: 3

## Slide 4: Welcome to current Impasse
All vendors committed to multi-cores. Yet, their architecture not stable:
The Trouble with Multicore: Chipmakers are busy designing microprocessors that most programmers can't handle—D. Patterson, IEEE Spectrum Jul’10.
See course info sheet for National Research Council, 2011: only hero programmers can exploit the vast parallelism in today’s machines.
Recommend: invent new stack (algorithms, programming model, HW)
3. V-CACM11: The software spiral (HW improvements  SW imp  HW imp) – growth engine for IT (A. Grove, Intel); Alas, now broken!
SW vendors avoid investment in long-term SW development since may bet on the wrong horse. Impasse bad for business.
Notes: 4

## Slide 5: Known Pain of Parallel Programming
Parallel programming is currently too difficult:
Term ‘parallel SW crisis’ used since 1991 following a CACM paper
To many users programming existing parallel computers is “as intimidating and time consuming as programming in assembly language” [NSF Blue-Ribbon Panel on Cyberinfrastructure, 2003].
AMD/Intel 2006: “Need PhD in CS to program today’s multicores”.
I will argue:
40yr old problem: Parallel architectures built using the following “methodology”: build-first figure-out-how-to-program-later.
[J. Hennessy: “Many of the early ideas were motivated by observations of what was easy to implement in the hardware rather than what was easy to use”]
This course: less about who is right; more about how to reason
Notes: 5

## Slide 6: Example of a problem to be discussed:1 or 2 Paradigm Shifts?
Serial to parallel: widely agreed
Within parallel: Existing “decomposition-first” paradigms. Painful to program.
Will there be a switch to a different (easier-to-program) paradigm?

## Slide 7: Architecture ‘Laws’
A Driving Metaphor (Wikipedia)
Amdahl's Law approximately suggests:
“ Suppose a car is traveling between two cities 60 miles apart, and has already spent one hour traveling half the distance at 30 mph. No matter how fast you drive the last half, it is impossible to achieve 90 mph average before reaching the second city. Since it has already taken you 1 hour and you only have a distance of 60 miles total; going infinitely fast you would only achieve 60 mph. ” Strong scaling Distance given; how fast can you make it?
Gustafson's Law (~where parallel machines are today) approximately states:
“ Suppose a car has already been traveling for some time at less than 90mph. Given enough time and distance to travel, the car's average speed can always eventually reach 90mph, no matter how long or how slowly it has already traveled. For example, if the car spent one hour at 30 mph, it could achieve this by driving at 120 mph for two additional hours, or at 150 mph for an hour, and so on.” Weak scaling How far you need to go for given speed?
The quantitative methodology we will learn in ENEE446 mandates rigorous understanding and application of such laws. But, what do they really say? Often: simplistic interpretations that neglect impact beyond HW organization
Driving metaphor: but where is the driver? driving at 150 mph and 30 mph are different. Perhaps, fast driveability (i.e., programmability) becomes #1 issue

## Slide 8: Flavor of parallelism: 1st example
Exchange Problem Replace A and B. Ex. A=2,B=5A=5,B=2.
Serial Alg: X:=A;A:=B;B:=X. 3 Ops. 3 Steps. Space 1.
Fewer steps (FS): X:=A B:=X
Y:=B A:=Y 4 ops. 2 Steps. Space 2.
Array Exchange Problem Given A[1..n] & B[1..n], replace A(i) and B(i), i=1..n.
Serial Alg: For i=1 to n do
X:=A(i);A(i):=B(i);B(i):=X /*serial replace
3n Ops. 3n Steps. Space 1.
Par Alg1: For i=1 to n pardo
X(i):=A(i);A(i):=B(i);B(i):=X(i) /*serial replace in parallel
3n Ops. 3 Steps. Space n.
Par Alg2: For i=1 to n pardo
X(i):=A(i) B(i):=X(i)
Y(i):=B(i) A(i):=Y(i) /*FS in parallel
4n Ops. 2 Steps. Space 2n.
Discussion
Par Alg 1 (and 2) Allows ‘decomposition’.
Parallelism requires extra space (memory).
Par Alg 1 clearly faster than Serial Alg.
Is Par Alg 2 preferred to Par Alg 1? [ParAlg 2 (and FS) reminds of ILP – easy form of (name) dependence]
Notes: 8

## Slide 9
Input: (i) All world airports.
(ii) For each, all airports to which there is a non-stop flight.
Find: smallest number of flights from DCA to every other airport.
Basic algorithm
Step i:
For all airports requiring i-1flights
For all its outgoing flights
Mark (concurrently!) all “yet unvisited” airports as requiring i flights (note nesting)
Serial: uses “serial queue”.
O(T) time; T – total # of flights
Parallel: parallel data-structures.
Inherent serialization: S.
Gain relative to serial: (first cut) ~T/S!
Decisive also relative to coarse-grained parallelism.
Note: (i) “Concurrently”: only change to serial algorithm
(ii) No “decomposition”/”partition”
POINTS: 1. Mental effort is considerably easier than for any of the computers currently sold.
2. This algorithm appears in a recent basic parallel computing curriculum; BUT no language + computer it recommends allows any speedups..
3. S depends on input graph .. A world beyond current architecture ‘laws’
Flavor of parallelism: 2nd example
Notes: 9

## Slide 10
Notes: 10

## Slide 11
Notes: 11

## Slide 12
Notes: 12

## Slide 13
Notes: 13

## Slide 14: Need
A general-purpose parallel computer framework [“successor to the Pentium for the many-core era”] that:
is easy to program;
gives good performance with any amount of parallelism provided by the algorithm; namely, up- and down-scalability including backwards compatibility on serial code;
supports application programming (VHDL/Verilog, OpenGL, MATLAB) and performance programming; and
fits current chip technology and scales with it.
(in particular: strong speed-ups for single-task completion time)
Notes: 14

## Slide 15: High-level objective of this course
advance you to discussing these issues in a critical & knowledgeable way
But why should you care? If for nothing else: Rising emphasis in job interviews
Two types of job interview impressions:
1. Just tell me what to do. I am great at delivering what I am told.
2. I recognize that functioning (even objectives) of products/services constantly evolves. Governed by a feedback loop between business development and technical specs, this evolution requires willingness from both techies and biz dev guys to go more than half way in order to understand the other side. I am interested in doing what it takes to make sure that anything I am doing stays on track towards a product that customers find attractive/competitive
Whom would you hire? in general, and for what jobs?
In what direction is globalization pushing job opportunities?