## Slide 1
Chapter 1
Fundamentals of Quantitative Design and Analysis
Computer Architecture
A Quantitative Approach, Fifth Edition

## Slide 2: Computer Technology
Performance improvements:
  Improvements in semiconductor technology
    Feature size, clock speed
  Improvements in computer architectures
    Enabled by HLL compilers, UNIX new archno new OS
    Lead to RISC architectures but X86 is CISC?
  Together have enabled:
    Lightweight computers
    Productivity-based managed/interpreted programming languages
Introduction

## Slide 3: Single Processor Performance
Introduction
RISC
Move to multi-processor
X86 was good enough, till PMD

## Slide 4: Current Trends in Architecture
Cannot continue to leverage Instruction-Level parallelism (ILP) (basically, assuming serial code)
  Single processor performance improvement ended in 2003
New models for performance:
  Data-level parallelism (DLP) Operate on many data items at the same time
  Thread-level parallelism (TLP) Tasks of work, operate independently and hopefully in parallel
These require explicit restructuring of the application
Don’t blame yourself if you find this confusing. See comments on SIMT in Fig 4.25, p. 314.
Introduction

## Slide 5: Classes of Computers
  Personal Mobile Device (PMD) $10 - $100s Standard ARM
  e.g. smart phones, tablet computers
  Emphasis on energy efficiency and real-time
Desktop Computing $300 – $2,500 Standard X86
  Emphasis on price-performance
Servers $5,000 - $10M
  Emphasis on availability, scalability, throughput
Clusters / Warehouse Scale Computers $100K - $200M
  Used for “Software as a Service (SaaS)”
  Emphasis on availability and price-performance
  Sub-class: Supercomputers, emphasis: floating-point performance and fast internal networks
Embedded Computers $10 - $100K
  Emphasis: price & application specific
Classes of Computers

## Slide 6: Parallelism
Classes of parallelism in applications:
  Data-Level Parallelism (DLP)
  Task-Level Parallelism (TLP)
  Request-Level Parallelism (RLP) – Many requests per second (Google queries); mostly independent
Classes of Computers

## Slide 7: Parallelism
Classes of architectural parallelism:
  Instruction-Level Parallelism (ILP) Exploits DLP at modest level. Compiler help. Pipelining. Speculative execution. ‘Out-of-order’ execution of serial code.
  Vector architectures/Graphic Processor Units (GPUs) Exploits DLP by applying a single instruction to a collection of data in parallel
  Thread-Level Parallelism Exploits either DLP or TLP. Tightly coupled HW model. Allows interaction among threads
  What if DLP defies single instruction and long enough threads?
  Request-Level Parallelism Exploits parallelism among largely decoupled tasks. Source: programmer or OS.
Classes of Computers

## Slide 8: Flynn’s Taxonomy
Single instruction stream, single data stream (SISD)
Single instruction stream, multiple data streams (SIMD)
  Vector architectures
  Multimedia extensions
  Graphics processor units
Multiple instruction streams, single data stream (MISD)
  No commercial implementation
Multiple instruction streams, multiple data streams (MIMD)
  Tightly-coupled MIMD
  Loosely-coupled MIMD
Classes of Computers

## Slide 9: Defining Computer Architecture
“Old” view of computer architecture:
  Instruction Set Architecture (ISA) design
  i.e. decisions regarding:
    registers, memory addressing, addressing modes, instruction operands, available operations, control flow instructions, instruction encoding
“Real” computer architecture:
  Design to meet specific requirements of the target machine
  Design to maximize performance within constraints: cost, power, and availability
  Includes ISA, microarchitecture, hardware
Defining Computer Architecture

## Slide 10: Trends in Technology
Integrated circuit technology
  Transistor density: 35%/year
  Die size: 10-20%/year
  Integration overall: 40-55%/year
DRAM capacity: 25-40%/year (slowing)
Flash (electrically erasable programmable read-only memory; standard storage device for PMD; nonvolatile) capacity: 50-60%/year
  15-20X cheaper/bit than DRAM
Magnetic disk technology: 40%/year
  15-25X cheaper/bit than Flash
  300-500X cheaper/bit than DRAM
Trends in Technology

## Slide 11: Bandwidth and Latency
Bandwidth or throughput
  Total work done in a given time (e.g., MBs/sec)
  10,000-25,000X improvement for processors
  300-1200X improvement for memory and disks
Latency or response time
  Time between start and completion of an event
  30-80X improvement for processors
  6-8X improvement for memory and disks
Trends in Technology

## Slide 12: Bandwidth and Latency
Log-log plot of bandwidth and latency milestones
Trends in Technology

## Slide 13: Transistors and Wires
Feature size
  Minimum size of transistor or wire in x or y dimension
  10 microns in 1971 to .032 microns in 2011 and .014 microns (14nm) in 2014
  Transistor performance scales linearly
    Wire delay does not improve with feature size!
  Integration density scales quadratically. Namely, the projected 10nm in 2016 means 1M larger density since 1971. Increase in die size is extra…
Trends in Technology

## Slide 14: Power and Energy
Problem: Get power in, get power out
Thermal Design Power (TDP)
  Characterizes sustained power consumption
  Used as target for power supply and cooling system
  Lower than peak power, higher than average power consumption
Clock rate can be reduced dynamically to limit power consumption
Energy per task is often a better measurement
Trends in Power and Energy

## Slide 15: Dynamic Energy and Power
Dynamic energy
  Transistor switch from 0 -> 1 or 1 -> 0
  ½ x Capacitive load x Voltage2
Dynamic power
  ½ x Capacitive load x Voltage2 x Frequency switched
Reducing clock rate reduces power, not energy
Trends in Power and Energy

## Slide 16: Power
Intel 80386 consumed ~ 2 W
3.3 GHz Intel Core i7 consumes 130 W
Heat must be dissipated from 1.5 x 1.5 cm chip
This is the limit of what can be cooled by air
Trends in Power and Energy

## Slide 17: Reducing Power
Techniques for reducing power:
  Do nothing well Turn off clock of inactive modules
  Dynamic Voltage-Frequency Scaling Multiple clock frequencies and voltages. Switch among them
  Low power state for DRAM, disks
  Overclocking, turning off cores If safe run one core faster. Turn off others
Trends in Power and Energy

## Slide 18: Static Power
Static power consumption
  Currentstatic x Voltage
  Scales with number of transistors
  To reduce: power gating (turn off)
Trends in Power and Energy

## Slide 19: Trends in Cost
Cost driven down by learning curve
  Yield
DRAM: price closely tracks cost
Microprocessors: price depends on volume
  10% less for each doubling of volume
Trends in Cost

## Slide 20: Integrated Circuit Cost
Integrated circuit
Bose-Einstein formula:
Defects per unit area = 0.016-0.057 defects per square cm (2010)
N = process-complexity factor = 11.5-15.5 (40 nm, 2010)
Trends in Cost

## Slide 21: Dependability
Module reliability
  Mean time to failure (MTTF)
  Mean time to repair (MTTR)
  Mean time between failures (MTBF) = MTTF + MTTR
  Availability = MTTF / MTBF
Dependability

## Slide 22: Measuring Performance
Typical performance metrics:
  Response time
  Throughput Total amount of work done in a given time
Speedup of X relative to Y
  Execution timeY / Execution timeX
Execution time
  Wall clock time: includes all system overheads
  CPU time: only computation time
Benchmarks
  Kernels (e.g. matrix multiply)
  Toy programs (e.g. sorting)
  Synthetic benchmarks (e.g. Dhrystone)
  Benchmark suites (e.g. SPEC06fp, TPC-C). Very impressive (well rounded) representation of applications. Even they must keep changing. Why?
  Problems (not in text): Vendor representatives set them.
  The next generation of computers: optimized for code that was
  optimized for current (or older) computers  inertia
Measuring Performance

## Slide 23: Principles of Computer Design
Take Advantage of Parallelism
  e.g. multiple processors, disks, memory banks, pipelining, multiple functional units
Principle of Locality
  Reuse of data and instructions
  (Evidence for serial code. But, what about parallel?)
  Temporal Locality (Locality in Time): If an item is referenced, it will tend to be referenced again soon (e.g., loops, reuse)
  Spatial Locality (Locality in Space): If an item is referenced, items whose addresses are close by tend to be referenced soon (e.g., straight-line code, array access)
Principles

## Slide 24: Principles of Computer Design cnt’d
Focus on the Common Case
  If overflow is rare in addition, optimize for simpler case
  Amdahl’s Law Drive 2hrs@30MPH. With 1hr@30MPH speedup is <= 2
Principles

## Slide 25: Principles of Computer Design
The Processor Performance Equation
Principles
HW technology
& organization
Organization
& ISA
ISA &
Compiler
Technology
For a given
program

## Slide 26: Pitfall: Mutiprocessors are a silver bullet
Switch to multiple processors ~2005, not due to insight on parallel programming or architecture breakthrough
Rather: power walls and ILP walls
Performance is now the programmer’s burden – not in the processor performance equation…
Popular version of “Moore’s law” – increasing performance with each generation – is now up to the programmer

## Slide 27: Principles of Computer Design
Principles
Different instruction types having different CPIs