## Slide 1
Chapter 4
Data-Level Parallelism in Vector, SIMD, and GPU Architectures
Computer Architecture
A Quantitative Approach, Fifth Edition

## Slide 2: Introduction
SIMD architectures can exploit significant data-level parallelism for:
  matrix-oriented scientific computing
  media-oriented image and sound processors
SIMD is more energy efficient than MIMD
  Only needs to fetch one instruction per data operation
  Makes SIMD attractive for personal mobile devices
SIMD allows programmer to continue to think sequentially
Introduction
Notes: XMT is MIMD, but still no need to do multiple fetches. Only broadcast to multiple processors.
XMT allow programmers to continue to think in a mathematically inductive way

## Slide 3: SIMD Parallelism
Vector architectures
SIMD extensions
Graphics Processor Units (GPUs)
For x86 processors:
  Expect two additional cores per chip per year
  SIMD width to double every four years
  Potential speedup from SIMD to be twice that from MIMD! Qualifier: X86 processors
Introduction
Notes: XMT allows much more than 2 more TCUs (or cores) per year

## Slide 4: Vector Architectures
Basic idea:
  Read sets of data elements into “vector registers”
  Operate on those registers
  Disperse the results back into memory
Registers are controlled by compiler
  Used to hide memory latency
  Leverage memory bandwidth
Vector Architectures

## Slide 5: VMIPS
Example architecture: VMIPS
  Loosely based on Cray-1
  Vector registers
    Each register holds a 64-element, 64 bits/element vector
    Register file has 16 read ports and 8 write ports
  Vector functional units
    Fully pipelined
    Data and control hazards are detected
  Vector load-store unit
    Fully pipelined
    One word per clock cycle after initial latency
  Scalar registers
    32 general-purpose registers
    32 floating-point registers
Vector Architectures

## Slide 6: VMIPS Instructions
ADDVV.D: add two vectors
ADDVS.D: add vector to a scalar
LV/SV: vector load and vector store from address
Example aX+Y,DAXPY Double-precision real Alpha X Plus Y
  L.D F0,a ; load scalar a
  LV V1,Rx ; load vector X
  MULVS.D V2,V1,F0 ; vector-scalar multiply
  LV V3,Ry ; load vector Y
  ADDVV V4,V2,V3 ; add
  SV Ry,V4 ; store the result
Requires 6 instructions vs. almost 600 for MIPS
Vector Architectures

## Slide 7: Vector Execution Time
Execution time depends on three factors:
  Length of operand vectors
  Structural hazards
  Data dependencies
VMIPS functional units consume one element per clock cycle
  For simplicity One pipeline lane, and initiation rate (rate in which vector unit consumes new operands and produce new results) is one element per clock for individual operations Execution time is approximately the vector length
Convoy
  Set of vector instructions that could potentially execute together without structural hazard. Property of code+HW
  Can estimate performance by # of convoys
Vector Architectures

## Slide 8: Chimes
Sequences with read-after-write dependency hazards can be in the same convoy via chaining
Chaining
  Allows a vector operation to start as soon as the individual elements of its vector source operand become available ’enhanced forwarding’
Chime
  Unit of time to execute one convoy
  m convoys executes in m chimes
  For vector length of n, requires m x n clock cycles
Vector Architectures

## Slide 9: Example
LV V1,Rx ;load vector X
MULVS.D V2,V1,F0 ;vector-scalar multiply
LV V3,Ry ;load vector Y
ADDVV.D V4,V2,V3 ;add two vectors
SV Ry,V4 ;store the sum
Convoys:
1 LV MULVS.D chaining
2 LV ADDVV.D separate convoy since structural hazard among LV instructions
3 SV
Since 3 chimes and 2 FP ops per result, the cycles per FLOP = 1.5
For 64 element vectors, requires 64 x 3 = 192 clock cycles
Vector Architectures

## Slide 10: Challenges
Start up time
  Latency of vector functional unit ignored by the chime model
  Assume the same as Cray-1
    Floating-point add => 6 clock cycles
    Floating-point multiply => 7 clock cycles
    Floating-point divide => 20 clock cycles
    Vector load => 12 clock cycles
Improvements: follow in the slides ahead
  > 1 element per clock cycle
  Non-64 wide vectors
  IF statements in vector code
  Memory system optimizations to support vector processors
  Multiple dimensional matrices
  Sparse matrices
  Programming a vector computer
Vector Architectures

## Slide 11: Multiple Lanes
Element n of vector register A is “hardwired” to element n of vector register B
  Allows for multiple hardware lanes
Vector Architectures

## Slide 12: Vector Length Register
Vector length not known at compile time?
Use Vector Length Register (VLR)
Use strip mining for vectors over the maximum vector length (MVL):
  low = 0;
  VL = (n % MVL); /*find odd-size piece using modulo op % */
  for (j = 0; j <= (n/MVL); j=j+1) { /*outer loop*/
  for (i = low; i < (low+VL); i=i+1) /*runs for length VL*/
  Y[i] = a * X[i] + Y[i] ; /*main operation*/
  low = low + VL; /*start of next vector*/
  VL = MVL; /*reset the length to maximum vector length*/
  }
Vector Architectures
First odd size, then MVL

## Slide 13: Vector Mask Registers
Consider:
for (i = 0; i < 64; i=i+1)
if (X[i] != 0)
X[i] = X[i] – Y[i];
Use vector mask register to “disable” elements:
LV V1,Rx ;load vector X into V1
LV V2,Ry ;load vector Y
L.D F0,#0 ;load FP zero into F0
SNEVS.D V1,F0 ;sets VM(i) to 1 if V1(i)!=F0
SUBVV.D V1,V1,V2 ;subtract under vector mask
SV Rx,V1 ;store the result in X
GFLOPS rate decreases!
Vector Architectures

## Slide 14: Memory Banks
Memory system must be designed to support high bandwidth for vector loads and stores
Spread accesses across multiple banks
  Control bank addresses independently
  Load or store non sequential words
  Support multiple vector processors sharing the same memory
Example:
  32 processors, each generating 4 loads and 2 stores/cycle
  Processor cycle time is 2.167 ns, SRAM cycle time is 15 ns
  How many memory banks needed?
192 – max # of memory references 32 X (4+2)
Each SRAM bank need 15/2.167 < 7 cycles/reference
 192 X 7 = 1,344 memory banks! (Largest configuration of Cray T90: 1024 memory banks ( required pipelined synchronous SRAM)
Vector Architectures

## Slide 15: Stride
Consider:
for (i = 0; i < 100; i=i+1)
for (j = 0; j < 100; j=j+1) {
A[i][j] = 0.0;
for (k = 0; k < 100; k=k+1)
A[i][j] = A[i][j] + B[i][k] * D[k][j];
}
Must vectorize multiplication of rows of B with columns of D
Use non-unit stride [the distance separating elements to be gathered into a single (vector) register is called the stride]
And Bank conflict (stall) occurs when the same bank is hit faster than bank busy time: LCM – least common multiple
  #banks / LCM(stride,#banks) < bank busy time
Example 8 memory banks. Bank busy time – 6 clocks. Total memory latency – 12 clocks. How long to complete 64-element vector load with stride of 1? With stride of 32?
Answer Stride of 1. Since 8, #banks, is larger than 6, bank busy time, the load will take 12+64=72 clocks  1.2 clocks/element
Stride of 32. Worst case for strides when multiple of #banks (.e.g. 32 and 8). Every access needs to wait for previous access 6 clocks. Load will take 12+1+6X63=391  6.1 clocks/element
Vector Architectures

## Slide 16: Scatter-Gather handling sparse matrices in vector architectures
Consider:
for (i = 0; i < n; i=i+1)
A[K[i]] = A[K[i]] + C[M[i]];
Use index vector:
LV Vk, Rk ;load K
LVI Va, (Ra+Vk) ;load A[K[]] gather
LV Vm, Rm ;load M
LVI Vc, (Rc+Vm) ;load C[M[]] gather
ADDVV.D Va, Va, Vc ;add them
SVI (Ra+Vk), Va ;store A[K[]] scatter
Loads (gather) and stores (scatter) can be pipelined, BUT are much slower than non-indexed loads and stores. Why? Memory banks unknown at start of instruction  Cannot be handled in groups. Also conflicts at memory banks each access incurs significat latency
Vector Architectures
scatter gather gather

## Slide 17: Programming Vec. Architectures
Compilers can provide feedback/hints to programmers
Will code vectorize? if not, what are problems? Helps experts to vectorize or provide hints to the compiler.
Programmers can provide hints to compiler
Dialog simplifies programming. Main factor The algorithm: dependence among loops
Level of vectorization in scientific programs Perfect Club benchmark
Vector Architectures

## Slide 18: SIMD Extensions for multimedia
Media applications operate on data types narrower than the native word size (e.g., many graphics systems use 8 bit for each of the 3 primary colors plus 8 bits for transparency)
  Example: disconnect carry chains to “partition” adder
Limitations, compared to vector instructions:
  Number of data operands encoded into op code
  No sophisticated addressing modes (strided, scatter-gather)
  No mask registers
SIMD Instruction Set Extensions for Multimedia

## Slide 19: SIMD Implementations
Implementations:
  Intel MMX (1996)
    Eight 8-bit integer ops or four 16-bit integer ops
  Streaming SIMD Extensions (SSE) (1999)
    Eight 16-bit integer ops
    Four 32-bit integer/fp ops or two 64-bit integer/fp ops
  Advanced Vector Extensions (2010)
    Four 64-bit integer/fp ops
  Operands must be consecutive and aligned memory locations
SIMD Instruction Set Extensions for Multimedia

## Slide 20: Example SIMD Code suffix 4D: instruction operating on 4 double precision operands at once
Example DAXPY:
L.D F0,a ;load scalar a
MOV F1, F0 ;copy a into F1 for SIMD MUL unclear point:
MOV F2, F0 ;copy a into F2 for SIMD MUL broadcast in real SIMD
MOV F3, F0 ;copy a into F3 for SIMD MUL instead of copy
DADDIU R4,Rx,#512 ;last address to load
Loop: L.4D F4,0[Rx] ;load X[i], X[i+1], X[i+2], X[i+3]
MUL.4D F4,F4,F0 ;a×X[i],a×X[i+1],a×X[i+2],a×X[i+3]
L.4D F8,0[Ry] ;load Y[i], Y[i+1], Y[i+2], Y[i+3]
ADD.4D F8,F8,F4 ;a×X[i]+Y[i], ..., a×X[i+3]+Y[i+3]
S.4D 0[Ry],F8 ;store into Y[i], Y[i+1], Y[i+2], Y[i+3]
DADDIU Rx,Rx,#32 ;increment index to X
DADDIU Ry,Ry,#32 ;increment index to Y
DSUBU R20,R4,Rx ;compute bound
BNEZ R20,Loop ;check if done
SIMD Instruction Set Extensions for Multimedia

## Slide 21: Roofline Performance Model
Basic idea:
  Plot peak floating-point throughput as a function of arithmetic intensity
  Ties together floating-point performance and memory performance for a target machine
Arithmetic intensity
  Floating-point operations per byte read
SIMD Instruction Set Extensions for Multimedia

## Slide 22: Examples
Y-axis Attainable GFLOPs/sec
Min(Peak Memory BW × Arithmetic Intensity up to a point limited by peak memory BW,
beyond that point by Peak Floating Point Perf.)
SIMD Instruction Set Extensions for Multimedia

## Slide 23: Graphics Processing Units
Given the hardware invested to do graphics well, how can be supplement it to improve performance of a wider range of applications?
Basic idea:
  Heterogeneous execution model
    CPU is the host, GPU is the device
  Develop a C-like programming language for GPU
  Unify all forms of GPU parallelism as CUDA thread
  Programming model is “Single Instruction Multiple Thread”
Graphical Processing Units

## Slide 24: Threads and Blocks
A thread is associated with each data element
Threads are organized into blocks
Blocks are organized into a grid
GPU hardware handles thread management, not applications or OS
Graphical Processing Units

## Slide 25: NVIDIA GPU Architecture
Similarities to vector machines:
  Works well with data-level parallel problems
  Scatter-gather transfers
  Mask registers
  Large register files
Differences:
  No scalar processor
  Uses multithreading to hide memory latency
  Has many functional units, as opposed to a few deeply pipelined units like a vector processor
Graphical Processing Units

## Slide 26: Example
Multiply two vectors of length 8192
  Code that works over all elements is the grid
  Thread blocks break this down into manageable sizes
    512 threads per block
  SIMD instruction executes 32 elements at a time
  Thus grid size = 16 blocks (X512 = 8192)
  Block is analogous to a strip-mined vector loop with vector length of 32 (X16 = 512)
  Block is assigned to a multithreaded SIMD processor by the thread block scheduler
  Current-generation GPUs (Fermi) have 7-15 multithreaded SIMD processors
Graphical Processing Units

## Slide 27: Terminology
Threads of SIMD instructions
  Each has its own PC
  Thread scheduler uses scoreboard to dispatch
  No data dependencies between threads!
  Keeps track of up to 48 threads of SIMD instructions
    Hides memory latency
Thread block scheduler schedules blocks to SIMD processors
Within each SIMD processor:
  32 SIMD lanes
  Wide and shallow compared to vector processors
Graphical Processing Units

## Slide 28: Example
NVIDIA GPU has 32,768 registers
  Divided into lanes
  Each SIMD thread is limited to 64 registers
  SIMD thread has up to:
    64 vector registers of 32 32-bit elements
    32 vector registers of 32 64-bit elements
  Fermi has 16 physical SIMD lanes, each containing 2048 registers
Graphical Processing Units

## Slide 29: NVIDIA Instruction Set Arch.
ISA is an abstraction of the hardware instruction set
  “Parallel Thread Execution (PTX)” i.e., CUDA-like
  Uses virtual registers
  Translation to machine code is performed in software
  Example one iteration of DAXPY loop:
  shl.s32 R8, blockIdx, 9 ; Thread Block ID * Block size (512 or 29) shift left
  block id to each block
  add.s32 R8, R8, threadIdx ; R8 = i = my CUDA thread ID
  thread id to each thread (total 8192 threads)
  shl.u32 R8, R8, 3 ; byte offset (per p. 300 in HP12)
  First 3 PTX instructions calculate unique byte offset in R8, which is added to base of array
  Following: load 2 double-precision FP operands, then multiply, add and store
  ld.global.f64 RD0, [X+R8] ; RD0 = X[i]
  ld.global.f64 RD2, [Y+R8] ; RD2 = Y[i]
  mul.f64 R0D, RD0, RD4 ; Product in RD0 = RD0 * RD4 (scalar a)
  add.f64 R0D, RD0, RD2 ; Sum in RD0 = RD0 + RD2 (Y[i])
  st.global.f64 [Y+R8], RD0 ; Y[i] = sum (X[i]*a + Y[i])
Graphical Processing Units

## Slide 30: Some comparison with vector architecture
Unlike vector architectures, GPUs don’t have separate instructions for sequential data transfers, strided data transfers, and gather-scatter data transfers. All data transfers are gather-scatter.
To regain efficiency, GPUs include special Coalescing hardware to recognize sequential addresses and notifies the Memory Interface Unit to request block transfers.
The GPU programmer must ensue that adjacent CUDA Threads access nearby addresses nearby addresses at the same time. (Done in above example.)

## Slide 31: Conditional Branching
Like vector architectures, GPU branch hardware uses internal masks
Also uses
  Branch synchronization stack
    Entries consist of masks for each SIMD lane
    I.e. which threads commit their results (all threads execute)
  Instruction markers to manage when a branch diverges into multiple execution paths
    Push on divergent branch
  …and when paths converge
    Act as barriers
    Pops stack
Per-thread-lane 1-bit predicate register, specified by programmer
Graphical Processing Units

## Slide 32: Example
if (X[i] != 0)
X[i] = X[i] – Y[i];
else X[i] = Z[i];
Assuming that R8 has already the scaled thread ID, the IF statement translates in PTX to
ld.global.f64 RD0, [X+R8] ; RD0 = X[i]
setp.neq.s32 P1, RD0, #0 ; P1 is predicate register 1
@!P1, bra ELSE1, *Push ; Push old mask, set new mask bits
; if P1 false, go to ELSE1 bra is branch
ld.global.f64 RD2, [Y+R8] ; RD2 = Y[i]
sub.f64 RD0, RD0, RD2 ; Difference in RD0
st.global.f64 [X+R8], RD0 ; X[i] = RD0
@P1, bra ENDIF1, *Comp ; complement mask bits
; if P1 true, go to ENDIF1
ELSE1: ld.global.f64 RD0, [Z+R8] ; RD0 = Z[i]
st.global.f64 [X+R8], RD0 ; X[i] = RD0
ENDIF1: <next instruction>, *Pop ; pop to restore old mask
Push old mask, complement current mask, restore old mask. Why? For nesting.
Illusion of each thread operating independently. In practice: no ops. Nesting: ½ speed/level
Graphical Processing Units

## Slide 33: NVIDIA GPU Memory Structures
Each SIMD Lane has private section of off-chip DRAM
  “Private memory”
  Contains stack frame, spilling registers, and private variables
Each multithreaded SIMD processor also has local memory
  Shared by SIMD lanes / threads within a block
Memory shared by SIMD processors is GPU Memory
  Host can read and write GPU memory
  Memory per: 1. Lane. 2. SIMD processor. 3. Block.
Graphical Processing Units

## Slide 34: Fermi Architecture Innovations
Each SIMD processor has
  Two SIMD thread schedulers, two instruction dispatch units
  16 SIMD lanes (SIMD width=32, chime=2 cycles), 16 load-store units, 4 special function units
  Thus, two threads of SIMD instructions are scheduled every two clock cycles
Fast double precision
Caches for GPU memory
64-bit addressing and unified address space
Error correcting codes
Faster context switching
Faster atomic instructions
Graphical Processing Units

## Slide 35: Fermi Multithreaded SIMD Proc.
Graphical Processing Units
Each SIMD lane has 2 pipelined units: FP and integer, logic for dispatching instruction to these units and queue for holding results. 4 Special Function Units (SFUs) calculate special functions (square roots, sines, etc)

## Slide 36: Summary
GPU are really just multi-threaded SIMD processors. They do have more processors, more lanes per processor and more multithreaded hardware than do traditional multi-cores.
GPUs rely on extensive multithreading to hide the very high DRAM latency. The chip area used for caches in system processors is spent instead on computing resources and on the large number of registers to hold the state of many threads of SIMD instructions.
Hiding latencies (by hoping for huge amounts of parallelism form the application and its code) is the underlying philosophy. But the relatively recent Fermi added some shared cache. Smaller (.25MB to .75 MB for L1 and .75MB for L2) than registers (2MB). HP12: more for keeping shared variables across threads closer than classic cache role (bringing main memory closer).

## Slide 37: Detecting and Enhancing Loop-Level Parallelism
Focuses on determining whether data accesses in later iterations are dependent on data values produced in earlier iterations
  Loop-carried dependence
Example 1:
for (i=999; i>=0; i=i-1)
x[i] = x[i] + s;
No loop-carried dependence
Detecting and Enhancing Loop-Level Parallelism

## Slide 38: Loop-Level Parallelism
Example 2:
for (i=0; i<100; i=i+1) {
A[i+1] = A[i] + C[i]; /* S1 */
B[i+1] = B[i] + A[i+1]; /* S2 */
}
S1 uses a value computed by S1 in previous iteration
S2 uses a value computed by S2 in previous iteration
S2 uses value computed by S1 in same iteration
Detecting and Enhancing Loop-Level Parallelism
S1,1 S1,2
S2,1 S2,2 draw dependencies
S3,1 S3,2
…

## Slide 39: Loop-Level Parallelism
Example 3:
for (i=0; i<100; i=i+1) {
A[i] = A[i] + B[i]; /* S1 */
B[i+1] = C[i] + D[i]; /* S2 */
}
S1 uses value computed by S2 in previous iteration but dependence is not circular so loop is parallel
Transform to:
A[0] = A[0] + B[0];
for (i=0; i<99; i=i+1) {
B[i+1] = C[i] + D[i];
A[i+1] = A[i+1] + B[i+1];
}
B[100] = C[99] + D[99];
Detecting and Enhancing Loop-Level Parallelism

## Slide 40: Loop-Level Parallelism
Example 4:
for (i=0;i<100;i=i+1) {
A[i] = B[i] + C[i];
D[i] = A[i] * E[i];
}
Example 5:
for (i=1;i<100;i=i+1) {
Y[i] = Y[i-1] + Y[i];
}
Wait.. The theory solutions: Can be computed in log n time. BUT, only with transformation
Practical solution: ‘reductions’ – last slide of Chapter 4
Detecting and Enhancing Loop-Level Parallelism

## Slide 41: Finding dependencies
Assume indices are affine:
  a x i + b (i is loop index)
Assume:
  Store to a x i + b, then
  Load from c x i + d
  i runs from m to n
  Dependence exists if:
    Given j, k such that m ≤ j ≤ n, m ≤ k ≤ n
    Store to a x j + b, load from a x k + d, and a x j + b = c x k + d
Detecting and Enhancing Loop-Level Parallelism

## Slide 42: Finding dependencies
Generally cannot determine at compile time
Test for absence of a dependence:
  GCD test:
    If a dependency exists, GCD(c,a) must evenly divide (d-b)
Example:
  for (i=0; i<100; i=i+1) {
  X[2*i+3] = X[2*i] * 5.0;
  }
Detecting and Enhancing Loop-Level Parallelism

## Slide 43: Finding dependencies
Example 2:
  for (i=0; i<100; i=i+1) {
  Y[i] = X[i] / c; /* S1 */
  X[i] = X[i] + c; /* S2 */
  Z[i] = Y[i] + c; /* S3 */
  Y[i] = c - Y[i]; /* S4 */ }
  True dependences: S1 to S3 & S1 to S4
  No loop carried dependence  loop is parallel
  Still S3 and S4 need to wait for S1 to complete
  Anti-dependences: S1 to S2 (for X[i]) & S3 to S4 (for Y[i])
  Output dependence: S1 to S4 for Y[i]
  for (i=0; i<100; i=i+1) {
  T[i] = X[i] / c; /* Y renamed T to remove output dependence
  X1[i] = X[i] + c; /* X renamed X1 to remove anti dependence
  Z[i] = T[i] + c; /* Y renamed T to remove anti dependence
  Y[i] = c - T[i];
Detecting and Enhancing Loop-Level Parallelism

## Slide 44: Reductions – Eliminating dependent computation
Reduction Operation:
for (i=9999; i>=0; i=i-1)
sum = sum + x[i] * y[i];
Transform to…
for (i=9999; i>=0; i=i-1)
sum [i] = x[i] * y[i];
for (i=9999; i>=0; i=i-1) These 2 commands are called ‘reduction’
finalsum = finalsum + sum[i];
Do on 10 processors: [processor 0 <= p <= 9, does the following]
for (i=999; i>=0; i=i-1)
finalsum[p] = finalsum[p] + sum[i+1000*p];
It remains to add up finalsum[0], finalsum[1] … finalsum[9]
Note: assumes associativity!
Detecting and Enhancing Loop-Level Parallelism