## Slide 1
Chapter 2
Memory Hierarchy Design
Computer Architecture
A Quantitative Approach, Sixth Edition

## Slide 2: Introduction
Programmers want unlimited amounts of memory with low latency
Fast memory technology is more expensive per bit than slower memory
Solution: organize memory system into a hierarchy
  Entire addressable memory space available in largest, slowest memory
  Incrementally smaller and faster memories, each containing a subset of the memory below it, proceed in steps up toward the processor
Temporal and spatial locality insures that nearly all references can be found in smaller memories
  Gives the allusion of a large, fast memory being presented to the processor
Introduction

## Slide 3: Memory Hierarchy
Introduction

## Slide 4
Figure 2.1 The levels in a typical memory hierarchy in a personal mobile device (PMD), such as a cell phone or tablet (A), in a laptop or desktop computer (B), and in a server (C). As we move farther away from the processor, the memory in the level below becomes slower and larger. Note that the time units change by a factor of 109 from picoseconds to milliseconds in the case of magnetic disks and that the size units change by a factor of 1010 from thousands of bytes to tens of terabytes. If we were to add warehouse-sized computers, as opposed to just servers, the capacity scale would increase by three to six orders of magnitude. Solid-state drives (SSDs) composed of Flash are used exclusively in PMDs, and heavily in both laptops and desktops. In many desktops, the primary storage system is SSD, and expansion disks are primarily hard disk drives (HDDs). Likewise, many servers mix SSDs and HDDs.

## Slide 5: Memory Performance Gap
Introduction

## Slide 6
Figure 2.2 Starting with 1980 performance as a baseline, the gap in performance, measured as the difference in the time between processor memory requests (for a single processor or core) and the latency of a DRAM access, is plotted over time. In mid-2017, AMD, Intel and Nvidia all announced chip sets using versions of HBM technology. Note that the vertical axis must be on a logarithmic scale to record the size of the processor-DRAM performance gap. The memory baseline is 64 KiB DRAM in 1980, with a 1.07 per year performance improvement in latency (see Figure 2.4 on page 88). The processor line assumes a 1.25 improvement per year until 1986, a 1.52 improvement until 2000, a 1.20 improvement between 2000 and 2005, and only small improvements in processor performance (on a per-core basis) between 2005 and 2015. As you can see, until 2010 memory access times in DRAM improved slowly but consistently; since 2010 the improvement in access time has reduced, as compared with the earlier periods, although there have been continued improvements in bandwidth. See Figure 1.1 in Chapter 1 for more information.

## Slide 7: Memory Hierarchy Design
Memory hierarchy design becomes more crucial with recent multi-core processors:
  Aggregate peak bandwidth grows with # cores:
    Intel Core i7 can generate two references per core per clock
    Four cores and 3.2 GHz clock
      25.6 billion 64-bit data references/second +
      12.8 billion 128-bit instruction references/second
      = 409.6 GB/s!
    DRAM bandwidth is only 8% of this (34.1 GB/s)
    Requires:
      Multi-port, pipelined caches
      Two levels of cache per core
      Shared third-level cache on chip
Introduction

## Slide 8: Performance and Power
High-end microprocessors have >10 MB on-chip cache
  Consumes large amount of area and power budget
Introduction

## Slide 9: Memory Hierarchy Basics
When a word is not found in the cache, a miss occurs:
  Fetch word from lower level in hierarchy, requiring a higher latency reference
  Lower level may be another cache or the main memory
  Also fetch the other words contained within the block
    Takes advantage of spatial locality
  Place block into cache in any location within its set, determined by address
    block address MOD number of sets in cache
Introduction

## Slide 10
Figure B.2 This example cache has eight block frames and memory has 32 blocks. The three options for caches are shown left to right. In fully associative, block 12 from the lower level can go into any of the eight block frames of the cache. With direct mapped, block 12 can only be placed into block frame 4 (12 modulo 8). Set associative, which has some of both features, allows the block to be placed anywhere in set 0 (12 modulo 4). With two blocks per set, this means block 12 can be placed either in block 0 or in block 1 of the cache. Real caches contain thousands of block frames, and real memories contain millions of blocks. The set associative organization has four sets with two blocks per set, called two-way set associative. Assume that there is nothing in the cache and that the block address in question identifies lower-level block 12.

## Slide 11: Memory Hierarchy Basics
n sets => n-way set associative [unclear what this line means]
  Direct-mapped cache => one block per set
  Fully associative => one set
Writing to cache: two strategies
  Write-through
    Immediately update lower levels of hierarchy
  Write-back
    Only update lower levels of hierarchy when an updated block is replaced
  Both strategies use write buffer to make writes asynchronous
Introduction

## Slide 12: Memory Hierarchy Basics
Miss rate
  Fraction of cache access that result in a miss
Causes of misses
  Compulsory
    First reference to a block
  Capacity
    Blocks discarded and later retrieved. Do they mean misses that even a fully associative cache could not avoid? If so, how to determine for individual reference?
  Conflict
    Program makes repeated references to multiple addresses from different blocks that map to the same location in the cache
Introduction
“The 3C’s model is conceptual; although its insights usually hold, it is not a definitive model for explaining cache behavior of individual references” p.82.
Notes: Capacity—misses even for fully associative cache
Conflict—misses for set associative (or direct mapped) cache that could have been avoided for fully associative cache

## Slide 13: Memory Hierarchy Basics
Speculative and multithreaded processors may execute other instructions during a miss
  Reduces performance impact of misses
Introduction

## Slide 14: Memory Hierarchy Basics
Six basic cache optimizations:
  Larger block size
    Reduces compulsory misses
    Increases capacity and conflict misses, increases miss penalty
  Larger total cache capacity to reduce miss rate
    Increases hit time, increases power consumption
  Higher associativity
    Reduces conflict misses
    Increases hit time, increases power consumption
  Higher number of cache levels
    Reduces overall memory access time
  Giving priority to read misses over writes
    Reduces miss penalty
  Avoiding address translation in cache indexing
    Reduces hit time
Introduction

## Slide 15: Memory Technology and Optimizations
Performance metrics
  Latency is concern of cache
  Bandwidth is concern of multiprocessors and I/O
  Access time
    Time between read request and when desired word arrives
  Cycle time
    Minimum time between unrelated requests to memory
SRAM memory has low latency, use for cache
Organize DRAM chips into many banks for high bandwidth, use for main memory
Memory Technology and Optimizations

## Slide 16: Memory Technology
SRAM
  Requires low power to retain bit
  Requires 6 transistors/bit
DRAM
  Must be re-written after being read
  Must also be periodically refreshed
    Every ~ 8 ms (roughly 5% of time)
    Each row can be refreshed simultaneously
  One transistor/bit
  Address lines are multiplexed:
    Upper half of address: row access strobe (RAS)
    Lower half of address: column access strobe (CAS)
Memory Technology and Optimizations

## Slide 17: Internal Organization of DRAM
Memory Technology and Optimizations

## Slide 18: Memory Technology
Amdahl:
  Memory capacity should grow linearly with processor speed
  Unfortunately, memory capacity and speed has not kept pace with processors
Some optimizations:
  Multiple accesses to same row
  Synchronous DRAM
    Added clock to DRAM interface
    Burst mode with critical word first
  Wider interfaces
  Double data rate (DDR)
  Multiple banks on each DRAM device
Memory Technology and Optimizations

## Slide 19: Memory Optimizations
Memory Technology and Optimizations

## Slide 20: Memory Optimizations
Memory Technology and Optimizations

## Slide 21: Memory Optimizations
DDR: [transfers data on both the rising and falling edges of the clock signal]
  DDR2
    Lower power (2.5 V -> 1.8 V)
    Higher clock rates (266 MHz, 333 MHz, 400 MHz)
  DDR3
    1.5 V
    800 MHz
  DDR4
    1-1.2 V
    1333 MHz
GDDR5 is graphics memory based on DDR3
Memory Technology and Optimizations

## Slide 22: Memory Optimizations
Reducing power in SDRAMs:
  Lower voltage
  Low power mode (ignores clock, continues to refresh)
Graphics memory:
  Achieve 2-5 X bandwidth per DRAM vs. DDR3
    Wider interfaces (32 vs. 16 bit)
    Higher clock rate
      Possible because they are attached via soldering instead of socketed DIMM modules
      … Soldering led to HBM (successor to GDDR5?)
Memory Technology and Optimizations

## Slide 23: Memory Power Consumption
Memory Technology and Optimizations

## Slide 24: Stacked/Embedded DRAMs
Stacked DRAMs in same package as processor [shorter distance/latency, more connections/bandwidth]
  High Bandwidth Memory (HBM)
Memory Technology and Optimizations

## Slide 25: Flash Memory
Type of EEPROM [Electrically Erasable Programmable Read-Only Memory and is a type of non-volatile memory]
Types: NAND (denser) and NOR (faster)
NAND Flash:
  Reads are sequential, reads entire page (.5 to 4 KiB)
  25 us for first byte, 40 MiB/s for subsequent bytes
  SDRAM: 40 ns for first byte, 4.8 GB/s for subsequent bytes
  2 KiB transfer: 75 uS vs 500 ns for SDRAM, 150X slower
  300 to 500X faster than magnetic disk
Memory Technology and Optimizations

## Slide 26: NAND Flash Memory
Must be erased (in blocks) before being overwritten
Nonvolatile, can use as little as zero power
Limited number of write cycles (~100,000)
$2/GiB, compared to $20-40/GiB for SDRAM and $0.09 GiB for magnetic disk
[GiB=232 Bytes. GB=109 Bytes]
Phase-Change/Memrister Memory
  Possibly 10X improvement in write performance and 2X improvement in read performance
Memory Technology and Optimizations

## Slide 27: Memory Dependability
Memory is susceptible to cosmic rays
Soft errors: dynamic errors
  Detected and fixed by error correcting codes (ECC)
Hard errors: permanent errors
  Use spare rows to replace defective rows
Chipkill: a RAID-like error recovery technique
RAID- Redundant Array of Independent Disks
Memory Technology and Optimizations

## Slide 28: Advanced Optimizations
Reduce hit time
  Small and simple first-level caches
  Way prediction
Increase bandwidth
  Pipelined caches, multibanked caches, non-blocking caches
Reduce miss penalty
  Critical word first, merging write buffers
Reduce miss rate
  Compiler optimizations
Reduce miss penalty or miss rate via parallelization
  Hardware or compiler prefetching
Advanced Optimizations

## Slide 29: L1 Size and Associativity
Access time vs. size and associativity
Advanced Optimizations

## Slide 30: L1 Size and Associativity
Energy per read vs. size and associativity
Advanced Optimizations

## Slide 31: Way Prediction
To improve hit time, predict the way to pre-set mux (using extra bit(s) )
  Mis-prediction gives longer hit time
  Prediction accuracy
    > 90% for two-way
    > 80% for four-way
    I-cache has better accuracy than D-cache
  First used on MIPS R10000 in mid-90s
  Used on ARM Cortex-A8
Extend to predict block as well
  “Way selection”
  Increases mis-prediction penalty
  Example: 4-way set-associative. Predicts which of the 4 blocks in a set to read next
Advanced Optimizations

## Slide 32: Pipelined Caches
Pipeline cache access to improve bandwidth
  Examples:
    Pentium: 1 cycle
    Pentium Pro – Pentium III: 2 cycles
    Pentium 4 – Core i7: 4 cycles
Increases branch mis-prediction penalty
Makes it easier to increase associativity
Advanced Optimizations

## Slide 33: Multibanked Caches
Organize cache as independent banks to support simultaneous access
  ARM Cortex-A8 supports 1-4 banks for L2
  Intel i7 supports 4 banks for L1 and 8 banks for L2
Interleave banks according to block address
Advanced Optimizations

## Slide 34: Nonblocking Caches
Allow hits before previous misses complete
  “Hit under miss”
  “Hit under multiple miss”
L2 must support this
In general, processors can hide L1 miss penalty but not L2 miss penalty
Advanced Optimizations

## Slide 35
Figure 2.11 The effectiveness of a nonblocking cache is evaluated by allowing 1, 2, or 64 hits under a cache miss with 9 SPECINT (on the left) and 9 SPECFP (on the right) benchmarks. The data memory system modeled after the Intel i7 consists of a 32 KiB L1 cache with a four-cycle access latency. The L2 cache (shared with instructions) is 256 KiB with a 10-clock cycle access latency. The L3 is 2 MiB and a 36-cycle access latency. All the caches are eight-way set associative and have a 64-byte block size. Allowing one hit under miss reduces the miss penalty by 9% for the integer benchmarks and 12.5% for the floating point. Allowing a second hit improves these results to 10% and 16%, and allowing 64 results in little additional improvement.

## Slide 36: Critical Word First, Early Restart
Critical word first
  Request missed word from memory first
  Send it to the processor as soon as it arrives
Early restart
  Request words in normal order
  Send missed work to the processor as soon as it arrives
Beneficial if block are large
Effectiveness of these strategies depends on block size and likelihood of another access to the portion of the block that has not yet been fetched
Advanced Optimizations

## Slide 37: Merging Write Buffer
When storing to a block that is already pending in the write buffer, update write buffer
Reduces stalls due to full write buffer
Do not apply to I/O addresses
Advanced Optimizations
No write buffering
Write buffering

## Slide 38
Figure 2.12 In this illustration of write merging, the write buffer on top does not use write merging while the write buffer on the bottom does. The four writes are merged into a single buffer entry with write merging; without it, the buffer is full even though three-fourths of each entry is wasted. The buffer has four entries, and each entry holds four 64-bit words. The address for each entry is on the left, with a valid bit (V) indicating whether the next sequential 8 bytes in this entry are occupied. (Without write merging, the words to the right in the upper part of the figure would be used only for instructions that wrote multiple words at the same time.)

## Slide 39: Compiler Optimizations
Loop Interchange
  Swap nested loops to access memory in sequential order Example: if a matrix is stored in row order and loop accesses it in column order switch to row order
Blocking
  Instead of accessing entire rows or columns, subdivide matrices into blocks
  Requires more memory accesses but improves locality of accesses
  If cache can store B2 memory words but not an entire matrix…
Advanced Optimizations

## Slide 40: Blocking
for (i = 0; i < N; i = i + 1)
for (j = 0; j < N; j = j + 1)
{
r = 0;
for (k = 0; k < N; k = k + 1)
r = r + y[i][k]*z[k][j];
x[i][j] = r;
};

## Slide 41
Figure 2.13 A snapshot of the three arrays x, y, and z when N = 6 and i = 1. The age of accesses to the array elements is indicated by shade: white means not yet touched, light means older accesses, and dark means newer accesses. The elements of y and z are read repeatedly to calculate new elements of x. The variables i, j, and k are shown along the rows or columns used to access the arrays.

## Slide 42: Blocking
for (jj = 0; jj < N; jj = jj + B)
for (kk = 0; kk < N; kk = kk + B)
for (i = 0; i < N; i = i + 1)
for (j = jj; j < min(jj + B,N); j = j + 1)
{
r = 0;
for (k = kk; k < min(kk + B,N); k = k + 1)
r = r + y[i][k]*z[k][j];
x[i][j] = x[i][j] + r;
};
The range of j (and k) is B

## Slide 43
Figure 2.14 The age of accesses to the arrays x, y, and z when B = 3. Note that, in contrast to Figure 2.13, a smaller number of elements is accessed.

## Slide 44: Hardware Prefetching
Fetch two blocks on miss (include next sequential block)
Advanced Optimizations
Pentium 4 Pre-fetching

## Slide 45: Compiler Prefetching
Insert prefetch instructions before data is needed
Non-faulting: prefetch doesn’t cause exceptions for virtual address faults and protection violations
Register prefetch
  Loads data into register
Cache prefetch
  Loads data into cache
Combine with loop unrolling and software pipelining
Advanced Optimizations

## Slide 46: Use HBM to Extend Hierarchy
128 MiB to 1 GiB
Smaller blocks require substantial tag storage
Larger blocks are potentially inefficient
One approach (L-H):
  Each SDRAM row is a block index
  Each row contains set of tags and 29 data segments
  29-set associative
  Hit requires a CAS
Advanced Optimizations

## Slide 47: Use HBM to Extend Hierarchy
Another approach (Alloy cache):
  Mold tag and data together
  Use direct mapped
Both schemes require two DRAM accesses for misses
  Two solutions:
    Use map to keep track of blocks
    Predict likely misses
Advanced Optimizations

## Slide 48: Use HBM to Extend Hierarchy
Advanced Optimizations

## Slide 49: Summary
Advanced Optimizations

## Slide 50
Figure B.19 The logical program in its contiguous virtual address space is shown on the left. It consists of four pages, A, B, C, and D. The actual location of three of the blocks is in physical main memory and the other is located on the disk.
Virtual memory, Section B4
Initially meant to remove the burden of the programmers from having to deal with
physical memory

## Slide 51: Protection Segue: HP-2012 slides for self-contained presentation
Virtual memory
Virtual machines

## Slide 52: The Limits of Physical Addressing
CPU
Memory
A0-A31
A0-A31
D0-D31
D0-D31
“Physical addresses” of memory locations
Data
All programs share one address space:
The physical address space
No way to prevent a program from accessing any machine resource
Machine language programs must be
aware of the machine organization

## Slide 53: Solution: Add a Layer of Indirection
CPU
Memory
A0-A31
A0-A31
D0-D31
D0-D31
Data
User programs run in an standardized
virtual address space
Address Translation hardware
managed by the operating system (OS)
maps virtual address to physical memory
“Physical Addresses”
Address
Translation
Virtual
Physical
“Virtual Addresses”
Hardware supports “modern” OS features:
Protection, Translation, Sharing

## Slide 54: Three Advantages of Virtual Memory
Translation:
  Program can be given consistent view of memory, even though physical memory is scrambled
  Makes multithreading reasonable (now used a lot!)
  Only the most important part of program (“Working Set”) must be in physical memory.
  Contiguous structures (like stacks) use only as much physical memory as necessary yet still grow later.
Protection:
  Different threads (or processes) protected from each other.
  Different pages can be given special behavior
    (Read Only, Invisible to user programs, etc).
  Kernel data protected from User programs
  Very important for protection from malicious programs
Sharing:
  Can map same physical page to multiple users (“Shared memory”)

## Slide 55: Page tables encode virtual address spaces
A machine usually supports
pages of a few sizes
(MIPS R4000):
Physical
Memory Space
A valid page table entry codes physical memory “frame” address for the page
A virtual address space
is divided into blocks
of memory called pages
frame
frame
frame
frame
A page table is indexed by a
virtual address
virtual address
Page Table
OS manages the page table for each ASID (thread)

## Slide 56
TLB Design Concepts
(Translation Look-Aside Buffer)
Anecdote TLB preceded caches, since address delays preceded data & instruction delays. Still what is better known: TLBs or caches?

## Slide 57: MIPS Address Translation: How does it work?
“Physical Addresses”
CPU
Memory
A0-A31
A0-A31
D0-D31
D0-D31
Data
TLB also contains
protection bits for virtual address
Virtual
Physical
“Virtual Addresses”
Translation
Look-Aside
Buffer
(TLB)
Translation Look-Aside Buffer (TLB)
A small fully-associative cache of
mappings from virtual to physical addresses
Fast common case: Virtual address is in TLB,
process has permission to read/write it.
What is the table of
mappings that it caches?

## Slide 58: Summary: TLB, Virtual Memory
Page tables map virtual address to physical address
TLBs are important for fast translation
TLB misses are significant in processor performance
  funny times, as most systems can’t access all of 2nd level cache without TLB misses!
Caches, TLBs, Virtual Memory all understood by examining how they deal with 4 questions: 1) Where can block be placed? 2) How is block found? 3) What block is replaced on miss? 4) How are writes handled?
Today VM allows many processes to share single memory without having to swap all processes to disk; today VM protection is more important than memory hierarchy benefits, but computers insecure
Notes: Let’s do a short review of what you learned last time.
Virtual memory was originally invented as another level of memory hierarchy such that programmers, faced with main memory much smaller than their programs, do not have to manage the loading and unloading portions of their program in and out of memory.
It was a controversial proposal at that time because very few programmers believed software can manage the limited amount of memory resource as well as human.
This all changed as DRAM size grows exponentially in the last few decades.
Nowadays, the main function of virtual memory is to allow multiple processes to share the same main memory so we don’t have to swap all the non-active processes to disk.
Consequently, the most important function of virtual memory these days is to provide memory protection.
The most common technique, but we like to emphasis not the only technique, to translate virtual memory address to physical memory address is to use a page table.
TLB, or translation lookaside buffer, is one of the most popular hardware techniques to reduce address translation time.
Since TLB is so effective in reducing the address translation time, what this means is that TLB misses will have a significant negative impact on processor performance.
+3 = 3 min. (X:43)

## Slide 59: Introduction to Virtual Machines
VMs developed in late 1960s
  Remained important in mainframe computing over the years
  Largely ignored in single user computers of 1980s and 1990s
Recently regained popularity due to
  increasing importance of isolation and security in modern systems,
  failures in security and reliability of standard operating systems,
  sharing of a single computer among many unrelated users,
  and the dramatic increases in raw speed of processors, which makes the overhead of VMs more acceptable

## Slide 60: What is a Virtual Machine (VM)?
Broadest definition includes all emulation methods that provide a standard software interface, such as the Java VM
“(Operating) System Virtual Machines” provide a complete system level environment at binary ISA
  Here assume ISAs always match the native hardware ISA
  E.g., IBM VM/370, VMware ESX Server, and Xen
Present illusion that VM users have entire computer to themselves, including a copy of OS
Single computer runs multiple VMs, and can support a multiple, different OSes
  On conventional platform, single OS “owns” all HW resources
  With a VM, multiple OSes all share HW resources
Underlying HW platform is called the host, and its resources are shared among the guest VMs

## Slide 61: Virtual Machine Monitors (VMMs)
Virtual machine monitor (VMM) or hypervisor is software that supports VMs
VMM determines how to map virtual resources to physical resources
Physical resource may be time-shared, partitioned, or emulated in software
VMM is much smaller than a traditional OS;
  isolation portion of a VMM is  10,000 lines of code

## Slide 62: VMM Overhead?
Depends on the workload
User-level processor-bound programs (e.g., SPEC) have zero-virtualization overhead
  Runs at native speeds since OS rarely invoked
I/O-intensive workloads  OS-intensive  execute many system calls and privileged instructions  can result in high virtualization overhead
  For System VMs, goal of architecture and VMM is to run almost all instructions directly on native hardware
If I/O-intensive workload is also I/O-bound (I/O is the bottleneck?)  low processor utilization since waiting for I/O  processor virtualization can be hidden  low virtualization overhead

## Slide 63: Other Uses of VMs
Focus here on protection
2 Other commercially important uses of VMs
Managing Software
  VMs provide an abstraction that can run the complete SW stack, even including old OSes like DOS
  Typical deployment: some VMs running legacy OSes, many running current stable OS release, few testing next OS release
Managing Hardware
  VMs allow separate SW stacks to run independently yet share HW, thereby consolidating number of servers
    Some run each application with compatible version of OS on separate computers, as separation helps dependability
  Migrate running VM to a different computer
    Either to balance load or to evacuate from failing HW
    Basic idea Make everything replaceable: i.e., HW, OS

## Slide 64: Requirements of a Virtual Machine Monitor
A VM Monitor (or hypervisor)
  Presents a SW interface to guest software,
  Isolates state of guests from each other, and
  Protects itself from guest software (including guest OSes)
Guest software should behave on a VM exactly as if running on the native HW
  Except for performance-related behavior or limitations of fixed resources shared by multiple VMs
Guest software should not be able to change allocation of real system resources directly
Hence, VMM must control  everything even though guest VM and OS currently running is temporarily using them
  Access to privileged state, Address translation, I/O, Exceptions and Interrupts, …

## Slide 65: Requirements of a Virtual Machine Monitor
VMM must be at higher privilege level than guest VM, which generally run in user mode
  Execution of privileged instructions handled by VMM
E.g., Timer interrupt: VMM suspends currently running guest VM, saves its state, handles interrupt, determine which guest VM to run next, and then load its state
  Guest VMs that rely on timer interrupt provided with virtual timer and an emulated timer interrupt by VMM
Requirements of system virtual machines are  same as paged-virtual memory:
At least 2 processor modes, system and user
Privileged subset of instructions available only in system mode, trap if executed in user mode
  All system resources controllable only via these instructions

## Slide 66: ISA Support for Virtual Machines
If VMs are planned for during design of ISA, easy to reduce instructions that must be executed by a VMM and how long it takes to emulate them
  Since VMs have been considered for desktop/PC server apps only recently, most ISAs were created without virtualization in mind, including 80x86 and most RISC architectures
VMM must ensure that guest system only interacts with virtual resources  conventional guest OS runs as user mode program on top of VMM
  If guest OS attempts to access or modify information related to HW resources via a privileged instruction--for example, reading or writing the page table pointer--it will trap to the VMM
If not, VMM must intercept instruction and support a virtual version of the sensitive information as the guest OS expects (examples soon)

## Slide 67: Impact of VMs on Virtual Memory
Virtualization of virtual memory if each guest OS in every VM manages its own set of page tables?
VMM separates real and physical memory
  Makes real memory a separate, intermediate level between virtual memory and physical memory
  Some use the terms virtual memory, physical/”real” memory, and machine memory to name the 3 levels
  Guest OS maps virtual memory to real memory via its page tables, and VMM page tables map real memory to physical memory
VMM maintains a shadow page table that maps directly from the guest virtual address space to the physical address space of HW
  Rather than pay extra level of indirection on every memory access
  VMM must trap any attempt by guest OS to change its page table or to access the page table pointer

## Slide 68: ISA Support for VMs & Virtual Memory
IBM 370 architecture added additional level of indirection that is managed by the VMM
  Guest OS keeps its page tables as before, so the shadow pages are unnecessary
To virtualize software TLB, VMM manages the real TLB and has a copy of the contents of the TLB of each guest VM
  Any instruction that accesses the TLB must trap
  TLBs with Process ID tags support a mix of entries from different VMs and the VMM, thereby avoiding flushing of the TLB on a VM switch

## Slide 69: Impact of I/O on Virtual Memory
Most difficult part of virtualization
  Increasing number of I/O devices attached to the computer
  Increasing diversity of I/O device types
  Sharing of a real device among multiple VMs,
  Supporting the myriad of device drivers that are required, especially if different guest OSes are supported on the same VM system
Give each VM generic versions of each type of I/O device driver, and let VMM to handle real I/O
Method for mapping virtual to physical I/O device depends on the type of device:
  Disks partitioned by VMM to create virtual disks for guest VMs
  Network interfaces shared between VMs in short time slices, and VMM tracks messages for virtual network addresses to ensure that guest VMs only receive their messages

## Slide 70: Back to HP-2017 Virtual Memory and Virtual Machines
Protection via virtual memory
  Keeps processes in their own memory space
Role of architecture
  Provide user mode and supervisor mode
  Protect certain aspects of CPU state
  Provide mechanisms for switching between user mode and supervisor mode
  Provide mechanisms to limit memory accesses
  Provide TLB to translate addresses
Virtual Memory and Virtual Machines

## Slide 71: Virtual Machines
Supports isolation and security
Sharing a computer among many unrelated users
Enabled by raw speed of processors, making the overhead more acceptable
Allows different ISAs and operating systems to be presented to user programs
  “System Virtual Machines”
  SVM software is called “virtual machine monitor” or “hypervisor”
  Individual virtual machines run under the monitor are called “guest VMs”
Virtual Memory and Virtual Machines

## Slide 72: Requirements of VMM
Guest software should:
  Behave on as if running on native hardware
  Not be able to change allocation of real system resources
VMM should be able to “context switch” guests
Hardware must allow:
  System and use processor modes
  Privileged subset of instructions for allocating system resources
Virtual Memory and Virtual Machines

## Slide 73: Impact of VMs on Virtual Memory
Each guest OS maintains its own set of page tables
  VMM adds a level of memory between physical and virtual memory called “real memory”
  VMM maintains shadow page table that maps guest virtual addresses to physical addresses
    Requires VMM to detect guest’s changes to its own page table
    Occurs naturally if accessing the page table pointer is a privileged operation
Virtual Memory and Virtual Machines

## Slide 74: Extending the ISA for Virtualization
Objectives:
  Avoid flushing TLB
  Use nested page tables instead of shadow page tables
  Allow devices to use DMA to move data
  Allow guest OS’s to handle device interrupts
  For security: allow programs to manage encrypted portions of code and data
Virtual Memory and Virtual Machines

## Slide 75: Fallacies and Pitfalls
Predicting cache performance of one program from another
Simulating enough instructions to get accurate performance measures of the memory hierarchy. Actually 3 pitfalls:
  Seek to predict performance of a large cache using a small trace
  Program’s locality behavior is not constant over an entire program
  Program’s locality may vary depending on the input
Not delivering high memory bandwidth in a cache-based system