## Slide 1
Chapter 3
Instruction-Level Parallelism and Its Exploitation
Computer Architecture
A Quantitative Approach, Sixth Edition

## Slide 2: Introduction
Pipelining become universal technique in 1985
  Overlaps execution of instructions
  Exploits “Instruction Level Parallelism”
Beyond this, there are two main approaches:
  Hardware-based dynamic approaches
    Used in server and desktop processors
    Not used as extensively in PMP processors
  Compiler-based static approaches
    Not as successful outside of scientific applications
Introduction

## Slide 3: Introduction
Pipelining become universal technique in 1985
  Overlaps execution of instructions
  Exploits “Instruction Level Parallelism”
Beyond this, there are two main approaches:
  Hardware-based dynamic approaches
    Used in server and desktop processors
    Not used as extensively in PMP processors
  However, per http://www.arm.com/products/processors/cortex-a/cortex-a15.php, The Cortex-A15 processor has an out-of-order superscalar pipeline with a tightly-coupled low-latency level-2 cache which can be up to 4MB in size. Additional improvements in floating point and NEON™ media performance result in devices that deliver the next-generation user experience for consumers as well as high-performance computation for web infrastructure applications.
  It is expected that mobile configurations of the Cortex-A15 MPCore processor will deliver over five times the performance of today’s advanced smartphones. In advanced infrastructure applications, the Cortex-A15 running at up to 2.5GHz will enable highly scalable solutions within constantly shrinking energy, thermal and cost budgets.
  Compiler-based static approaches
    Not as successful outside of scientific applications
Introduction

## Slide 4: 5 Steps of MIPS Datapath Read Appendix C!!!
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
ALU
Memory
Reg File
MUX
MUX
Data
Memory
MUX
Sign
Extend
Zero?
IF/ID
ID/EX
MEM/WB
EX/MEM
4
Adder
Next SEQ PC
Next SEQ PC
RD
RD
RD
WB Data
Next PC
Address
RS1
RS2
Imm
MUX

## Slide 5: Backup slide: Visualizing Pipelining
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5

## Slide 6: Most important: Pipelining is not quite that easy!
Limits to pipelining: Hazards prevent next instruction from executing during its designated clock cycle
  Structural hazards: HW cannot support this combination of instructions (single person to fold and put clothes away)
  Data hazards: Instruction depends on result of prior instruction still in the pipeline (missing sock)
  Control hazards: Caused by delay between the fetching of instructions and decisions about changes in control flow (branches and jumps or decide what to wear before knowing whether you go to the office or the beach).

## Slide 7: One Memory Port/Structural Hazards
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Instr 3
Instr 4
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg

## Slide 8: One Memory Port/Structural Hazards
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Stall
Instr 3
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg
Bubble
Bubble
Bubble
Bubble
Bubble
How do you “bubble” the pipe?

## Slide 9: Speed Up Equations for Pipelining
For simple RISC pipeline, Ideal CPI = 1:
Speedup from pipelining = (average instruction time pipelined) /(average instruction time unpipelined)
Pipelining with stalls
Only above formula for ENEE446

## Slide 10: Data Hazard on R1
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Time (clock cycles)
IF
ID/RF
EX
MEM
WB

## Slide 11: Three Generic Data Hazards
Read After Write (RAW) InstrJ tries to read operand before InstrI writes it
Caused by a “Dependence” (in compiler nomenclature). This hazard results from an actual need for communication.
I: add r1,r2,r3
J: sub r4,r1,r3

## Slide 12: Three Generic Data Hazards
Write After Read (WAR) InstrJ writes operand before InstrI reads it
Called an “anti-dependence” by compiler writers. This results from reuse of the name “r1”.
Can’t happen in MIPS 5 stage pipeline because:
  All instructions take 5 stages, and
  Reads are always in stage 2, and
  Writes are always in stage 5
I: sub r4,r1,r3
J: add r1,r2,r3
K: mul r6,r1,r7

## Slide 13: Three Generic Data Hazards
Write After Write (WAW) InstrJ writes operand before InstrI writes it.
Called an “output dependence” by compiler writers This also results from the reuse of name “r1”.
Can’t happen in MIPS 5 stage pipeline because:
  All instructions take 5 stages, and
  Writes are always in stage 5
Will see WAR and WAW in more complicated pipes
I: sub r1,r4,r3
J: add r1,r2,r3
K: mul r6,r1,r7

## Slide 14: Forwarding to Avoid Data Hazard
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
sub r4,r1,r3
and r6,r1,r7
or r8,r1,r9
xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg

## Slide 15: Forwarding to Avoid LW-SW Data Hazard
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
add r1,r2,r3
lw r4, 0(r1)
sw r4,12(r1)
or r8,r6,r9
xor r10,r9,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg

## Slide 16: Data Hazard Even with Forwarding
Time (clock cycles)
I
n
s
t
r.
O
r
d
e
r
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
or r8,r1,r9
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Notes: MIPS actutally didn’t interlecok: MPU without Interlocked Pipelined Stages

## Slide 17: Data Hazard Even with Forwarding
Time (clock cycles)
or r8,r1,r9
I
n
s
t
r.
O
r
d
e
r
lw r1, 0(r2)
sub r4,r1,r6
and r6,r1,r7
Reg
ALU
DMem
Ifetch
Reg
Reg
Ifetch
ALU
DMem
Reg
Bubble
Ifetch
ALU
DMem
Reg
Bubble
Reg
Ifetch
ALU
DMem
Bubble
Reg

## Slide 18: Control Hazard on Branches Three Stage Stall
10: beq r1,r3,36
14: and r2,r3,r5
18: or r6,r1,r7
22: add r8,r1,r9
36: xor r10,r1,r11
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
What do you do with the 3 instructions in between?
How do you do it?
Where is the “commit”?

## Slide 19: Branch Stall Impact
If CPI = 1, 30% branch, Stall 3 cycles => new CPI = 1.9!
Two part solution:
  Determine branch taken or not sooner, AND
  Compute taken branch address earlier

## Slide 20: Four Branch Hazard Alternatives
#1: Stall until branch direction is clear
#2: Predict Branch Not Taken
  Execute successor instructions in sequence
  “Squash” instructions in pipeline if branch actually taken
  Advantage of late pipeline state update
  47% MIPS branches not taken on average
  PC+4 already calculated, so use it to get next instruction
#3: Predict Branch Taken
  53% MIPS branches taken on average
  But haven’t calculated branch target address in MIPS
    MIPS still incurs 1 cycle branch penalty
    Other machines: branch target known before outcome

## Slide 21: Four Branch Hazard Alternatives
#4: Delayed Branch Example in next slide
  Define branch to take place AFTER a following instruction
  branch instruction sequential successor1 sequential successor2 ........ sequential successorn
  branch target if taken
  1 slot delay allows proper decision and branch target address in 5 stage pipeline
Branch delay of length n

## Slide 22: Scheduling Branch Delay Slots
A is the best choice, fills delay slot & reduces instruction count (IC)
In B, the sub instruction may need to be copied, increasing IC
In B and C, must be okay to execute sub when branch fails ‘must be okay’ means that the work is wasted, but the program will still execute correctly
add $1,$2,$3
if $2=0 then
delay slot
A. From before branch
B. From branch target
C. From fall through
add $1,$2,$3
if $1=0 then
delay slot
add $1,$2,$3
if $1=0 then
delay slot
sub $4,$5,$6
sub $4,$5,$6
becomes
becomes
becomes
if $2=0 then
add $1,$2,$3
add $1,$2,$3
if $1=0 then
sub $4,$5,$6
add $1,$2,$3
if $1=0 then
sub $4,$5,$6
Notes: Limitations on delayed-branch scheduling come from 1) restrictions on the instructions that can be moved/copied into the delay slot and 2) limited ability to predict at compile time whether a branch is likely to be taken or not.
In B and C, the use of $1 prevents the add instruction from being moved to the delay slot
In B the sub may need to be copied because it could be reached by another path. B is preferred when the branch is taken with high probability (such as loop branches

## Slide 23: Instruction-Level Parallelism
When exploiting instruction-level parallelism, goal is to minimize CPI
  Pipeline CPI =
    Ideal pipeline CPI +
    Structural stalls +
    Data hazard stalls +
    Control stalls
Parallelism within basic block is limited
  Typical size of basic block = 3-6 instructions
  Must optimize across branches
Introduction

## Slide 24: Data Dependence
Loop-Level Parallelism
  Unroll loop statically or dynamically
  Use SIMD (vector processors and GPUs)
Challenges:
  Data dependency
    Instruction j is data dependent on instruction i if
      Instruction i produces a result that may be used by instruction j
      Instruction j is data dependent on instruction k and instruction k is data dependent on instruction i
Dependent instructions cannot be executed simultaneously
Introduction

## Slide 25: Data Dependence
Dependencies are a property of programs
Pipeline organization determines if how dependence is detected and if it causes a stall
Data dependence conveys:
  Possibility of a hazard
  Order in which results must be calculated
  Upper bound on exploitable instruction level parallelism
Dependencies that flow through memory locations are difficult to detect
Introduction

## Slide 26: Name Dependence
Two instructions use the same name but no flow of information
  Not a true data dependence, but is a problem when reordering instructions
  Antidependence: instruction j writes a register or memory location that instruction i reads
    Initial ordering (i before j) must be preserved
  Output dependence: instruction i and instruction j write the same register or memory location
    Ordering must be preserved
To resolve, use register renaming techniques
Introduction

## Slide 27: Other Factors
Data Hazards
  Read after write (RAW)
  Write after write (WAW)
  Write after read (WAR)
Control Dependence
  Ordering of instruction i with respect to a branch instruction
    Instruction control dependent on a branch cannot be moved before the branch so that its execution is no longer controlled by the branch
    An instruction not control dependent on a branch cannot be moved after the branch so that its execution is controlled by the branch
Introduction

## Slide 28: Examples [RISC-V commands: R1x1, etc]
or instruction dependent on add and sub
Assume x4 isn’t used after skip
  Possible to move sub before the branch
Introduction
Example 1:
add x1,x2,x3
beq x4,x0,L
sub x1,x1,x6
L: …
or x7,x1,x8
Example 2:
add x1,x2,x3
beq x12,x0,skip
sub x4,x5,x6
add x5,x4,x9
skip:
or x7,x8,x9

## Slide 29: Compiler Techniques for Exposing ILP
Pipeline scheduling
  Separate dependent instruction from the source instruction by the pipeline latency of the source instruction
Example:
  for (i=999; i>=0; i=i-1)
  x[i] = x[i] + s;
Compiler Techniques

## Slide 30: Pipeline Stalls
Loop: fld f0,0(x1)
stall
fadd.d f4,f0,f2
stall
stall
fsd f4,0(x1)
addi x1,x1,-8
bne x1,x2,Loop
Compiler Techniques
Loop: fld f0,0(x1)
addi x1,x1,-8
fadd.d f4,f0,f2
stall
stall
fsd f4,08(x1) bne x1,x2,Loop
8 clock cycles 7 clock cycles

## Slide 31: Loop Unrolling
Loop unrolling
  Unroll by a factor of 4 (assume # elements is divisible by 4)
  Eliminate unnecessary instructions
Loop: fld f0,0(x1)
fadd.d f4,f0,f2
fsd f4,0(x1) //drop addi & bne
fld f6,-8(x1)
fadd.d f8,f6,f2
fsd f8,-8(x1) //drop addi & bne
fld f10,-16(x1)
fadd.d f12,f10,f2
fsd f12,-16(x1) //drop addi & bne
fld f14,-24(x1)
fadd.d f16,f14,f2
fsd f16,-24(x1)
addi x1,x1,-32
bne x1,x2,Loop
Compiler Techniques
note: number of live registers vs. original loop
6X4 + 2  26/4
clock cycles/loop

## Slide 32: Loop Unrolling/Pipeline Scheduling
Pipeline schedule the unrolled loop:
Loop: fld f0,0(x1)
fld f6,-8(x1)
fld f108,-16(x1)
fld f14,-24(x1)
fadd.d f4,f0,f2
fadd.d f8,f6,f2
fadd.d f12,f10,f2
fadd.d f16,f14,f2
fsd f4,0(x1)
fsd f8,-8(x1)
fsd f12,-16(x1)
fsd f16,-24(x1)
addi x1,x1,-32
bne x1,x2,Loop
Compiler Techniques
3X4 + 2 = 14 cycles
14/4 = 3.5 cycles per element

## Slide 33: 5 Loop Unrolling Decisions
Requires understanding how one instruction depends on another and how the instructions can be changed or reordered given the dependences:
Determine loop unrolling useful by finding that loop iterations were independent (except for maintenance code)
Use different registers to avoid unnecessary constraints forced by using same registers for different computations
Eliminate the extra test and branch instructions and adjust the loop termination and iteration code
Determine that loads and stores in unrolled loop can be interchanged by observing that loads and stores from different iterations are independent
  Transformation requires analyzing memory addresses and finding that they do not refer to the same address
Schedule the code, preserving any dependences needed to yield the same result as the original code

## Slide 34: Dependence graph reasoning
In the above example, each iteration had 3 “core instructions” A, B and C
Denote the instructions of iteration i: iA, iB and iC. Let us suppress for now control instructions.
Each instruction is a node in the dependence graph.
Each dependence is a directed edge
A common theme in the current chapter is seeking (towards execution) serial numbering of the instructions that obeys the directed edges
Such numbering is know as topological sort

## Slide 35: 3 Limits to Loop Unrolling
Decrease in amount of overhead amortized with each extra unrolling
  Amdahl’s Law
Growth in code size
  For larger loops, concern it increases the instruction cache miss rate
Register pressure: potential shortfall in registers created by aggressive unrolling and scheduling
  If not possible to allocate all live values to registers, may lose some or all of its advantage
Loop unrolling reduces impact of branches on pipeline; another way is branch prediction

## Slide 36: Strip Mining
Unknown (at compile time) number of loop iterations?
  Number of iterations = n
  Goal: make k copies of the loop body
  Generate pair of loops:
    First executes n mod k times
    Second executes n / k times
    “Strip mining”
Compiler Techniques

## Slide 37: Branch Prediction
Basic 2-bit predictor:
  For each branch:
    Predict taken or not taken
    If the prediction is wrong two consecutive times, change prediction
Correlating predictor:
  Multiple 2-bit predictors for each branch
  One for each possible combination of outcomes of preceding n branches
    (m,n) predictor: behavior from last m branches to choose from 2m n-bit predictors
Tournament predictor:
  Combine correlating predictor with local predictor
Branch Prediction

## Slide 38: Dynamic Branch Prediction
Solution: 2-bit scheme where change prediction only if get misprediction twice
Blue: stop, not taken
Grey: go, taken
Adds hysteresis (slowing effect) to decision making process
T
T
NT
NT
Predict Taken
Predict Not
Taken
Predict Taken
Predict Not
Taken
T
NT
T
NT

## Slide 39: Branch Prediction
Branch Prediction
gshare
tournament

## Slide 40: Branch Prediction Performance
Branch Prediction

## Slide 41: Branch Prediction Performance
Branch Prediction

## Slide 42: Tagged Hybrid Predictors
Need to have predictor for each branch and history
  Problem: this implies huge tables
  Solution:
    Use hash tables, whose hash value is based on branch address and branch history
    Longer histories may lead to increased chance of hash collision, so use multiple tables with increasingly shorter histories
Branch Prediction

## Slide 43: Tagged Hybrid Predictors
Branch Prediction

## Slide 44: Tagged Hybrid Predictors
Branch Prediction

## Slide 45: Dynamic Scheduling
Rearrange order of instructions to reduce stalls while maintaining data flow
Advantages:
  Compiler doesn’t need to have knowledge of microarchitecture
  Handles cases where dependencies are unknown at compile time
Disadvantage:
  Substantial increase in hardware complexity
  Complicates exceptions
Dynamic Scheduling

## Slide 46: Dynamic Scheduling
Dynamic scheduling implies:
  Out-of-order execution
  Out-of-order completion
Example 1:
  fdiv.d f0,f2,f4
  fadd.d f10,f0,f8
  fsub.d f12,f8,f14
  fsub.d is not dependent, issue before fadd.d
Dynamic Scheduling

## Slide 47: Dynamic Scheduling
Example 2:
  fdiv.d f0,f2,f4
  fmul.d f6,f0,f8
  fadd.d f0,f10,f14
  fadd.d is not dependent, but the antidependence makes it impossible to issue earlier without register renaming
Dynamic Scheduling

## Slide 48: Register Renaming
Example 3:
fdiv.d f0,f2,f4
fadd.d f6,f0,f8
fsd f6,0(x1)
fsub.d f8,f10,f14
fmul.d f6,f10,f8
  name dependence with f6
antidependence
antidependence
Dynamic Scheduling

## Slide 49: Register Renaming
Example 3:
fdiv.d f0,f2,f4
fadd.d S,f0,f8
fsd S,0(x1)
fsub.d T,f10,f14
fmul.d f6,f10,T
Now only RAW hazards remain, which can be strictly ordered
Dynamic Scheduling

## Slide 50: Register Renaming
Tomasulo’s Approach
  Tracks when operands are available
  Introduces register renaming in hardware
    Minimizes WAW and WAR hazards
Register renaming is provided by reservation stations (RS)
  Contains:
    The instruction
    Buffered operand values (when available)
    Reservation station number of instruction providing the operand values
Dynamic Scheduling

## Slide 51: Register Renaming
RS fetches and buffers an operand as soon as it becomes available (not necessarily involving register file)
Pending instructions designate the RS to which they will send their output
  Result values broadcast on a result bus, called the common data bus (CDB)
Only the last output updates the register file
As instructions are issued, the register specifiers are renamed with the reservation station
May be more reservation stations than registers
Load and store buffers
  Contain data and addresses, act like reservation stations
Dynamic Scheduling

## Slide 52: A Dynamic Algorithm: Tomasulo’s
For IBM 360/91 (before caches!)
   Long memory latency
Goal: High Performance without special compilers
Small number of floating point registers (4 in 360) prevented interesting compiler scheduling of operations
  This led Tomasulo to try to figure out how to get more effective registers — renaming in hardware!
Why Study 1966 Computer?
The descendants of this have flourished!
  Alpha 21264, Pentium 4, AMD Opteron, Power 5, …

## Slide 53: Tomasulo Algorithm
Control & buffers distributed with Function Units (FU)
  FU buffers called “reservation stations”; have pending operands
Registers in instructions replaced by values or pointers to reservation stations(RS); called register renaming ;
  Renaming avoids WAR, WAW hazards
  More reservation stations than registers, so can do optimizations compilers can’t
Results to FU from RS, not through registers, over Common Data Bus that broadcasts results to all FUs
  Avoids RAW hazards by executing an instruction only when its operands are available
Load and Stores treated as FUs with RSs as well
Integer instructions can go past branches (predict taken), allowing FP ops beyond basic block in FP queue

## Slide 54: Tomasulo’s Algorithm
Dynamic Scheduling

## Slide 55: Tomasulo’s Algorithm
Three Steps:
  Issue
    Get next instruction from FIFO queue
    If available RS, issue the instruction to the RS with operand values if available
    If operand values not available, stall the instruction
  Execute
    When operand becomes available, store it in any reservation stations waiting for it
    When all operands are ready, issue the instruction
    Loads and store maintained in program order through effective address
    No instruction allowed to initiate execution until all branches that proeceede it in program order have completed
  Write result
    Write result on CDB into reservation stations and store buffers
      (Stores must wait until address and value are received)
Dynamic Scheduling

## Slide 56: Reservation Station Components
Op: Operation to perform in the unit (e.g., + or –)
Vj, Vk: Value of Source operands
  Store buffers has V field, result to be stored
Qj, Qk: Reservation stations producing source registers (value to be written)
  Note: Qj,Qk=0 => ready
  Store buffers only have Qi for RS producing result
Busy: Indicates reservation station or FU is busy
Register result status—Indicates which functional unit will write each register, if one exists. Blank when no pending instructions that will write that register.
Notes: What you might have thought
1. 4 stages of instruction executino
2.Status of FU: Normal things to keep track of (RAW & structura for busyl):
Fi from instruction format of the mahine (Fi is dest)
Add unit can Add or Sub
Rj, Rk - status of registers (Yes means ready)
Qj,Qk - If a no in Rj, Rk, means waiting for a FU to write result; Qj, Qk means wihch FU waiting for it
3.Status of register result (WAW &WAR)s:
which FU is going to write into registers
Scoreboard on 6600 = size of FU
6.7, 6.8, 6.9, 6.12, 6.13, 6.16, 6.17
FU latencies: Add 2, Mult 10, Div 40 clocks

## Slide 57: Three Stages of Tomasulo Algorithm & Example
1. Issue—get instruction from FP Op Queue
  If reservation station free (no structural hazard), control issues instr & sends operands (renames registers).
2. Execute—operate on operands (EX)
  When both operands ready then execute; if not ready, watch Common Data Bus for result
3. Write result—finish execution (WB)
  Write on Common Data Bus to all awaiting units; mark reservation station available
Normal data bus: data + destination (“go to” bus)
Common data bus: data + source (“come from” bus)
  64 bits of data + 4 bits of Functional Unit source address
  Write if matches expected Functional Unit (produces result)
  Does the broadcast
Example speed: 3 clocks for Fl .pt. +,-; 10 for * ; 40 clks for /

## Slide 58: Tomasulo Example
Clock cycle counter
FU count
down
Instruction stream
3 Load/Buffers
3 FP Adder R.S.
2 FP Mult R.S.

## Slide 59: Dependence Graph
‘Data Flow’ Perspective
Draw a node for each instruction
Draw and incoming edge for each data-dependence (including anti dependence)

## Slide 60: The dependence graph. 6 nodes shown. Add directed edge for RAW: result register = operand Note: F6 is WAR (or WAW)
LD F6 MULTD F0 F2 F4
DIVD F10 F0 F6
LD F2 SUBD F8 F6 F2
ADDD F6 F8 F2

## Slide 61: Tomasulo Example Cycle 1

## Slide 62: Tomasulo Example Cycle 2
Note: Can have multiple loads outstanding

## Slide 63: Tomasulo Example Cycle 3
Note: registers names are removed (“renamed”) in Reservation Stations; MULT issued
Load1 completing; what is waiting for Load1?

## Slide 64: Tomasulo Example Cycle 4
Load2 completing; what is waiting for Load2?

## Slide 65: Tomasulo Example Cycle 5
Timer starts down for Add1, Mult1. Unclear: Add starts at 2. Not 3.
Note: DIVD already has the value of F6  No WAR hazard for ADDD

## Slide 66: Tomasulo Example Cycle 6
Repeating: Issue ADDD here despite name dependency on F6?

## Slide 67: Tomasulo Example Cycle 7
Add1 (SUBD) completing; what is waiting for it?

## Slide 68: Tomasulo Example Cycle 8

## Slide 69: Tomasulo Example Cycle 9

## Slide 70: Tomasulo Example Cycle 10
Add2 (ADDD) completing; what is waiting for it?

## Slide 71: Tomasulo Example Cycle 11
Write result of ADDD here?
All quick instructions complete in this cycle!

## Slide 72: Tomasulo Example Cycle 12

## Slide 73: Tomasulo Example Cycle 13

## Slide 74: Tomasulo Example Cycle 14

## Slide 75: Tomasulo Example Cycle 15
Mult1 (MULTD) completing; what is waiting for it?

## Slide 76: Tomasulo Example Cycle 16
Just waiting for Mult2 (DIVD) to complete

## Slide 77: Faster than light computation (skip a couple of cycles)

## Slide 78: Tomasulo Example Cycle 55

## Slide 79: Tomasulo Example Cycle 56
Mult2 (DIVD) is completing; what is waiting for it?

## Slide 80: Tomasulo Example Cycle 57
Once again: In-order issue, out-of-order execution and out-of-order completion.

## Slide 81: Why can Tomasulo overlap iterations of loops?
Register renaming
  Multiple iterations use different physical destinations for registers (dynamic loop unrolling).
Reservation stations
  Permit instruction issue to advance past integer control flow operations
  Also buffer old values of registers - totally avoiding the WAR stall
Other perspective: Tomasulo building data flow dependency graph on the fly

## Slide 82: Tomasulo’s scheme offers 2 major advantages
Distribution of the hazard detection logic
  distributed reservation stations and the CDB
  If multiple instructions waiting on single result, & each instruction has other operand, then instructions can be released simultaneously by broadcast on CDB
  If a centralized register file were used, the units would have to read their results from the registers when register buses are available
Elimination of stalls for WAW and WAR hazards

## Slide 83: Tomasulo Drawbacks
Complexity
  delays of 360/91, MIPS 10000, Alpha 21264, IBM PPC 620 in CA:AQA 2/e, but not in silicon!
Many associative stores (CDB) at high speed
Performance limited by Common Data Bus
  Each CDB must go to multiple functional units high capacitance, high wiring density
  Number of functional units that can complete per cycle limited to one!
    Multiple CDBs  more FU logic for parallel assoc stores
Non-precise interrupts!
  We will address this later

## Slide 84: And In Conclusion … #1
Leverage Implicit Parallelism for Performance: Instruction Level Parallelism
Loop unrolling by compiler to increase ILP
Branch prediction to increase ILP
Dynamic HW exploiting ILP
  Works when can’t know dependence at compile time
  Can hide L1 cache misses
  Code for one machine runs well on another

## Slide 85: And In Conclusion … #2
Reservations stations: renaming to larger set of registers + buffering source operands
  Prevents registers as bottleneck
  Avoids WAR, WAW hazards
  Allows loop unrolling in HW
Not limited to basic blocks (integer units gets ahead, beyond branches) with speculation
Helps cache misses as well
Lasting Contributions
  Dynamic scheduling
  Register renaming
  Load/store disambiguation
360/91 descendants are Intel Pentium 4, IBM Power 5, AMD Athlon/Opteron, …

## Slide 86: Example
Dynamic Scheduling

## Slide 87: Tomasulo’s Algorithm
Example loop:
Loop: fld f0,0(x1)
fmul.d f4,f0,f2
fsd f4,0(x1)
addi x1,x1,8
bne x1,x2,Loop // branches if x16 != x2
Dynamic Scheduling

## Slide 88: Tomasulo’s Algorithm
Dynamic Scheduling

## Slide 89: Hardware-Based Speculation
Execute instructions along predicted execution paths but only commit the results if prediction was correct
Instruction commit: allowing an instruction to update the register file when instruction is no longer speculative
Need an additional piece of hardware to prevent any irrevocable action until an instruction commits
  I.e. updating state or taking an execution
Hardware-Based Speculation

## Slide 90: Reorder Buffer
Reorder buffer – holds the result of instructions between completion and commit
Four fields:
  Instruction type: branch/store/register
  Destination field: register number
  Value field: output value
  Ready field: completed execution?
Modify reservation stations:
  Operand source is now reorder buffer instead of functional unit
Hardware-Based Speculation

## Slide 91: Reorder Buffer
Issue:
  Allocate RS and ROB, read available operands
Execute:
  Begin execution when operand values are available
Write result:
  Write result and ROB tag on CDB
Commit:
  When ROB reaches head of ROB, update register
  When a mispredicted branch reaches head of ROB, discard all entries
Hardware-Based Speculation

## Slide 92: Reorder Buffer
Register values and memory values are not written until an instruction commits
On misprediction:
  Speculated entries in ROB are cleared
Exceptions:
  Not recognized until it is ready to commit
Hardware-Based Speculation

## Slide 93: Reorder Buffer
Hardware-Based Speculation

## Slide 94: Reorder Buffer
Hardware-Based Speculation

## Slide 95: Multiple Issue and Static Scheduling
To achieve CPI < 1, need to complete multiple instructions per clock
Solutions:
  Statically scheduled superscalar processors
  VLIW (very long instruction word) processors
  Dynamically scheduled superscalar processors
Multiple Issue and Static Scheduling

## Slide 96: Multiple Issue
Multiple Issue and Static Scheduling

## Slide 97: VLIW Processors
Package multiple operations into one instruction
Example VLIW processor:
  One integer instruction (or branch)
  Two independent floating-point operations
  Two independent memory references
Must be enough parallelism in code to fill the available slots
Multiple Issue and Static Scheduling

## Slide 98: Loop Unrolling/Pipeline Scheduling
Pipeline schedule the unrolled loop:
Loop: fld f0,0(x1)
fld f6,-8(x1)
fld f8,-16(x1)
fld f14,-24(x1)
fadd.d f4,f0,f2
fadd.d f8,f6,f2
fadd.d f12,f0,f2
fadd.d f16,f14,f2
fsd f4,0(x1)
fsd f8,-8(x1)
fsd f12,-16(x1)
fsd f16,-24(x1)
addi x1,x1,-32
bne x1,x2,Loop
Compiler Techniques
3X4 + 2 = 14 cycles
14/4 = 3.5 cycles per element

## Slide 99: Recall Loop Unrolling/Pipeline Scheduling
Pipeline schedule the unrolled loop:
Loop: fld f0,0(x1)
fld f6,-8(x1)
fld f8,-16(x1)
fld f14,-24(x1)
fadd.d f4,f0,f2
fadd.d f8,f6,f2
fadd.d f12,f0,f2
fadd.d f16,f14,f2
fsd f4,0(x1)
fsd f8,-8(x1)
fsd f12,-16(x1)
fsd f16,-24(x1)
addi x1,x1,-32
bne x1,x2,Loop
Compiler Techniques
3X4 + 2 = 14 cycles
14/4 = 3.5 cycles per element

## Slide 100: VLIW Processors
Disadvantages:
  Statically finding parallelism
  Code size
  No hazard detection hardware
  Binary code compatibility
Unrolled 7 times to avoid delays. 7 results in 9 clocks, or 1.3 clocks per iteration (1.8X). Average: 2.5 ops per clock, 50% efficiency. Note: Need more registers in VLIW (15 vs. 6 in SS)
Multiple Issue and Static Scheduling

## Slide 101: Problems with 1st Generation VLIW
Increase in code size
  generating enough operations in a straight-line code fragment requires ambitiously unrolling loops
  whenever VLIW instructions are not full, unused functional units translate to wasted bits in instruction encoding
Operated in lock-step; no hazard detection HW
  a stall in any functional unit pipeline caused entire processor to stall, since all functional units must be kept synchronized
  Compiler might predict function units, but caches hard to predict
Binary code compatibility
  Pure VLIW => different numbers of functional units and unit latencies require different versions of the code

## Slide 102: Intel/HP IA-64 “Explicitly Parallel Instruction Computer (EPIC)”
IA-64: instruction set architecture
128 64-bit integer regs + 128 82-bit floating point regs
  Not separate register files per functional unit as in old VLIW
Hardware checks dependencies (interlocks => binary compatibility over time)
Predicated execution (select 1 out of 64 1-bit flags) => 40% fewer mispredictions?
Itanium™ was first implementation (2001)
  Highly parallel and deeply pipelined hardware at 800Mhz
  6-wide, 10-stage pipeline at 800Mhz on 0.18 µ process
Itanium 2™ is name of 2nd implementation (2005)
  6-wide, 8-stage pipeline at 1666Mhz on 0.13 µ process
  Caches: 32 KB I, 32 KB D, 128 KB L2I, 128 KB L2D, 9216 KB L3

## Slide 103: Dynamic Scheduling, Multiple Issue, and Speculation
Modern microarchitectures:
  Dynamic scheduling + multiple issue + speculation
Two approaches:
  Assign reservation stations and update pipeline control table in half clock cycles
    Only supports 2 instructions/clock
  Design logic to handle any possible dependencies between the instructions
Issue logic is the bottleneck in dynamically scheduled superscalars
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 104: Overview of Design. Problem with figure: the main info is … in the caption. See next slide
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 105
Figure 3.21 The basic organization of a multiple issue processor with speculation. In this case, the organization could allow a FP multiply, FP add, integer, and load/store to all issues simultaneously (assuming one issue per clock per functional unit). Note that several datapaths must be widened to support multiple issues: the CDB, the operand buses, and, critically, the instruction issue logic, which is not shown in this figure. The last is a difficult problem, as we discuss in the text.

## Slide 106: Multiple Issue
Examine all the dependencies among the instructions in the bundle
If dependencies exist in bundle, encode them in reservation stations
Also need multiple completion/commit
To simplify RS allocation:
  Limit the number of instructions of a given class that can be issued in a “bundle”, i.e. on FP, one integer, one load, one store
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 107: Multithreading
Crosscutting topic relevant to pipelining & superscalar (Ch. 3), GPUs (Ch. 4) and multiporcessors (Ch. 5)
Thread: like a process that has state and program counter
But, threads typically share the address space of other threads, with easy access to their data within the same process.
(Underlined two non-identical use of the word “process”.)

## Slide 108
Figure 3.31 How four different approaches use the functional unit execution slots of a superscalar processor. The horizontal dimension represents the instruction execution capability in each clock cycle. The vertical dimension represents a sequence of clock cycles. An empty (white) box indicates that the corresponding execution slot is unused in that clock cycle. The shades of gray and black correspond to four different threads in the multithreading processors. Black is also used to indicate the occupied issue slots in the case of the superscalar without multithreading support. The Sun T1 and T2 (aka Niagara) processors are fine-grained, multithreaded processors, while the Intel Core i7 and IBM Power7 processors use SMT. The T2 has 8 threads, the Power7 has 4, and the Intel i7 has 2. In all existing SMTs, instructions issue from only one thread at a time. The difference in SMT is that the subsequent decision to execute an instruction is decoupled and could execute the operations coming from several different instructions in the same clock cycle.
Simultaneous MultiThreading (SMT)

## Slide 109: Example
Loop: ld x2,0(x1) //x2=array element
addi x2,x2,1 //increment x2
sd x2,0(x1) //store result
addi x1,x1,8 //increment pointer
bne x2,x3,Loop //branch if not last
Dynamic Scheduling, Multiple Issue, and Speculation
Consider the execution of this loop, on a two-issue processor.
Once without speculation.
Once with speculation

## Slide 110: Example (No Speculation)
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 111: Example (Mutiple Issue with Speculation)
Dynamic Scheduling, Multiple Issue, and Speculation

## Slide 112: Branch-Target Buffer
Need high instruction bandwidth
  Branch-Target buffers
    Next PC prediction buffer, indexed by current PC
Adv. Techniques for Instruction Delivery and Speculation

## Slide 113
Figure 3.25 A branch-target buffer. The PC of the instruction being fetched is matched against a set of instruction addresses stored in the first column; these represent the addresses of known branches. If the PC matches one of these entries, then the instruction being fetched is a taken branch, and the second field, predicted PC, contains the prediction for the next PC after the branch. Fetching begins immediately at that address. The third field, which is optional, may be used for extra prediction state bits.
Branch-Target Buffer

## Slide 114: Branch Folding
Optimization:
  Larger branch-target buffer
  Add target instruction into buffer to deal with longer decoding time required by larger buffer
  “Branch folding”
Adv. Techniques for Instruction Delivery and Speculation

## Slide 115: Return Address Predictor
Most unconditional branches come from function returns
The same procedure can be called from multiple sites
  Causes the buffer to potentially forget about the return address from previous calls
Create return address buffer organized as a stack
Adv. Techniques for Instruction Delivery and Speculation

## Slide 116: Return Address Predictor
Adv. Techniques for Instruction Delivery and Speculation

## Slide 117: Integrated Instruction Fetch Unit
Design monolithic unit that performs:
  Branch prediction
  Instruction prefetch
    Fetch ahead
  Instruction memory access and buffering
    Deal with crossing cache lines
Adv. Techniques for Instruction Delivery and Speculation

## Slide 118: Register Renaming
Register renaming vs. reorder buffers
  Instead of virtual registers from reservation stations and reorder buffer, create a single register pool
    Contains visible registers and virtual registers
    Conceptually extends Tomasulo’s register renaming to…registers
  Use hardware-based map to rename registers during issue
  WAW and WAR hazards are avoided
  Speculation recovery occurs by copying during commit
  Still need a ROB-like queue to update table in order
  Simplifies commit:
    Record that mapping between architectural register and physical register is no longer speculative
    Free up physical register used to hold older value
    In other words: SWAP physical registers on commit
  Physical register de-allocation is more difficult
    Simple approach: deallocate virtual register when next instruction writes to its mapped architecturally-visibly register
Adv. Techniques for Instruction Delivery and Speculation

## Slide 119: Integrated Issue and Renaming
Combining instruction issue with register renaming:
  Issue logic pre-reserves enough physical registers for the bundle
  Issue logic finds dependencies within bundle, maps registers as necessary
  Issue logic finds dependencies between current bundle and already in-flight bundles, maps registers as necessary
Adv. Techniques for Instruction Delivery and Speculation

## Slide 120: How Much?
How much to speculate
  Mis-speculation degrades performance and power relative to no speculation
    May cause additional misses (cache, TLB)
  Prevent speculative code from causing higher costing misses (e.g. L2)
Speculating through multiple branches
  Complicates speculation recovery
Speculation and energy efficiency
  Note: speculation is only energy efficient when it significantly improves performance
Adv. Techniques for Instruction Delivery and Speculation

## Slide 121: How Much?
Adv. Techniques for Instruction Delivery and Speculation
integer

## Slide 122: Energy Efficiency
Value prediction
  Uses:
    Loads that load from a constant pool
    Instruction that produces a value from a small set of values
  Not incorporated into modern processors
  Similar idea--address aliasing prediction--is used on some processors to determine if two stores or a load and a store reference the same address to allow for reordering
Adv. Techniques for Instruction Delivery and Speculation

## Slide 123: Fallacies and Pitfalls
It is easy to predict the performance/energy efficiency of two different versions of the same ISA if we hold the technology constant
Fallacies and Pitfalls

## Slide 124: Fallacies and Pitfalls
Processors with lower CPIs / faster clock rates will also be faster
  Pentium 4 had higher clock, lower CPI
  Itanium had same CPI, lower clock
Fallacies and Pitfalls

## Slide 125: Fallacies and Pitfalls
Sometimes bigger and dumber is better
  Pentium 4 and Itanium were advanced designs, but could not achieve their peak instruction throughput because of relatively small caches as compared to i7
And sometimes smarter is better than bigger and dumber
  TAGE branch predictor outperforms gshare with less stored predictions
Fallacies and Pitfalls

## Slide 126: Fallacies and Pitfalls
Believing that there are large amounts of ILP available, if only we had the right techniques
Fallacies and Pitfalls