## Slide 1
Chapter 6
Warehouse-Scale Computers to Exploit Request-Level and Data-Level Parallelism
Computer Architecture
A Quantitative Approach, Sixth Edition

## Slide 2: Introduction
Warehouse-scale computer (WSC)
  Provides Internet services
    Search, social networking, online maps, video sharing, online shopping, email, cloud computing, etc.
  Differences with HPC “clusters”:
    Clusters have higher performance processors and network
    Clusters emphasize thread-level parallelism, WSCs emphasize request-level parallelism
  Differences with datacenters:
    Datacenters consolidate different machines and software into one location
    Datacenters emphasize virtual machines and hardware heterogeneity in order to serve varied customers
Introduction

## Slide 3: Introduction
Important design factors for WSC:
  Cost-performance
    Small savings add up
  Energy efficiency
    Affects power distribution and cooling
    Work per joule
  Dependability via redundancy
  Network I/O
  Interactive and batch processing workloads
Introduction

## Slide 4
Figure 6.1 List of outages and anomalies with the approximate frequencies of occurrences in the first year of a new cluster of 2400 servers. We label what Google calls a cluster an array; see Figure 6.5. Based on Barroso, L.A., 2010. Warehouse Scale Computing [keynote address]. In: Proceedings of ACM SIGMOD, June 8–10, 2010, Indianapolis, IN.

## Slide 5: Introduction
  Ample computational parallelism is not important
    Most jobs are totally independent
    “Request-level parallelism”
  Operational costs count
    Power consumption is a primary, not secondary, constraint when designing system
  Scale and its opportunities and problems
    Can afford to build customized systems since WSC require volume purchase
  Location counts
    Real estate, power cost; Internet, end-user, and workforce availability
  Computing efficiently at low utilization
  Scale and the opportunities/problems associated with scale
    Unique challenges: custom hardware, failures
    Unique opportunities: bulk discounts
Introduction

## Slide 6: Efficiency and Cost of WSC
Location of WSC
  Proximity to Internet backbones, electricity cost, property tax rates, low risk from earthquakes, floods, and hurricanes
Power distribution
Efficiency and Cost of WSC

## Slide 7: Prgrm’g Models and Workloads
Batch processing framework: MapReduce
  Map: applies a programmer-supplied function to each logical input record
    Runs on thousands of computers
    Provides new set of key-value pairs as intermediate values
  Reduce: collapses values using another programmer-supplied function
Programming Models and Workloads for WSCs

## Slide 8: Prgrm’g Models and Workloads
Example:
  map (String key, String value):
    // key: document name
    // value: document contents
    for each word w in value
      EmitIntermediate(w,”1”); // Produce list of all words
  reduce (String key, Iterator values):
    // key: a word
    // value: a list of counts
    int result = 0;
    for each v in values:
      result += ParseInt(v); // get integer from key-value pair
    Emit(AsString(result));
Programming Models and Workloads for WSCs

## Slide 9: Prgrm’g Models and Workloads
Availability:
  Use replicas of data across different servers
  Use relaxed consistency:
    No need for all replicas to always agree
File systems: GFS and Colossus
Databases: Dynamo and BigTable
Programming Models and Workloads for WSCs

## Slide 10: Prgrm’g Models and Workloads
MapReduce runtime environment schedules map and reduce task to WSC nodes
  Workload demands often vary considerably
  Scheduler assigns tasks based on completion of prior tasks
  Tail latency/execution time variability: single slow task can hold up large MapReduce job
  Runtime libraries replicate tasks near end of job
Programming Models and Workloads for WSCs

## Slide 11: Prgrm’g Models and Workloads
Programming Models and Workloads for WSCs

## Slide 12: Computer Architecture of WSC
WSC often use a hierarchy of networks for interconnection
Each 19” rack holds 48 1U servers connected to a rack switch
Rack switches are uplinked to switch higher in hierarchy
  Uplink has 6-24X times lower bandwidthGoal is to maximize locality of communication relative to the rack
Computer Ar4chitecture of WSC

## Slide 13: Storage
Storage options:
  Use disks inside the servers, or
  Network attached storage through Infiniband
  WSCs generally rely on local disks
  Google File System (GFS) uses local disks and maintains at least three replicas
Computer Ar4chitecture of WSC

## Slide 14: Array Switch
Switch that connects an array of racks
  Array switch should have 10 X the bisection bandwidth of rack switch
  Cost of n-port switch grows as n2
  Often utilize content addressible memory chips and FPGAs
Computer Ar4chitecture of WSC

## Slide 15: WSC Memory Hierarchy
Servers can access DRAM and disks on other servers using a NUMA-style interface
Computer Ar4chitecture of WSC

## Slide 16
Figure 6.6 Latency, bandwidth, and capacity of the memory hierarchy of a WSC (Barroso et al., 2013). Figure 6.7 plots this same information.

## Slide 17: WSC Memory Hierarchy
Computer Ar4chitecture of WSC

## Slide 18
Figure 6.7 Graph of latency, bandwidth, and capacity of the memory hierarchy of a WSC for data in Figure 6.6 (Barroso et al., 2013).
The meaningful things are:
The behavior of each line separately.
Comparing the relative changes among the lines.

## Slide 19: WSC Memory Hierarchy
Computer Ar4chitecture of WSC

## Slide 20
Figure 6.8 A Layer 3 network used to link arrays together and to the Internet (Greenberg et al., 2009). A load balancer monitors how busy a set of servers is and directs traffic to the less loaded ones to try to keep the servers approximately equally utilized. Another option is to use a separate border router to connect the Internet to the data center Layer 3 switches. As we will see in Section 6.6, many modern WSCs have abandoned the conventional layered networking stack of traditional switches.

## Slide 21: Infrastructure and Costs of WSC
Cooling
  Air conditioning used to cool server room
  64 F – 71 F
    Keep temperature higher (closer to 71 F)
  Cooling towers can also be used
    Minimum temperature is “wet bulb temperature”
Physcical Infrastrcuture and Costs of WSC

## Slide 22
Figure 6.9 Mechanical design for cooling systems. CWS stands for circulating water system. From Hamilton, J., 2010. Cloud computing economies of scale. In: Paper Presented at the AWS Workshop on Genomics and Cloud Computing, June 8, 2010, Seattle, WA. http://mvdirona.com/jrh/TalksAndPapers/JamesHamilton_GenomicsCloud20100608.pdf.

## Slide 23: Infrastructure and Costs of WSC
Cooling system also uses water (evaporation and spills)
  E.g. 70,000 to 200,000 gallons per day for an 8 MW facility
Power cost breakdown:
  Chillers: 30-50% of the power used by the IT equipment
  Air conditioning: 10-20% of the IT power, mostly due to fans
How many servers can a WSC support?
  Each server:
    “Nameplate power rating” gives maximum power consumption
    To get actual, measure power under actual workloads
  Oversubscribe cumulative server power by 40%, but monitor power closely
Physcical Infrastrcuture and Costs of WSC

## Slide 24: Infrastructure and Costs of WSC
Determining the maximum server capacity
  Nameplate power rating: maximum power that a server can draw
  Better approach: measure under various workloads
  Oversubscribe by 40%
Typical power usage by component:
  Processors: 42%
  DRAM: 12%
  Disks: 14%
  Networking: 5%
  Cooling: 15%
  Power overhead: 8%
  Miscellaneous: 4%
Physcical Infrastrcuture and Costs of WSC

## Slide 25: Measuring Efficiency of a WSC
Power Utilization Effectiveness (PEU)
  = Total facility power / IT equipment power
  Median PUE on 2006 study was 1.69
Performance
  Latency is important metric because it is seen by users
  Bing study: users will use search less as response time increases
  Service Level Objectives (SLOs)/Service Level Agreements (SLAs)
    E.g. 99% of requests be below 100 ms
Physcical Infrastrcuture and Costs of WSC

## Slide 26: Measuring Efficiency of a WSC
Physcical Infrastrcuture and Costs of WSC

## Slide 27
Figure 6.12 Negative impact of delays at the Bing search server on user behavior (Schurman and Brutlag, 2009).

## Slide 28: Cost of a WSC
Capital expenditures (CAPEX)
  Cost to build a WSC
  $9 to 13/watt
Operational expenditures (OPEX)
  Cost to operate a WSC
Physcical Infrastrcuture and Costs of WSC

## Slide 29: Cloud Computing
Amazon Web Services
  Virtual Machines: Linux/Xen
  Low cost
  Open source software
  Initially no guarantee of service
  No contract
Cloud Computing

## Slide 30: Cloud Computing
Cloud Computing Growth
Cloud Computing

## Slide 31: Fallacies and Pitfalls
Fallacy: Cloud computing providers are losing money
  AWS has a margin of 25%, Amazon retail 3%
Pitfall: Focusing on average performance instead of 99th percentile performance. Even getting bad performance infrequently is enough to drive cloud customer to a competitor
Pitfall: Using too wimpy a processor when trying to improve WSC cost-performance
Pitfall: Inconsistent Measure of PUE (Power Utilization Effectiveness) by different companies
Fallacy: Capital costs of the WSC facility are higher than for the servers that it houses
Fallcies and Pitfalls

## Slide 32: Fallacies and Pitfalls
Pitfall: Trying to save power with inactive low power modes versus active low power modes
Fallacy: Given improvements in DRAM dependability and the fault tolerance of WSC systems software, there is no need to spend extra for ECC (error correcting code) memory in a WSC
Pitfall: Coping effectively with microsecond (e.g. Flash and 100 GbE) delays as opposed to nansecond or millisecond delays (namely: all delays are important)
Fallacy: Turning off hardware during periods of low activity improves the cost-performance of a WSC
Fallcies and Pitfalls