## Slide 1: General-Purpose Many-Core Parallelism – Broken, But Fixable
Uzi Vishkin
Scope: max speedup from on-chip parallelism
Notes: Consider the level of application innovation in high-end general-purposes desktop computing over the last decade. I believe that it has been minimal, perhaps with the exception of computer graphics. Consider progress on internet and mobile for comparison where nearly 500,000 work developing mobile apps on their own dime.
Being motivated. Before technology constraints forced Intel to move to multi-cores, it was forced to extend X86 from 32- to 64-bit. Intel invested $4B in the Itanium and then wanted to cancel it. Was put on the right track only because competition from AMD. No correcting competition existed for over a decade. Will better conditions for competition emerge?

## Slide 2: Commodity computer systems
19462003 General-purpose computing: Serial. 5KHz4GHz.
2004 Clock frequency growth flatGeneral-purpose computing goes parallel. ’If you want your program to run significantly faster … you’re going to have to parallelize it’
19802014
#Transistors/chip: 29K10sB
Bandwidth/latency: 300
Intel Platform 2015, March05:
#”cores”: ~dy-2003
~2011: Advance from d1 to d2
Did this happen?..
Notes: Did this happen – have we even stayed on d1 ?

## Slide 3: How is many-core parallel computing doing?
Current-day system architectures allow good speedups on regular dense-matrix type programs, but are basically unable to do much outside that
What’s missing
  Irregular problems/program
  Strong scaling, and
  - Cost-effective parallel programming for regular problems
    Sweat-to-gain ratio is (often too) high
    Though some progress with domain-specific languages
Requires revolutionary approach
  Revolutionary: Throw out & replace   high bar
Notes: Students in my recent computer engineering junior class were dismayed to hear that. Nearly all (mostly serial) programs they have learned and written do not fit this mold and they felt that this was too limiting.

## Slide 4: Example Memory How did serial architectures deal with locality?
1. Gap opened between improvements in
  - Latency to memory, and
  - Processor speed
2. Locality observation Serial programs tend to reuse data, or nearby addresses 
  Increasing role for caches in architecture; yet,
  Same basic programming model
In summary
Starting point: Successful programming model
Found a way to hold on to it

## Slide 5: Locality in Parallel Computing
Early on Processors with local memory
 Practice of parallel programming meant:
  Program for parallelism, and
  Program for locality
Consistent with: design for peak performance
But, not with: cost-effective programming
In summary
Never: Truly successful parallel programming model
 Less to hold on to..

## Slide 6: Back-up: Current systems/revolutionary changes
  Multiprocessors HP-12: Computer consisting of tightly coupled processors whose coordination and usage are controlled by a single OS and that share memory through a shared address space
  GPUs HW handles thread management. But, leave open missing items
  BACKUP:
  Goal Fit as many FUs as you can into silicon. Now, use all of them all the time
  Architecture, including memory, optimized for peak performance on limited workloads, rather than sustained general-purpose performance
  Each thread is SIMD  limit on thread divergence (both sides of a branch)
  HW uses parallelism for FUs and hiding memory latency
    No: shared cache for general data, or truly all-to-all interconnection network to shared memory  Works well for plenty of “structured” parallelism
  Minimal parallelism: just to break even with serial 
  Cannot handle serial & low-parallel code. Leave open missing items: strong scaling, irregular, cost-effective regular
  Also: DARPA-HProductivityCS. Still: “Only heroic programmers can exploit the vast parallelism in today’s machines” [“GameOver”, CSTB/NAE’11]

## Slide 7
Build-first, figure-out-how-to-program later  architecture
Graphics cards
Where to start
Parallel programming: MPI, Open MP
GPUs. CUDA. GPGPU
so that
ν Dense-matrix-type
X Irregular,Cost-effective,Strong scaling
ν
Heterogeneous system
Hardware-first threads
Place holder
Past
Future?
Heterogeneous   lowering the bar: Keep what we have, but augment it.
Enabled by: increasing transistor budget, 3D VLSI & design of power

## Slide 8
Build-first, figure-out-how-to-program later  architecture
Graphics cards
How to think about parallelism? PRAM & Parallel algorithms
Parallel programming: MPI, Open MP
GPUs. CUDA. GPGPU
Concepts Theory, MTA, NYU-Ultra SB-PRAM, XMT Many-core. Quantitative validation XMT
ν Dense-matrix-type
X Irregular,Cost-effective,Strong scaling
Fine, but more important:
ν
Heterogeneous system
Hardware-first threads
Algorithms-first thread
Past
Future?
Legend: Remainder of this talk

## Slide 9: Serial Abstraction & A Parallel Counterpart
Serial abstraction: any single instruction available for execution in a serial program executes immediately – ”Immediate Serial Execution (ISE)”
Abstraction for making parallel computing simple: indefinitely many instructions, which are available for concurrent execution, execute immediately, dubbed Immediate Concurrent Execution (ICE) – same as ‘parallel algorithmic thinking (PAT)’ for PRAM
What could I do in parallel at each step assuming unlimited hardware

#
ops
..
..
time
#
ops
..
..
.
.
.
.
.
.
time
Time = Work
Work = total #ops
Time << Work
Serial Execution, Based on Serial Abstraction
Parallel Execution, Based on Parallel Abstraction
Notes: Serial--Abstracts away: different execution time for operation (memory hierarchy). Made serial programming simple. Programmers: conceptualize. HW and compilers: implement. Program: instruction to execute next (inductively)
Parallel--Step-by-step (inductive) explication of the instructions available next for concurrent execution. # processors not even mentioned. Falls back on the serial abstraction if 1 instruction/step

## Slide 10
Example of Parallel algorithm Breadth-First-Search (BFS)

## Slide 13
Parallel complexity
W = ~(|V| + |E|)
T = ~d, the number of layers
Average parallelism = ~W/T
(i) “Concurrently” as in natural BFS: only change to serial algorithm
(ii) Defies “decomposition”/”partition”
Mental effort
1. Sometimes easier than serial
2. Within common denominator of other parallel approaches. In fact, much easier

## Slide 14: Memory example (cont’d)
XMT Approach
Rationale Consider parallel version of serial algorithm
Premise Similar* locality to serial 
  1. Large shared cache on-chip
  2. High-bandwidth, low latency interconnection network
[2011 technical introduction: Using Simple Abstraction to Reinvent Computing for Parallelism, CACM, 1/2011, 75-85 http://www.umiacs.umd.edu/users/vishkin/XMT/]
3D VLSI Bigger shared cache, lower distance (latency & power for data movement) and bandwidth with TSVs (through-silicon vias)
* Parallel transitions from time t to t+1: subset of serial transitions

## Slide 15: Not just talking
Algorithms&Software
ICE/WorkDepth/PAT
Creativity ends here
PRAM
Programming & workflow
No ‘parallel programming’ course beyond freshmen
Stable compiler
IP for dynamic thread allocation  Intel TBB 4/13
PRAM-On-Chip HW Prototypes
64-core, 75MHz FPGA of XMT
(Explicit Multi-Threaded) architecture
SPAA98..CF08
128-core intercon. network IBM 90nm: 9mmX5mm, 400 MHz [HotI07]Fund
work on asynch NOCS’10
FPGA designASIC
IBM 90nm: 10mmX10mm
Scales: 1K+ cores on-chip. Power & Tech updates  cycle accurate simulator
Notes: Creativity--By nature, algorithms require some level of creativity. Ideally, programming does not.

## Slide 16: Orders-of-magnitude speedups & complexity Next slide: ease-of-programming
 | XMT | GPU/CPU | factor
Graph Biconnectivity 2012 | 33X | 4X random graphs Muuuch parallelism | >>8
Graph Triconnectivity 2012 | 129X | ? | ?
Max Flow 2011 | 108X | 2.5X | 43
Burrows Wheeler Compression Transform - bzip2 Decompression | 25X 13X | X/2.8 … on GPU ? | 70 ?
non-trivial stress tests
- 3 graph algorithms: No algorithmic creativity.
- 1st “truly parallel” speedup for lossless data compression. SPAA 2013. Beats Google Snappy (message passing within warehouse scale computers)
State of project
- 2012: quant validation of (most advanced) PRAM algorithms: ~65 man years
2013-: 1. Apps 2. Update Memory&enabling technologies/opportunities. 3. Minimize HW investment. Fit into current ecosystem (ARM,POWER,X86).

## Slide 17: Not alone in building new parallel computer prototypes in academia
At least 3 more US universities in the last 2 decades
Unique(?) daring own course-taking students to program it for performance
  - Graduate students do 6 programming assignments, including biconnectivity, in a theory course
  - Freshmen do parallel programming assignments for problem load competitive with serial course
And we went out for
  HS students: magnet and inner city schools
“XMT is an essential component of our Parallel Computing courses because it is the one place where we are able to strip away industrial accidents from the student's mind, in terms of programming necessity, and actually build creative algorithms to solve problems”—national award winning HS teacher. 6th year of teaching XMT. 81 HS students in 2013.
  HS vs PhD success stories
  And …

## Slide 18: Middle School Summer Camp Class, July’09 (20 of 22 students). Math HS Teacher D. Ellison, U. Indiana
Notes: 7 were rising 6th graders
Summer camp for children from underrepresented groups

## Slide 19: What about the missing items ?
Recap
Feasible Orders of magnitude better with different hardware.
Evidence Broad portfolio; e.g., most advanced parallel algorithms; high-school students do PhD-thesis level work
Who should care?
- DARPA Opportunity for competitors to surprise the US military and economy
Vendors
  Confluence of mobile & wall-plugged processor market creates unprecedented competition. Standard: ARM. Quad-cores and architecture techniques reached plateau. No other way to get significantly ahead.
  Smart node in the cloud helped by large local memories of other nodes
  Bring Watson irregular technologies to personal user

## Slide 20: But,
- Chicken-and-egg effect Few end-user apps use missing items (since..missing)
- My guess Under water, the “end-user application iceberg” is much larger than today’s parallel end-user applications.
Supporting evidence
  Irregular problems: many and rising. Data compression. Computer Vision. Bio-related. Sparse scientific. Sparse sensing & recovery. EDA
  “Test of the educated innocents”
    Students in last computer engineering non-elective class: nearly all serial programs we learned/wrote do not fit this regular mold
    Cannot believe that the regular mold is sufficient for more than a small minority of potential applications
    For balance Heard from a colleague: so we teach the wrong things
2013 Embedded processor vendors hear from their customers. New attitude…

## Slide 21: Can such ideas gain traction?
Naive answer: “Sure, since they are good”.
So, why not in the past?
  Wall Street companies: risk averse. Too big for startup
  Focus on fighting out GPUs (only competition)
  60+ yrs same “computing stack”  lowest common ancestor of company units for change: CEO… who can initiate it? … Turf issues

## Slide 22: My conclusion
- A time bomb that will explode sooner or later
- Will take over domination of a core area of IT. How much more?

## Slide 23: Snapshot: XMT High-level language
Cartoon Spawn creates threads; a
thread progresses at its own speed
and expires at its Join.
Synchronization: only at the Joins. So,
virtual threads avoid busy-waits by
expiring. New: Independence of order
semantics (IOS)
The array compaction (artificial) problem
Input: Array A[1..n] of elements.
Map in some order all A(i) not equal 0 to array D.
1
0
5
0
0
0
4
0
0
1
4
5
e0
e2
e6
A
D
For program below:
e$ local to thread $;
x is 3

## Slide 24: XMT-C
Single-program multiple-data (SPMD) extension of standard C.
Includes Spawn and PS - a multi-operand instruction.
Essence of an XMT-C program
int x = 0;
Spawn(0, n-1) /* Spawn n threads; $ ranges 0 to n − 1 */
{ int e = 1;
if (A[$] not-equal 0)
{ PS(x,e);
D[e] = A[$] }
}
n = x;
Notes: (i) PS is defined next (think F&A). See results for
e0,e2, e6 and x. (ii) Join instructions are implicit.

## Slide 25: XMT Assembly Language
Standard assembly language, plus 3 new instructions: Spawn, Join, and PS.
The PS multi-operand instruction
New kind of instruction: Prefix-sum (PS).
Individual PS, PS Ri Rj, has an inseparable (“atomic”) outcome:
Store Ri + Rj in Ri, and
(ii) Store original value of Ri in Rj.
Several successive PS instructions define a multiple-PS instruction. E.g., the
sequence of k instructions:
PS R1 R2; PS R1 R3; ...; PS R1 R(k + 1)
performs the prefix-sum of base R1 elements R2,R3, ...,R(k + 1) to get:
R2 = R1; R3 = R1 + R2; ...; R(k + 1) = R1 + ... + Rk; R1 = R1 + ... + R(k + 1).
Idea: (i) Several ind. PS’s can be combined into one multi-operand instruction.
(ii) Executed by a new multi-operand PS functional unit. Enhanced Fetch&Add.
Story: 1500 cars enter a gas station with 1000 pumps. Main XMT patent: Direct in unit time a car to a EVERY pump; PS patent: Then, direct in unit time a car to EVERY pump becoming available

## Slide 26: Programmer’s Model as Workflow
Arbitrary CRCW Work-depth algorithm.
- Reason about correctness & complexity in synchronous PRAM-like model
SPMD reduced synchrony
  Main construct: spawn-join block. Can start any number of processes at once. Threads advance at own speed, not lockstep
  Prefix-sum (ps). Independence of order semantics (IOS) – matches Arbitrary CW. For locality: assembly language threads are not-too-short
  Establish correctness & complexity by relating to WD analyses
  Circumvents: (i) decomposition-inventive; (ii) “the problem with threads”, e.g., [Lee]. Issue addressed in a PhD thesis nesting of spawns
Tune (compiler or expert programmer): (i) Length of sequence of round trips to memory, (ii) QRQW, (iii) WD. [VCL07]
  - Correctness & complexity by relating to prior analyses
spawn
join
spawn
join
Notes: Prefix-sum is the well-known fetch-and-add/increment commutative ‘atomic operation’, introduced by the NYU-Ultracomputer project in the early 1980s.
Our only innovation there is in a more efficient direct HW implementation

## Slide 27: XMT Architecture Overview
BestInClass serial core – master thread control unit (MTCU)
Parallel cores (TCUs) grouped in clusters
Global memory space evenly partitioned in cache banks using hashing
No local caches at TCU. Avoids expensive cache coherence hardware
HW-supported run-time load-balancing of concurrent threads over processors. Low thread creation overhead. (Extend classic stored-program+program counter; cited by 40 patents; Prefix-sum to registers & to memory. )
Cluster 1
Cluster 2
Cluster C
DRAM Channel 1
DRAM Channel D
MTCU
Hardware Scheduler/Prefix-Sum Unit
Parallel Interconnection Network
Memory Bank 1
Memory Bank 2
Memory Bank M
Shared Memory
(L1 Cache)
…
- Enough interconnection network
bandwidth
Notes: Back-up slide: XMT Block Diagram –

## Slide 28: Backup - Holistic design
Lead question How to build and program general-purpose many-core processors for single task completion time?
Carefully design a highly-parallel platform ~Top-down objectives:
High PRAM-like abstraction level. ‘Synchronous’.
Easy coding Isolate creativity to parallel algorithms
Not falling behind on any type & amount of parallelism
Backwards compatibility on serial
Have HW operate near its full intrinsic capacity
Reduced-synchrony & no busy-waits; to accommodate varied memory response time
Low overhead start & load balancing of fine-grained threads
High all-to-all processors/memory bandwidth. Parallel memories
Notes: Easy code--
See next slide for my inspiration on how to operate near full intrinsic capacity
Tensions: Synchronous for higher abstraction, reduced synchrony & no-busy-waits for physical reality

## Slide 29: Backup- How?
The contractor’s algorithm
1. Many job sites: Place a ladder in every LR 
2. Make progress as your capacity allows
System principle 1st/2nd order PoR/LoR
PoR: Predictability of reference
LoR: Locality of reference
Presentation challenge
Vertical platform. Each level: lifetime career
Strategy Snapshots. Limitation Not as satisfactory
Notes: Place a ladder:
Each processor represents a job site: issues instructions and when the working material arrives can fire-up the functional-units (laborers).
Inspired by a contractor at home. He perfected this so well that we needed to replace him in order get back our life

## Slide 30
The classic SW-HW bridge, GvN47
Program-counter & stored program
XMT: upgrade for parallel abstraction
Virtual over physical:
distributed solution
H. Goldstine, J. von Neumann.
Planning and coding problems for an
electronic computing instrument, 1947
Notes: GvN47

## Slide 31: Revisit of “how to gain traction”
Ideal for commercialization: add “HW hooks” to current CPU IP
Next best thing:
  Reuse as much as possible
  Benefit from ecosystem of ISA

## Slide 32: Workflow from parallel algorithms to programming versus trial-and-error
Option 1
PAT
Rethink algorithm: Take better advantage of cache
Hardware
PAT
Tune
Hardware
Option 2
Parallel algorithmic thinking (say PRAM)
Compiler
Is Option 1 good enough for the parallel programmer’s model?
Options 1B and 2 start with a PRAM algorithm, but not option 1A.
Options 1A and 2 represent workflow, but not option 1B.
Not possible in the 1990s.
Possible now.
Why settle for less?
Insufficient inter-thread bandwidth?
Domain decomposition,
or task decomposition
Program
Program
Prove
correctness
Still correct
Still correct
Legend creativity hyper-creativity [More creativity  less productivity]
Sisyphean(?)
loop

## Slide 33: Who should produce the parallel code?
Choices [state-of-the-art compiler research perspective]
Programmer only
  Writing parallel code is tedious.
  Good at ‘seeing parallelism’, esp. irregular parallelism.
  But are bad at seeing locality and granularity considerations.
    Have poor intuitions about compiler transformations.
Compiler only
  Can see regular parallelism, but not irregular parallelism.
  Great at doing compiler transformations to improve parallelism, granularity and locality.
 Hybrid solution: Programmer specifies high-level parallelism, but little else. Compiler does the rest.
Goals:
Ease of programming
  Declarative programming
(My) Broader questions
Where will the algorithms come from?
Is today’s HW good enough?
XMT relevant for all 3 questions
Thanks: Prof. Barua
Notes: For question on algorithm: obvious.
For question on compilers: see Prof. Barua’s comments. XMT is all about ‘seeing parallelism’.
For HW: stay tuned. Hint: engineering (not computer engineering…) typically goes from specs to building.

## Slide 34: Denial Example: BFS [EduPar2011]
2011 NSF/IEEE-TCPP curriculum teach BFS using OpenMP
Teaching experiment Joint F2010 UIUC/UMD class. 42 students
Good news Easy coding (since no meaningful ‘decomposition’)
Bad news None got speedup over serial on 8-proc SMP machine
BFS alg was easy but .. no good: no speedups
Speedups on 64-processor XMT 7x to 25x
Hey, unfair! Hold on: <1/4 of the silicon area of SMP
Symptom of the bigger “denial”
‘Only problem Developers lack parallel programming skills’
Solution Education. False Teach then see that HW is the problem
HotPAR10 performance results include BFS:
XMT/GPU Speed-up same silicon area, highly parallel input: 5.4X
Small HW configuration, large diameter: 109X wrt same GPU
Notes: Unfair since 64 processors are compared to 8

## Slide 35: Discussion of BFS results
Contrast with smartest people: PPoPP’12, Stanford’11 .. BFS on multi-cores, again only if the diameter is small, improving on SC’10 IBM/GaTech & 6 recent papers, all 1st rate conferences
BFS is bread & butter. Call the Marines each time you need
bread? Makes one wonder Is something wrong with the field?
‘Decree’ Random graphs = ‘reality’. In the old days: Expander graphs taught in graph design. Planar graphs were real
Lots of parallelism  more HW design freedom. E.g., GPUs get decent speedup with lots of parallelism, and
But, not enough for general parallel algorithms. BFS (& max-flow): much better speedups on XMT. Same easier programs
Notes: Contrast – Marines and perhaps parallel computing people are really brave. If you give them a piece of hardware, nothing will stop them. But is it wise?
Decree-- For academia, it has been. For industry, it seems to work, perhaps because competition is so limited. Isn’t it fascinating how we find ourselves in a hole and keep digging?
Lots of parallelism –This is not where the trick is.

## Slide 36: Power Efficiency
heterogeneous design  TCUs used only when beneficial
extremely lightweight TCUs. Avoid complex HW overheads: coherent caches, branch prediction, superscalar issue, or speculation. Instead TCUs compensate with much parallelism
distributed design allows easy turned off of unused TCUs
compiler and run-time system hide memory latency with computation as possible  less power in idle stall cycles
HW-supported thread scheduling is both much faster and less energy consuming than traditional software driven scheduling
same for prefix-sum based thread synchronization
custom high-bandwidth network from XMT lightweight cores to memory has been highly tuned for power efficiency
we showed that the power efficiency of the network can be further improved using asynchronous logic

## Slide 37
Back-up slide
Possible mindset behind vendors’ HW
“The hidden cost of low bandwidth communication” BMM94:
HW vendors see the cost benefit of lowering performance of interconnects, but grossly underestimate the programming difficulties and the high software development costs implied.
2. Their exclusive focus on runtime benchmarks misses critical costs, including: (i) the time to write the code, and (ii) the time to port the code to different distribution of data or to different machines that require different distribution of data.
Architects ask (e.g., me) what gadget to add?
 Sorry: I also don’t know. Most components not new. Still ‘importing airplane parts to a car’ does not yield the same benefits
   Compatibility of serial code matters more

## Slide 38: More On PRAM-On-Chip Programming
10th grader* comparing parallel programming approaches
  “I was motivated to solve all the XMT programming assignments we got, since I had to cope with solving the algorithmic problems themselves, which I enjoy doing. In contrast, I did not see the point of programming other parallel systems available to us at school, since too much of the programming was effort getting around the was the system was engineered, and this was not fun”
*From Montgomery Blair Magnet, Silver Spring, MD

## Slide 39: Independent validation by DoD employee
Nathaniel Crowell. Parallel algorithms for graph problems, May 2011. MSc scholarly paper, CS@UMD. Not part of the XMT team
http://www.cs.umd.edu/Grad/scholarlypapers/papers/NCrowell.pdf
Evaluated XMT for public domain problems of interest to DoD
Developed serial then XMT programs
Solved with minimal effort (MSc scholarly paper..) many problems. E.g., 4 SSCA2 kernels, Algebraic connectivity and Fiedler vector (Parallel Davidson Eigensolver)
Good speedups
No way where one could have done that on other parallel platforms so quickly
Reports: extra effort for producing parallel code was minimal
Notes: More like a couple of PhD theses on other platforms
Reports: NSA people told me that with GPUs, the experience has been 1 week for a working program and then ½ year for performance

## Slide 40
advanced planarity testing
advanced triconnectivity
planarity testing
triconnectivity
st-numbering
k-edge/vertex
connectivity
minimum spanning forest
Euler tours
ear decompo- sition search
bicon- nectivity
strong orientation
centroid decomposition
tree contraction
lowest common ancestors
graph connectivity
tree Euler tour
list ranking
2-ruling set
prefix-sums
deterministic coin tossing
Importance of list ranking for tree and graph algorithms
Point of recent study
Root of OofM speedups:
Speedup on various input sizes
on much simpler problems

## Slide 41: Software release
Allows to use your own computer for programming on an XMT environment & experimenting with it, including:
a) Cycle-accurate simulator of the XMT machine
b) Compiler from XMTC to that machine
Also provided, extensive material for teaching or self-studying parallelism, including
Tutorial + manual for XMTC (150 pages)
Class notes on parallel algorithms (100 pages)
Video recording of 9/15/07 HS tutorial (300 minutes)
Video recording of Spring’09 grad Parallel Algorithms lectures (30+hours)
www.umiacs.umd.edu/users/vishkin/XMT/sw-release.html,
Or just Google “XMT”
Notes: 41

## Slide 42: Helpful (?) Analogy
  Grew on tasty salads: Natural ingredients; No dressing/cheese
  Now salads requiring tones of dressing and cheese. Taste?
  Reminds (only?) me of
  Dressing Huge blue-chip & government investment in system & app software to overcome HW limitations. (limited scope) DSLs.
  Taste Speed-ups only on limited apps.
  Contrasted with:
  Simple ingredients Parallel algorithms theory. Few basic architecture ideas on control & data paths and memory system
    Modest academic project
    Taste Better speedups by orders of magnitude. HS student vs PhDs

## Slide 43: Participants
Grad students: James Edwards, Fady Ghanim Recent PhDs: Aydin Balkan, George Caragea, Mike Horak, Fuat Keceli, Alex Tzannes*, Xingzhi Wen
Industry design experts (pro-bono).
Rajeev Barua, Compiler. Co-advisor X2. NSF grant.
Gang Qu, VLSI and Power. Co-advisor.
Steve Nowick, Columbia U., Asynch logic. Co-advisor. NSF team grant.
Ron Tzur, U. Colorado, K12 Education. Co-advisor. NSF seed funding
K12: Montgomery Blair Magnet HS, MD, Thomas Jefferson HS, VA, Baltimore (inner city) Ingenuity Project Middle School 2009 Summer Camp, Montgomery County Public Schools
Marc Olano, UMBC, Computer graphics. Co-advisor.
Tali Moreshet, Swarthmore College, Power. Co-advisor.
Bernie Brooks, NIH. Co-Advisor.
Marty Peckerar, Microelectronics
Igor Smolyaninov, Electro-optics
Funding: NSF, NSA deployed XMT computer, NIH
Transferred IP for Intel/TBB-customized XMT lazy scheduling. 4’2013
Reinvention of Computing for Parallelism. 1st out of 49 for Maryland Research Center of Excellence (MRCE) by USM. None funded. 17 members, including UMBC, UMBI, UMSOM. Mostly applications.
* 1st place, ACM Student Research Competition, PACT’11. Post-doc, UIUC