## Slide 1: General-Purpose Many-Core Parallelism – Broken, But Fixable
Uzi Vishkin
Scope: max speedup from on-chip parallelism
Notes: Consider the level of application innovation in high-end general-purposes desktop computing over the last decade. I believe that it has been minimal, perhaps with the exception of computer graphics. Consider progress on internet and mobile for comparison where nearly 500,000 work developing mobile apps on their own dime.
Being motivated. Before technology constraints forced Intel to move to multi-cores, it was forced to extend X86 from 32- to 64-bit. Intel invested $4B in the Itanium and then wanted to cancel it. Was put on the right track only because competition from AMD. No correcting competition existed for over a decade. Will better conditions for competition emerge?

## Slide 2: Commodity computer systems
19462003 General-purpose computing: Serial. 5KHz4GHz.
2004 Clock frequency growth flatGeneral-purpose computing goes parallel. ’If you want your program to run significantly faster … you’re going to have to parallelize it’
19802014
#Transistors/chip: 29K10sB
Bandwidth/latency: 300
Intel Platform 2015, March05:
#”cores”: ~dy-2003
~2011: Advance from d1 to d2
Did this happen?..
Notes: Did this happen – have we even stayed on d1 ?

## Slide 3: How is many-core parallel computing doing?
Current-day system architectures allow good speedups on regular dense-matrix type programs, but are basically unable to do much outside that
What’s missing
  Irregular problems/program
  Strong scaling, and
  - Cost-effective parallel programming for regular problems
    Sweat-to-gain ratio is (often too) high
    Though some progress with domain-specific languages
Requires revolutionary approach
  Revolutionary: Throw out & replace   high bar
Notes: Students in my recent computer engineering junior class were dismayed to hear that. Nearly all (mostly serial) programs they have learned and written do not fit this mold and they felt that this was too limiting.

## Slide 4: Example Memory How did serial architectures deal with locality?
1. Gap opened between improvements in
  - Latency to memory, and
  - Processor speed
2. Locality observation Serial programs tend to reuse data, or nearby addresses 
  Increasing role for caches in architecture; yet,
  Same basic programming model
In summary
Starting point: Successful programming model
Found a way to hold on to it

## Slide 5: Locality in Parallel Computing
Early on Processors with local memory
 Practice of parallel programming meant:
  Program for parallelism, and
  Program for locality
Consistent with: design for peak performance
But, not with: cost-effective programming
In summary
Never: Truly successful parallel programming model
 Less to hold on to..

## Slide 6: Back-up: Current systems/revolutionary changes
  Multiprocessors HP-12: Computer consisting of tightly coupled processors whose coordination and usage are controlled by a single OS and that share memory through a shared address space
  GPUs HW handles thread management. But, leave open missing items
  BACKUP:
  Goal Fit as many FUs as you can into silicon. Now, use all of them all the time
  Architecture, including memory, optimized for peak performance on limited workloads, rather than sustained general-purpose performance
  Each thread is SIMD  limit on thread divergence (both sides of a branch)
  HW uses parallelism for FUs and hiding memory latency
    No: shared cache for general data, or truly all-to-all interconnection network to shared memory  Works well for plenty of “structured” parallelism
  Minimal parallelism: just to break even with serial 
  Cannot handle serial & low-parallel code. Leave open missing items: strong scaling, irregular, cost-effective regular
  Also: DARPA-HProductivityCS. Still: “Only heroic programmers can exploit the vast parallelism in today’s machines” [“GameOver”, CSTB/NAE’11]

## Slide 7
Build-first, figure-out-how-to-program later  architecture
Graphics cards
Where to start
Parallel programming: MPI, Open MP
GPUs. CUDA. GPGPU
so that
ν Dense-matrix-type
X Irregular,Cost-effective,Strong scaling
ν
Heterogeneous system
Hardware-first threads
Place holder
Past
Future?
Heterogeneous   lowering the bar: Keep what we have, but augment it.
Enabled by: increasing transistor budget, 3D VLSI & design of power

## Slide 8
Build-first, figure-out-how-to-program later  architecture
Graphics cards
How to think about parallelism? PRAM & Parallel algorithms
Parallel programming: MPI, Open MP
GPUs. CUDA. GPGPU
Concepts Theory, MTA, NYU-Ultra SB-PRAM, XMT Many-core. Quantitative validation XMT
ν Dense-matrix-type
X Irregular,Cost-effective,Strong scaling
Fine, but more important:
ν
Heterogeneous system
Hardware-first threads
Algorithms-first thread
Past
Future?
Legend: Remainder of this talk

## Slide 9: Serial Abstraction & A Parallel Counterpart
Serial abstraction: any single instruction available for execution in a serial program executes immediately – ”Immediate Serial Execution (ISE)”
Abstraction for making parallel computing simple: indefinitely many instructions, which are available for concurrent execution, execute immediately, dubbed Immediate Concurrent Execution (ICE) – same as ‘parallel algorithmic thinking (PAT)’ for PRAM
What could I do in parallel at each step assuming unlimited hardware

#
ops
..
..
time
#
ops
..
..
.
.
.
.
.
.
time
Time = Work
Work = total #ops
Time << Work
Serial Execution, Based on Serial Abstraction
Parallel Execution, Based on Parallel Abstraction
Notes: Serial--Abstracts away: different execution time for operation (memory hierarchy). Made serial programming simple. Programmers: conceptualize. HW and compilers: implement. Program: instruction to execute next (inductively)
Parallel--Step-by-step (inductive) explication of the instructions available next for concurrent execution. # processors not even mentioned. Falls back on the serial abstraction if 1 instruction/step

## Slide 10
Example of Parallel algorithm Breadth-First-Search (BFS)

## Slide 13
Parallel complexity
W = ~(|V| + |E|)
T = ~d, the number of layers
Average parallelism = ~W/T
(i) “Concurrently” as in natural BFS: only change to serial algorithm
(ii) Defies “decomposition”/”partition”
Mental effort
1. Sometimes easier than serial
2. Within common denominator of other parallel approaches. In fact, much easier

## Slide 14: Memory example (cont’d)
XMT Approach
Rationale Consider parallel version of serial algorithm
Premise Similar* locality to serial 
  1. Large shared cache on-chip
  2. High-bandwidth, low latency interconnection network
[2011 technical introduction: Using Simple Abstraction to Reinvent Computing for Parallelism, CACM, 1/2011, 75-85 http://www.umiacs.umd.edu/users/vishkin/XMT/]
3D VLSI Bigger shared cache, lower distance (latency & power for data movement) and bandwidth with TSVs (through-silicon vias)
* Parallel transitions from time t to t+1: subset of serial transitions

## Slide 15: Not just talking
Algorithms&Software
ICE/WorkDepth/PAT
Creativity ends here
PRAM
Programming & workflow
No ‘parallel programming’ course beyond freshmen
Stable compiler
IP for dynamic thread allocation  Intel TBB 4/13
PRAM-On-Chip HW Prototypes
64-core, 75MHz FPGA of XMT
(Explicit Multi-Threaded) architecture
SPAA98..CF08
128-core intercon. network IBM 90nm: 9mmX5mm, 400 MHz [HotI07]Fund
work on asynch NOCS’10
FPGA designASIC
IBM 90nm: 10mmX10mm
Scales: 1K+ cores on-chip. Power & Tech updates  cycle accurate simulator
Notes: Creativity--By nature, algorithms require some level of creativity. Ideally, programming does not.

## Slide 16: Orders-of-magnitude speedups & complexity Next slide: ease-of-programming
 | XMT | GPU/CPU | factor
Graph Biconnectivity 2012 | 33X | 4X random graphs Muuuch parallelism | >>8
Graph Triconnectivity 2012 | 129X | ? | ?
Max Flow 2011 | 108X | 2.5X | 43
Burrows Wheeler Compression Transform - bzip2 Decompression | 25X 13X | X/2.8 … on GPU ? | 70 ?
non-trivial stress tests
- 3 graph algorithms: No algorithmic creativity.
- 1st “truly parallel” speedup for lossless data compression. SPAA 2013. Beats Google Snappy (message passing within warehouse scale computers)
State of project
- 2012: quant validation of (most advanced) PRAM algorithms: ~65 man years
2013-: 1. Apps 2. Update Memory&enabling technologies/opportunities. 3. Minimize HW investment. Fit into current ecosystem (ARM,POWER,X86).

## Slide 17: Not alone in building new parallel computer prototypes in academia
At least 3 more US universities in the last 2 decades
Unique(?) daring own course-taking students to program it for performance
  - Graduate students do 6 programming assignments, including biconnectivity, in a theory course
  - Freshmen do parallel programming assignments for problem load competitive with serial course
And we went out for
  HS students: magnet and inner city schools
“XMT is an essential component of our Parallel Computing courses because it is the one place where we are able to strip away industrial accidents from the student's mind, in terms of programming necessity, and actually build creative algorithms to solve problems”—national award winning HS teacher. 6th year of teaching XMT. 81 HS students in 2013.
  HS vs PhD success stories
  And …

## Slide 18: Middle School Summer Camp Class, July’09 (20 of 22 students). Math HS Teacher D. Ellison, U. Indiana
Notes: 7 were rising 6th graders
Summer camp for children from underrepresented groups

## Slide 19: What about the missing items ?
Recap
Feasible Orders of magnitude better with different hardware.
Evidence Broad portfolio; e.g., most advanced parallel algorithms; high-school students do PhD-thesis level work
Who should care?
- DARPA Opportunity for competitors to surprise the US military and economy
Vendors
  Confluence of mobile & wall-plugged processor market creates unprecedented competition. Standard: ARM. Quad-cores and architecture techniques reached plateau. No other way to get significantly ahead.
  Smart node in the cloud helped by large local memories of other nodes
  Bring Watson irregular technologies to personal user

## Slide 20: But,
- Chicken-and-egg effect Few end-user apps use missing items (since..missing)
- My guess Under water, the “end-user application iceberg” is much larger than today’s parallel end-user applications.
Supporting evidence
  Irregular problems: many and rising. Data compression. Computer Vision. Bio-related. Sparse scientific. Sparse sensing & recovery. EDA
  “Test of the educated innocents”
    Students in last computer engineering non-elective class: nearly all serial programs we learned/wrote do not fit this regular mold
    Cannot believe that the regular mold is sufficient for more than a small minority of potential applications
    For balance Heard from a colleague: so we teach the wrong things
2013 Embedded processor vendors hear from their customers. New attitude…

## Slide 21: Can such ideas gain traction?
Naive answer: “Sure, since they are good”.
So, why not in the past?
  Wall Street companies: risk averse. Too big for startup
  Focus on fighting out GPUs (only competition)
  60+ yrs same “computing stack”  lowest common ancestor of company units for change: CEO… who can initiate it? … Turf issues

## Slide 22: My conclusion
- A time bomb that will explode sooner or later
- Will take over domination of a core area of IT. How much more?

## Slide 23: Snapshot: XMT High-level language
Cartoon Spawn creates threads; a
thread progresses at its own speed
and expires at its Join.
Synchronization: only at the Joins. So,
virtual threads avoid busy-waits by
expiring. New: Independence of order
semantics (IOS)
The array compaction (artificial) problem
Input: Array A[1..n] of elements.
Map in some order all A(i) not equal 0 to array D.
1
0
5
0
0
0
4
0
0
1
4
5
e0
e2
e6
A
D
For program below:
e$ local to thread $;
x is 3

## Slide 24: XMT-C
Single-program multiple-data (SPMD) extension of standard C.
Includes Spawn and PS - a multi-operand instruction.
Essence of an XMT-C program
int x = 0;
Spawn(0, n-1) /* Spawn n threads; $ ranges 0 to n − 1 */
{ int e = 1;
if (A[$] not-equal 0)
{ PS(x,e);
D[e] = A[$] }
}
n = x;
Notes: (i) PS is defined next (think F&A). See results for
e0,e2, e6 and x. (ii) Join instructions are implicit.

## Slide 25: XMT Assembly Language
Standard assembly language, plus 3 new instructions: Spawn, Join, and PS.
The PS multi-operand instruction
New kind of instruction: Prefix-sum (PS).
Individual PS, PS Ri Rj, has an inseparable (“atomic”) outcome:
Store Ri + Rj in Ri, and
(ii) Store original value of Ri in Rj.
Several successive PS instructions define a multiple-PS instruction. E.g., the
sequence of k instructions:
PS R1 R2; PS R1 R3; ...; PS R1 R(k + 1)
performs the prefix-sum of base R1 elements R2,R3, ...,R(k + 1) to get:
R2 = R1; R3 = R1 + R2; ...; R(k + 1) = R1 + ... + Rk; R1 = R1 + ... + R(k + 1).
Idea: (i) Several ind. PS’s can be combined into one multi-operand instruction.
(ii) Executed by a new multi-operand PS functional unit. Enhanced Fetch&Add.
Story: 1500 cars enter a gas station with 1000 pumps. Main XMT patent: Direct in unit time a car to a EVERY pump; PS patent: Then, direct in unit time a car to EVERY pump becoming available

## Slide 26: Programmer’s Model as Workflow
Arbitrary CRCW Work-depth algorithm.
- Reason about correctness & complexity in synchronous PRAM-like model
SPMD reduced synchrony
  Main construct: spawn-join block. Can start any number of processes at once. Threads advance at own speed, not lockstep
  Prefix-sum (ps). Independence of order semantics (IOS) – matches Arbitrary CW. For locality: assembly language threads are not-too-short
  Establish correctness & complexity by relating to WD analyses
  Circumvents: (i) decomposition-inventive; (ii) “the problem with threads”, e.g., [Lee]. Issue addressed in a PhD thesis nesting of spawns
Tune (compiler or expert programmer): (i) Length of sequence of round trips to memory, (ii) QRQW, (iii) WD. [VCL07]
  - Correctness & complexity by relating to prior analyses
spawn
join
spawn
join
Notes: Prefix-sum is the well-known fetch-and-add/increment commutative ‘atomic operation’, introduced by the NYU-Ultracomputer project in the early 1980s.
Our only innovation there is in a more efficient direct HW implementation

## Slide 27: XMT Architecture Overview
BestInClass serial core – master thread control unit (MTCU)
Parallel cores (TCUs) grouped in clusters
Global memory space evenly partitioned in cache banks using hashing
No local caches at TCU. Avoids expensive cache coherence hardware
HW-supported run-time load-balancing of concurrent threads over processors. Low thread creation overhead. (Extend classic stored-program+program counter; cited by 40 patents; Prefix-sum to registers & to memory. )
Cluster 1
Cluster 2
Cluster C
DRAM Channel 1
DRAM Channel D
MTCU
Hardware Scheduler/Prefix-Sum Unit
Parallel Interconnection Network
Memory Bank 1
Memory Bank 2
Memory Bank M
Shared Memory
(L1 Cache)
…
- Enough interconnection network
bandwidth
Notes: Back-up slide: XMT Block Diagram –

## Slide 28: Backup - Holistic design
Lead question How to build and program general-purpose many-core processors for single task completion time?
Carefully design a highly-parallel platform ~Top-down objectives:
High PRAM-like abstraction level. ‘Synchronous’.
Easy coding Isolate creativity to parallel algorithms
Not falling behind on any type & amount of parallelism
Backwards compatibility on serial
Have HW operate near its full intrinsic capacity
Reduced-synchrony & no busy-waits; to accommodate varied memory response time
Low overhead start & load balancing of fine-grained threads
High all-to-all processors/memory bandwidth. Parallel memories
Notes: Easy code--
See next slide for my inspiration on how to operate near full intrinsic capacity
Tensions: Synchronous for higher abstraction, reduced synchrony & no-busy-waits for physical reality

## Slide 29: Backup- How?
The contractor’s algorithm
1. Many job sites: Place a ladder in every LR 
2. Make progress as your capacity allows
System principle 1st/2nd order PoR/LoR
PoR: Predictability of reference
LoR: Locality of reference
Presentation challenge
Vertical platform. Each level: lifetime career
Strategy Snapshots. Limitation Not as satisfactory
Notes: Place a ladder:
Each processor represents a job site: issues instructions and when the working material arrives can fire-up the functional-units (laborers).
Inspired by a contractor at home. He perfected this so well that we needed to replace him in order get back our life

## Slide 30
The classic SW-HW bridge, GvN47
Program-counter & stored program
XMT: upgrade for parallel abstraction
Virtual over physical:
distributed solution
H. Goldstine, J. von Neumann.
Planning and coding problems for an
electronic computing instrument, 1947
Notes: GvN47

## Slide 31: Revisit of “how to gain traction”
Ideal for commercialization: add “HW hooks” to current CPU IP
Next best thing:
  Reuse as much as possible
  Benefit from ecosystem of ISA

## Slide 32: Workflow from parallel algorithms to programming versus trial-and-error
Option 1
PAT
Rethink algorithm: Take better advantage of cache
Hardware
PAT
Tune
Hardware
Option 2
Parallel algorithmic thinking (say PRAM)
Compiler
Is Option 1 good enough for the parallel programmer’s model?
Options 1B and 2 start with a PRAM algorithm, but not option 1A.
Options 1A and 2 represent workflow, but not option 1B.
Not possible in the 1990s.
Possible now.
Why settle for less?
Insufficient inter-thread bandwidth?
Domain decomposition,
or task decomposition
Program
Program
Prove
correctness
Still correct
Still correct
Legend creativity hyper-creativity [More creativity  less productivity]
Sisyphean(?)
loop

## Slide 33: Who should produce the parallel code?
Choices [state-of-the-art compiler research perspective]
Programmer only
  Writing parallel code is tedious.
  Good at ‘seeing parallelism’, esp. irregular parallelism.
  But are bad at seeing locality and granularity considerations.
    Have poor intuitions about compiler transformations.
Compiler only
  Can see regular parallelism, but not irregular parallelism.
  Great at doing compiler transformations to improve parallelism, granularity and locality.
 Hybrid solution: Programmer specifies high-level parallelism, but little else. Compiler does the rest.
Goals:
Ease of programming
  Declarative programming
(My) Broader questions
Where will the algorithms come from?
Is today’s HW good enough?
XMT relevant for all 3 questions
Thanks: Prof. Barua
Notes: For question on algorithm: obvious.
For question on compilers: see Prof. Barua’s comments. XMT is all about ‘seeing parallelism’.
For HW: stay tuned. Hint: engineering (not computer engineering…) typically goes from specs to building.

## Slide 34: Denial Example: BFS [EduPar2011]
2011 NSF/IEEE-TCPP curriculum teach BFS using OpenMP
Teaching experiment Joint F2010 UIUC/UMD class. 42 students
Good news Easy coding (since no meaningful ‘decomposition’)
Bad news None got speedup over serial on 8-proc SMP machine
BFS alg was easy but .. no good: no speedups
Speedups on 64-processor XMT 7x to 25x
Hey, unfair! Hold on: <1/4 of the silicon area of SMP
Symptom of the bigger “denial”
‘Only problem Developers lack parallel programming skills’
Solution Education. False Teach then see that HW is the problem
HotPAR10 performance results include BFS:
XMT/GPU Speed-up same silicon area, highly parallel input: 5.4X
Small HW configuration, large diameter: 109X wrt same GPU
Notes: Unfair since 64 processors are compared to 8

## Slide 35: Discussion of BFS results
Contrast with smartest people: PPoPP’12, Stanford’11 .. BFS on multi-cores, again only if the diameter is small, improving on SC’10 IBM/GaTech & 6 recent papers, all 1st rate conferences
BFS is bread & butter. Call the Marines each time you need
bread? Makes one wonder Is something wrong with the field?
‘Decree’ Random graphs = ‘reality’. In the old days: Expander graphs taught in graph design. Planar graphs were real
Lots of parallelism  more HW design freedom. E.g., GPUs get decent speedup with lots of parallelism, and
But, not enough for general parallel algorithms. BFS (& max-flow): much better speedups on XMT. Same easier programs
Notes: Contrast – Marines and perhaps parallel computing people are really brave. If you give them a piece of hardware, nothing will stop them. But is it wise?
Decree-- For academia, it has been. For industry, it seems to work, perhaps because competition is so limited. Isn’t it fascinating how we find ourselves in a hole and keep digging?
Lots of parallelism –This is not where the trick is.

## Slide 36: Power Efficiency
heterogeneous design  TCUs used only when beneficial
extremely lightweight TCUs. Avoid complex HW overheads: coherent caches, branch prediction, superscalar issue, or speculation. Instead TCUs compensate with much parallelism
distributed design allows easy turned off of unused TCUs
compiler and run-time system hide memory latency with computation as possible  less power in idle stall cycles
HW-supported thread scheduling is both much faster and less energy consuming than traditional software driven scheduling
same for prefix-sum based thread synchronization
custom high-bandwidth network from XMT lightweight cores to memory has been highly tuned for power efficiency
we showed that the power efficiency of the network can be further improved using asynchronous logic

## Slide 37
Back-up slide
Possible mindset behind vendors’ HW
“The hidden cost of low bandwidth communication” BMM94:
HW vendors see the cost benefit of lowering performance of interconnects, but grossly underestimate the programming difficulties and the high software development costs implied.
2. Their exclusive focus on runtime benchmarks misses critical costs, including: (i) the time to write the code, and (ii) the time to port the code to different distribution of data or to different machines that require different distribution of data.
Architects ask (e.g., me) what gadget to add?
 Sorry: I also don’t know. Most components not new. Still ‘importing airplane parts to a car’ does not yield the same benefits
   Compatibility of serial code matters more

## Slide 38: More On PRAM-On-Chip Programming
10th grader* comparing parallel programming approaches
  “I was motivated to solve all the XMT programming assignments we got, since I had to cope with solving the algorithmic problems themselves, which I enjoy doing. In contrast, I did not see the point of programming other parallel systems available to us at school, since too much of the programming was effort getting around the was the system was engineered, and this was not fun”
*From Montgomery Blair Magnet, Silver Spring, MD

## Slide 39: Independent validation by DoD employee
Nathaniel Crowell. Parallel algorithms for graph problems, May 2011. MSc scholarly paper, CS@UMD. Not part of the XMT team
http://www.cs.umd.edu/Grad/scholarlypapers/papers/NCrowell.pdf
Evaluated XMT for public domain problems of interest to DoD
Developed serial then XMT programs
Solved with minimal effort (MSc scholarly paper..) many problems. E.g., 4 SSCA2 kernels, Algebraic connectivity and Fiedler vector (Parallel Davidson Eigensolver)
Good speedups
No way where one could have done that on other parallel platforms so quickly
Reports: extra effort for producing parallel code was minimal
Notes: More like a couple of PhD theses on other platforms
Reports: NSA people told me that with GPUs, the experience has been 1 week for a working program and then ½ year for performance

## Slide 40
advanced planarity testing
advanced triconnectivity
planarity testing
triconnectivity
st-numbering
k-edge/vertex
connectivity
minimum spanning forest
Euler tours
ear decompo- sition search
bicon- nectivity
strong orientation
centroid decomposition
tree contraction
lowest common ancestors
graph connectivity
tree Euler tour
list ranking
2-ruling set
prefix-sums
deterministic coin tossing
Importance of list ranking for tree and graph algorithms
Point of recent study
Root of OofM speedups:
Speedup on various input sizes
on much simpler problems

## Slide 41: Software release
Allows to use your own computer for programming on an XMT environment & experimenting with it, including:
a) Cycle-accurate simulator of the XMT machine
b) Compiler from XMTC to that machine
Also provided, extensive material for teaching or self-studying parallelism, including
Tutorial + manual for XMTC (150 pages)
Class notes on parallel algorithms (100 pages)
Video recording of 9/15/07 HS tutorial (300 minutes)
Video recording of Spring’09 grad Parallel Algorithms lectures (30+hours)
www.umiacs.umd.edu/users/vishkin/XMT/sw-release.html,
Or just Google “XMT”
Notes: 41

## Slide 42: Helpful (?) Analogy
  Grew on tasty salads: Natural ingredients; No dressing/cheese
  Now salads requiring tones of dressing and cheese. Taste?
  Reminds (only?) me of
  Dressing Huge blue-chip & government investment in system & app software to overcome HW limitations. (limited scope) DSLs.
  Taste Speed-ups only on limited apps.
  Contrasted with:
  Simple ingredients Parallel algorithms theory. Few basic architecture ideas on control & data paths and memory system
    Modest academic project
    Taste Better speedups by orders of magnitude. HS student vs PhDs

## Slide 43: Participants
Grad students: James Edwards, Fady Ghanim Recent PhDs: Aydin Balkan, George Caragea, Mike Horak, Fuat Keceli, Alex Tzannes*, Xingzhi Wen
Industry design experts (pro-bono).
Rajeev Barua, Compiler. Co-advisor X2. NSF grant.
Gang Qu, VLSI and Power. Co-advisor.
Steve Nowick, Columbia U., Asynch logic. Co-advisor. NSF team grant.
Ron Tzur, U. Colorado, K12 Education. Co-advisor. NSF seed funding
K12: Montgomery Blair Magnet HS, MD, Thomas Jefferson HS, VA, Baltimore (inner city) Ingenuity Project Middle School 2009 Summer Camp, Montgomery County Public Schools
Marc Olano, UMBC, Computer graphics. Co-advisor.
Tali Moreshet, Swarthmore College, Power. Co-advisor.
Bernie Brooks, NIH. Co-Advisor.
Marty Peckerar, Microelectronics
Igor Smolyaninov, Electro-optics
Funding: NSF, NSA deployed XMT computer, NIH
Transferred IP for Intel/TBB-customized XMT lazy scheduling. 4’2013
Reinvention of Computing for Parallelism. 1st out of 49 for Maryland Research Center of Excellence (MRCE) by USM. None funded. 17 members, including UMBC, UMBI, UMSOM. Mostly applications.
* 1st place, ACM Student Research Competition, PACT’11. Post-doc, UIUC

## Slide 44: Mixed bag of incentives
Vendor loyalists
In past decade, diminished competition among vendors. The recent “GPU chase/race” demonstrates power of competition. Now back with a vengeance: 3rd and 4th in mobile dropped out in 2012
What’s in it for researchers who are not generalists? and how many HW/SW/algorithm/app generalists you know?
Zero-sum with other research interests; e.g., spin (?) of Game Over report into supporting power over missing items

## Slide 45: Algorithms dart Parallel Random-Access Machine/Model
PRAM:
n synchronous processors all having unit time access to a shared memory.
Basis for Parallel PRAM algorithmic theory
- 2nd in magnitude only to serial algorithmic theory
- Simpler than above. See later
- Won the “battle of ideas” in the 1980s. Repeatedly:
Challenged without success  no real alternative!
Today: Latent, though not widespread, knowledgebase
Drawing a target?
State-of-the-art 1993 LogP well-cited paper: unrealistic for implementation
Why high bandwidth hard for 1993 technology
Low bandwidth  PRAM lower bounds [VW85,MNV94]  real conflict
Notes: Mention Arbitrary CRCW PRAM

## Slide 46: Reward game is skewed gives (illusion of) job security
You might wonder: why if we have such a great architecture, don’t we have many more single-application papers?
Easier to publish on “hard-to-program” platforms
  Remember STI Cell? ‘Vendor-backed is robust’: remember Itanium?
Application papers for easy-to-program architectures are considered “boring”
  Even when they show good results
Recipe for academic publication and promotions
  Take simple application (e.g. Breadth-First Search in graph)
  Implement it on latest difficult-to-program vendor-backed parallel architecture
  Discuss challenges and workarounds to establish intellectual merit
  Stand out of the crowd for industry impact
Job security Architecture sure to be replaced (difficult to program ..)
Notes: Illusion because market place is sure to reject parallelism in the mainstream, making everybody a loser
Stand out: deans love the industry brand-name and the citation count among all those doing the same thing

## Slide 47: General-purpose parallel computing for speeding up single task
Current commercial systems not robust
- SW spiral broken
Look like industrial accidents
Did not emerge from a clean-slate design
Order-of-magnitude behind* on ease-of-programming Unnecessary burden on programmers. Possibly inventive:
- decomposition
- assignment
- orchestration
- mapping
- reasoning about concurrency (race conditions)
- (for GPUs) making the whole program highly parallel
OofM behind* on speedups for irregular apps
No compact/rigorous induction-like way to reason
Notes: SW spiral broken—no current contract between programmers and architects
* Behind what’s feasible. Next slide

## Slide 48: Is it feasible to rewrite the serial book for parallel?
XMT: Yes! 1-1 match to serial stack
Clean slate design
Theory of parallel algorithm. Couple induction with simple parallel abstraction.
Parallel SPPC
Validation
- Architecture, compiler, run-time
- OofM ahead on ease-of-programming and speedups. Including: most advanced algorithmic problems

## Slide 49
Example: The list ranking problem
Parallel pointer jumping
ICE pseudocode
for 1 <= i <= n pardo
while S(i) != S(S(i)) do
W(i) := W(i) + W(S(i))
S(i) := S(S(i))
end while
end for
Note
- Tight synchrony
- Reads before writes
Complexity O(log n) time, O(n log n) work. Serial: Time = Work = O(n)
Unusual Much (~n) parallelism. Often far less
Notes: People stand in a very long line to the movies. Everyone sees only the back of the person in front. Where are you in the line? or is the line just going around the block .. and there is no movie?

## Slide 50
psBaseReg flag; // number of threads that require another loop iteration
void pointer_jump(int S[n], int W[n], int n) {
int W_temp[n]; int S_temp[n];
do {
spawn(0, n-1) {
if (S[$] != S[S[$]]) {
W_temp[$] = W[$] + W[S[$]]; S_temp[$] = S[S[$]];}
else {W_temp[$] = W[$];S_temp[$] = S[$];}
}
flag = 0;
spawn(0, n-1) {
if (S_temp[$] != S_temp[S_temp[$]]) {
int i = 1;
ps(i, flag);
W[$] = W_temp[$] + W_temp[S_temp[$]];
S[$] = S_temp[S_temp[$]];}
else {W[$] = W_temp[$]; S[$] = S_temp[$];}
}
} while (flag != 0);
}
XMTC program

## Slide 51: Speedup for List Ranking (vs. Best Serial)
Chart: 1024-TCU XMT vs. Intel Core i7 920
| 1000 | 3200 | 10000 | 32000 | 100000 | 320000 | 1000000 | 3200000 | 10000000
jump-bsplit | 0.176 | 0.54191 | 0.59905 | 0.74751 | 1.2119 | 1.6601 | 3.4576 | 5.628 | 6.3826
jump-HW | 6.0347 | 7.6325 | 8.1836 | 10.7153 | 17.9714 | 14.6971 | 8.6061 | 10.4438 | 10.8604
cointoss-bsplit | 0.23166 | 0.27487 | 0.48997 | 1.1658 | 3.3201 | 6.7268 | 16.5653 | 29.3702 | 35.854
cointoss-HW | 1.3755 | 2.1817 | 3.7367 | 8.8344 | 27.861 | 31.0131 | 40.2613 | 56.5306 | 61.6363
hybrid-bsplit | 0.17557 | 0.54239 | 0.60829 | 1.4285 | 3.6941 | 6.8599 | 16.6285 | 29.6351 | 35.9535
hybrid-HW | 5.9667 | 7.6123 | 8.226 | 14.3069 | 36.5029 | 33.0712 | 40.717 | 56.6791 | 61.7158
List size (x 1,000) | jump |  | cointoss |  | hybrid | 
 | bsplit | HW | bsplit | HW | bsplit | HW
1 | 0.18 | 6.03 | 0.23 | 1.38 | 0.18 | 5.97
3.2 | 0.54 | 7.63 | 0.27 | 2.18 | 0.54 | 7.61
10 | 0.60 | 8.18 | 0.49 | 3.74 | 0.61 | 8.23
32 | 0.75 | 10.72 | 1.17 | 8.83 | 1.43 | 14.31
100 | 1.21 | 17.97 | 3.32 | 27.86 | 3.69 | 36.50
320 | 1.66 | 14.70 | 6.73 | 31.01 | 6.86 | 33.07
1,000 | 3.46 | 8.61 | 16.57 | 40.26 | 16.63 | 40.72
3,200 | 5.63 | 10.44 | 29.37 | 56.53 | 29.64 | 56.68
10,000 | 6.38 | 10.86 | 35.85 | 61.64 | 35.95 | 61.72
Algorithms
cointoss: coin tossing
jump: pointer jumping
hybrid: cointoss until the list size is below some threshold, then jump (accelerating cascades)
Spawn types
bsplit: binary splitting
HW: XMT hardware thread initiation
Focus XMT feature Low overhead initiation of all TCUs
HW (with feature) versus bsplit (without feature). Both within XMT

Note (for later)
 Compare speedups for input = 1000s
Notes: Note: best speedups >= 60X vs > 30X without feature (or on GPUs – next slide).
However, for parallelism in the few 1000s, the XMT speedups are ~8X, while all other platforms give none!
Unique: in other systems you will find either ‘low overhead initiation of fine-grained threads’ (GPUs) or support for serial & limited parallelism. Not both.

## Slide 52: Comparison with Prior Work on List Ranking
Bader et al. 2005
  Speedups <= 3x on a Sun E4500 SMP (using 8 processors)
  Speedups <= 6x on a Cray MTA-2 (using 8 processors, or 1024 HW streams as in 1024-TCU XMT)
  Speedups are relative to the same parallel algorithm running on a single processor on the same machine (list size = 80 million)
  No comparison with the best sequential algorithm
Rehman et al. 2009
  Speedups <=34x in cycle count (18x wall clock time) on NVIDIA GTX 280 GPU (list size 4M) over best sequential algorithm on Intel Core 2 Quad Q6600 vs <= 62X for 10M (57X for 4M) on XMT
  Pointer jumping for 4K: no speedup on GPU vs 8X for XMT
  MAIN POINT Limited number (e.g., 4K) of very short threads  order-of-magnitude advantage to XMT over all others
D. Bader, G. Cong, and J. Feo. On the architectural requirements for efficient execution of graph algorithms. In Proc. Int’l Conf. on Parallel Processing (ICPP), pp. 547-556, June 2005.
M. S. Rehman, K. Kothapalli, and P. J. Narayanan. Fast and Scalable List Ranking on the GPU. In Int’l Conf. on Supercomputing (ICS), pp. 235-243, June 2009.
Notes: Recall comment on GPU productivity problems if whole program is not highly parallel.
I claimed that it affects productivity as upgrading a serial program requires major overhaul for parallelism of the whole program.
You may say: but, list ranking has enough parallelism for interesting input sizes.
Not so! Often, list ranking routines occur with limited input sizes for interesting problems…

## Slide 53
Biconnectivity Speedups [EdwardsV]: 9X to 33X relative to up to best result of up to 4X [Cong-Bader] over 12-processor SMP. No GPU results.
Int’l Workshop on Programming Models and Applications for Multicores and Manycores, to appear in Proc. PPoPP’12, Feb 25-29, 2012
Biconnectivity speedups were particularly challenging since DFS-based serial algorithms is very compact; however:
Stronger speedups for triconnectivity: submitted. Unaware of prior parallel results.
Ease-of-programming
Normal algorithm-to-programming (of [TarjanV]) versus creative and complex program
Most advanced algorithm in parallel algorithms textbooks
Spring’12 class: programming HW assignment!

## Slide 54: “The U.S. Is Busy Building Supercomputers, but Needs Someone to Run Them”*, 12/2011
‘Low-end’ supercomputers $1-10M/unit
Supercomputing leaders Not enough programmers
Comments 1. Fewer (total) programmers than many-cores
2. Prog. models of many-cores too similar to expect a difference
3. IMO denial. Just a symptom. The problem is the HW
Opportunity Space
<~1TB main memory. If 1000-core HW, order-of-magnitude:
Lower Cost (~$10K/unit),
Easier programming
Greater speedups (performance)
Could LANL be interested?
* http://www.thedailybeast.com/articles/2011/12/28/the-u-s-is-busy-building-supercomputers-but-needs-someone-to-run-them.html
Notes: Example Story mentions genomics research, as a key application. Does LANL care for this application?

## Slide 55
Unchallenged in a Fall’11 DC event ‘what a wonderful dynamic field. 10 yrs ago DEC&Sun were great companies, now gone’; Apple, IBM, Motorola also out of high-end commodity processors.
Oh dear, compare this cheerfulness with:
“The Trouble with Multicore: Chipmakers are busy designing microprocessors that most programmers can't handle”—D. Patterson, IEEE Spectrum 7/2010
Only heroic programmers can exploit the vast parallelism in current machines – The Future of Computing: Game over or Next level, National Research Council, 2011
Ask yourself Dynamic OR consolidation and diminished competition? Satisfied with recent yrs innovation in high-end commodity apps?
Next How did we get to this point, and how to get out?
Notes: Unchallenged – Vendors appear not to have a clue how to solve the 40 yrs old problem of building easy-to-program parallel machines. Lacking (and despairing of) a technical solution, their business strategy should be torn between preempting: (i) public perception of uncertainty; and (ii) drive researchers to give industry the solution it needs. The former may be fine for a vendor, but it puts the rest of us to sleep, and comes at the expense of the economy and the profession.
IMO, some of the same speakers also implied the opposite elsewhere; e.g., lower on this slide..
Consolidation – ‘winner takes all’ and the implied higher barrier to entry that follows – cited as a problem for getting the US out of today’s recession
How can one establish that many more apps would have been invented with easier to program platforms?

## Slide 56
Is it an industrial disease if so many in academia, industry, and Wall Street see black as white?
If yes, consider
Publicity is justly commended as a remedy for social and industrial diseases. Sunlight is said to be the best of disinfectants; electric light the most efficient policeman—Louis D. Brandeis
BTW, IMO vendors will be happy if shown the way. But: 1. people say what they think that vendors want to hear; 2. vendors cannot protest against compliments to their own products
Notes: BTW – When you get a compliment you typically don’t ask the other party if they forgot to take their pills today…

## Slide 57
What if we keep digging (around HW dart)
Example: how to attract students? Starts par prog course with a parallel version of basic matrix multiply or tile-based one? The latter: Deliver 1st par prog trauma ASAP: Shock and awe  Okay to teach later, but .. how many tiles to fit 1000X1000 matrices in cache of modern PC?
A sociology of science angle
Ludwik Fleck, 1935 (the Turing of sociology of science):
Research too esoteric to be reliable  exoteric validation
Exoteric validation: exactly what general programmers could have provided, but … they have not!
Next Why vendors’ approach cannot work (and rejection by programmers is all but certain)
Notes: Polish Israeli researcher. The most prestigious award in sociology of science named after him. Much of the 1960s book Structure of Scientific Revolutions (Thomas Kuhn’s ‘paradigm shift’ ) was based on this 1935 work.

## Slide 58: “Application dreamer” between a rock and a hard place Permeated the following working assumption Programming models for larger-scale & mainstream systems – similar  importing ills of parallel computing to mainstream
Optimized for things you can “truly measure”: (old) benchmarks & power.
What about productivity?
Low priority at best  Denial .. in other words
Decomposition-inventive design **creativity**
 Reason about concurrency in threads **complexity**
For some parallel HW: issues if whole program is not highly parallel. Will highlight
Even if it is: **too much work**
[Credit: wordpress.com]
What if keep digging 2
Programmer’s productivity busters Many-core HW
Notes: Will highlight – case of GPUs

## Slide 59
Casualties of too-costly SW development
Cost and time-to-market of applications
Business model for innovation (& American ingenuity)
Advantage to lower wage CS job markets
Mission of research enterprises. PhD theses (bioinformatics): program around the engineering of parallel machines. Not robust contributions: new algorithms or modeling app domain.
NSF HS plan: attract best US minds with less programming, 10K CS teachers
.. Only future of the field & U.S. (and ‘US-like’) competitiveness
Still HW vendor ‘11: ‘Okay, you do have a convenient way to do parallel programming; so what’s the big deal?’ or ‘this is SW not HW’
Notes: Cost -- Example: Suppose that DoD spends $100M/year on developing high-end source code for commodity desktops. Suppose that this cost can be cut by a factor of 10. Imagine: (i) what else you could with the same code development budget and/or (ii) just with the money.
Will it make sense to invest $10M to save $100M/year in this example?
Mission—yet will not support a new architecture, only burn money on architectures that waste time of researchers/programmers

## Slide 60: Threats to validity of current power modeling
System 1 5 days correct code +1d performance
System 2 5 days correct code +1/2 year (125d) performance
How would you compare total power?
Power to develop app
Power to use app
Would the applications be the same?
If System 1 promotes more use (more apps, more programmers), is it really bad?
Notes: If System 2 perhaps we should go to back to farming
If we go to an extreme, is a cemetery (no power consumption) the ideal?
Is this a religious/political/ideological issue, or is it a serious debate?
If the latter, where are the economists/business perspective?

## Slide 61: But, what is the performance penalty for easy programming? Surprise benefit! vs. GPU [HotPar10]
1024-TCU XMT simulations vs. code by others for GTX280. < 1 is slowdown. Sought: similar silicon area & same clock.
Postscript regarding BFS
59X if average parallelism is 20
109X if XMT is … downscaled to 64 TCUs

## Slide 62: Problem acronyms
BFS: Breadth-first search on graphs
Bprop: Back propagation machine learning alg.
Conv: Image convolution kernel with separable filter
Msort: Merge-sort algorith
NW: Needleman-Wunsch sequence alignment
Reduct: Parallel reduction (sum)
Spmv: Sparse matrix-vector multiplication

## Slide 63: Backup slides
Many forget that the only reason that PRAM algorithms did not become standard CS knowledge is that there was no demonstration of an implementable computer architecture that allowed programmers to look at a computer like a PRAM. XMT changed that, and now we should let Mark Twain complete the job.
We should be careful to get out of an experience only the wisdom that is in it— and stop there; lest we be like the cat that sits down on a hot stove-lid. She will never sit down on a hot stove-lid again— and that is well; but also she will never sit down on a cold one anymore.— Mark Twain

## Slide 64: Lessons from Invention of Computing
H. Goldstine, J. von Neumann. Planning and coding problems for an electronic computing instrument, 1947: “.. in comparing codes 4 viewpoints must be kept in mind, all of them of comparable importance:
Simplicity and reliability of the engineering solutions required by the code
Simplicity, compactness and completeness of the code
Ease and speed of the human procedure of translating mathematical conceived methods into the code, and also of finding and correcting errors in coding or of applying to it changes that have been decided upon at a later stage
Efficiency of the code in operating the machine near its full intrinsic speed
Take home
Legend features that fail the “truly measure” test
In today’s language programmer’s productivity
Birth (?) of CS: Translation into code of non-specific methods
.. how to match that for parallelism

## Slide 65: How does XMT address BSP (bulk-synchronous parallelism) concerns?
XMTC programming incorporates programming for
locality & reduced synchrony
as 2nd order considerations
On-chip interconnection network: high bandwidth
Memory architecture: low latencies
1st comment on ease-of-programming
I was motivated to solve all the XMT programming assignments we got, since I had to cope with solving the algorithmic problems themselves which I enjoy doing. In contrast, I did not see the point of programming other parallel systems available to us at school, since too much of the programming was effort getting around the way the systems were engineered, and this was not fun.
Jacob Hurwitz, 10th grader, Montgomery Blair High School Magnet Program, Silver Spring, Maryland, December 2007.
Among those who did all graduate course programming assignments.

## Slide 66: XMT (Explicit Multi-Threading): A PRAM-On-Chip Vision
IF you could program a current manycore  great speedups. XMT: Fix the IF
XMT was designed from the ground up with the following features:
Allows a programmer’s workflow, whose first step is algorithm design for work-depth. Thereby, harness the whole PRAM theory
No need to program for locality beyond use of local thread variables, post work-depth
Hardware-supported dynamic allocation of “virtual threads” to processors.
Sufficient interconnection network bandwidth
Gracefully moving between serial & parallel execution (no off-loading)
Backwards compatibility on serial code
Support irregular, fine-grained algorithms (unique). Some role for hashing.
Tested HW & SW prototypes
Software release of full XMT environment
SPAA’09: ~10X relative to Intel Core 2 Duo

## Slide 67: Movement of data – back of the thermal envelope argument
4X: GPU result over XMT for convolution
Say total data movement as GPU but in ¼ time
Power (Watt) is energy/time  PowerXMT~¼ PowerGPU
Later slides: 3.7 PowerXMT~PowerGPU
Finally,
No other XMT algorithms moves data at higher rate
Scope of comment single chip architectures

## Slide 68
Basic Algorithm (sometimes informal)
Serial program (C)
Add data-structures (for serial algorithm)
Decomposition
Assignment
Orchestration
Mapping
Add parallel data-structures
(for PRAM-like algorithm)
Parallel
Programming
(Culler-Singh)
Parallel program (XMT-C)
XMT Computer
(or Simulator)
Parallel computer
Standard Computer
3
1
2
4
4 easier than 2
Problems with 3
4 competitive with 1: cost-effectiveness; natural
PERFORMANCE PROGRAMMING & ITS PRODUCTIVITY
Low overheads!

## Slide 69
Serial program (C)
Decomposition
Assignment
Orchestration
Mapping
Parallel
Programming
(Culler-Singh)
Parallel program (XMT-C)
XMT architecture
(Simulator)
Parallel computer
Standard Computer
Application programmer’s interfaces (APIs)
(OpenGL, VHDL/Verilog, Matlab)
compiler
Automatic?
Yes
Yes
Maybe
APPLICATION PROGRAMMING & ITS PRODUCTIVITY

## Slide 70
XMT Block Diagram – Back-up slide

## Slide 71: ISA
Any serial (MIPS, X86). MIPS R3000.
Spawn (cannot be nested)
Join
SSpawn (can be nested)
PS
PSM
Instructions for (compiler) optimizations

## Slide 72: The Memory Wall
Concerns: 1) latency to main memory, 2) bandwidth to main memory.
Position papers: “the memory wall” (Wulf), “its the memory, stupid!” (Sites)
Note: (i) Larger on chip caches are possible; for serial computing, return on using them: diminishing. (ii) Few cache misses can overlap (in time) in serial computing; so: even the limited bandwidth to memory is underused.
XMT does better on both accounts:
• uses more the high bandwidth to cache.
• hides latency, by overlapping cache misses; uses more bandwidth to main memory, by generating concurrent memory requests; however, use of the cache alleviates penalty from overuse.
Conclusion: using PRAM parallelism coupled with IOS, XMT reduces the effect of cache stalls.

## Slide 73: State-of-the-art
Unsatisfactory products
Diminished competition among vendors
No funding for really new architecture
Today’s academics Limited to the best he/she can derive from vendor products (trained and rewarded)
Missing Profound questioning of products
Absurdity Industry expects from its people to: (i) look for guidance to improve products; e.g., from academia (ii) present a brave posture to the world regarding the same products; in turn, lead academia/funding not to develop answers to (i)

## Slide 74: Problem: Develop a Technology
Definition Technology: capability given by the practical application of knowledge
how to build and program parallel machines parallel algorithmic thinking
The rest of this talk
Snapshots of the technology
Order of magnitude advantages on ease-of-programming and speedups
Challenges

## Slide 75: Somewhere: Explanation for current reality
Recall Technology: capability given by the practical application of knowledge
XMT: build and program parallel machines parallel algorithmic thinking
VERY few teach both algorithms AND architecture
Theorists stop at creating knowledge
Nearly impossible for young architects to develop a platform (Exception: UT TRIPS. Now: Microsoft, NVidia)
Diminished competition in architecture
(Unintended) Research reward system: conform or perish
No room for questioning vendors’
Every society honors its live conformists and its dead troublemakers—McLaughlin

## Slide 76: Are we really trying to ensure that many-cores are not rejected by programmers?
Einstein’s observation A perfection of means, and confusion of aims, seems to be our main problem
Conformity incentives are for perfecting means
Consider a vendor-backed flawed system. Wonderful opportunity for our originality-seeking publications culture:
* The simplest problem requires creativity  More papers
* Cite one another if on similar systems maximize citations
and claim ‘industry impact’
Ultimate job security – By the time the ink dries on these papers, next flawed ‘modern’ ‘state-of-the-art’ system. Culture of short-term impact
Unchallenged in a power DC meeting – ‘what a wonderful dynamic field. 10 yrs ago DEC&Sun were great companies, now gone’; dynamic? or diminished competition?

## Slide 77: Parallel Programming Today
Current Parallel Programming
High-friction navigation - by implementation [walk/crawl]
Initial program (1week) begins trial & error tuning (½ year; architecture dependent)
PRAM-On-Chip Programming
Low-friction navigation – mental design and analysis [fly]
Once constant-factors-minded algorithm is set, implementation and tuning is straightforward
Notes: Quantitative: moves on foot/crawl. Qualitative: obstructions hinder visibility.

## Slide 78: Chronology around fault line
Too easy
‘Paracomputer’ Schwartz80
BSP Valiant90
LOGP UC-Berkeley93
Map-Reduce. Success; not manycore
CLRS-09, 3rd edition
TCPP curriculum 2010
Nearly all parallel machines to date
“.. machines that most programmers cannot handle"
“Only heroic programmers”
Too difficult
SV-82 and V-Thesis81
PRAM theory (in effect)
CLR-90 1st edition
J-92
NESL
KKT-01
XMT97+ Supports the rich PRAM algorithms literature
V-11
Just right: PRAM model FW77
Nested parallelism: issue for both; e.g., Cilk
Current interest new "computing stacks“: programmer's model, programming languages, compilers, architectures, etc.
Merit of fault-line image Two pillars holding a building (the stack) must be on the same side of a fault line  chipmakers cannot expect: wealth of algorithms and high programmer’s productivity with architectures for which PRAM is too easy (e.g., force programming for locality).

## Slide 79: Telling a fault line from the surface
PRAM too difficult
ICE
WD
PRAM
Sufficient bandwidth
PRAM too easy
PRAM “simplest model”*
BSP/Cilk *
Insufficient bandwidth
*per TCPP
Old soft claim, e.g., [BMM94]: hidden cost of low bandwidth
New soft claim: the surface (PRAM easy/difficult) reveals side W.R.T. the bandwidth fault line.
Surface
Fault line

## Slide 80
Missing Many-Core Understanding
Comparison of many-core platforms for:
Ease-of-programming, and
Achieving hard speedups (over best serial algorithms for the same problem) for strong scaling
strong scaling: solution time ~ 1/#processors for fixed problem size
weak scaling: problem size fixed per processor
Guess what happens to vendors and researchers supported by them once a comparison does not go their way?!
Notes: ----- Meeting Notes (5/29/11 07:01) -----
Fleck 1935. The 'Turing award' of that community is named after him.

## Slide 81: ‘Soft observation’ vs ‘Hard observation’ is a matter of community
In theory, hard things include asymptotic complexity, lower bounds, etc.
In systems, they tend to include concrete numbers
Who is right? Pornography matter of geography
My take: each community does something right. Advantages Theory: reasoning about revolutionary changes. Systems: small incremental changes ‘quantitative approach’; often the case.

## Slide 82: How was the “non-specificity” addressed?
Answer: GvN47 based coding for whatever future application on math. induction coupled with a simple abstraction
Then came: HW, Algorithms+SW
[Engineering problem. So, why mathematician? Hunch: hard for engineers to relate to .. then and now. A. Ghuloum (Intel), CACM 9/09: “..hardware vendors tend to understand the requirements from the examples that software developers provide… ]
Met desiderata for code and coding. See, e.g.:
- Knuth67, The art of Computer Programming. Vol. 1: Fundamental Algorithms. Chapter 1: Basic concepts 1.1 Algorithms 1.2 Math Prelims 1.2.1 Math Induction
Algorithms: 1. Finiteness 2. Definiteness 3. Input & Output 4. Effectiveness
Gold standards
Definiteness: Helped by Induction
Effectiveness: Helped by “Uniform cost criterion" [AHU74] abstraction
2 comments on induction: 1. 2nd nature for math: proofs & axiom of the natural numbers. 2. need to read into GvN47: “..to make the induction complete..”
Notes: HW vendors have a hummer for optimizing incremental changes. However, they now need to deal with a paradigm shift, but having a hummer tends to make everything look to us like a nail.

## Slide 83: Merging: Example for Algorithm & Program
Input: Two arrays A[1. . n], B[1. . n]; elements from a totally ordered domain S. Each array is monotonically non-decreasing.
Merging: map each of these elements into a monotonically non-decreasing array C[1..2n]
Serial Merging algorithm
SERIAL − RANK(A[1 . . ];B[1. .])
Starting from A(1) and B(1), in each round:
compare an element from A with an element of B
determine the rank of the smaller among them
Complexity: O(n) time (and O(n) work...)
PRAM Challenge: O(n) work, least time
Also (new): fewest spawn-joins

## Slide 84: Merging algorithm (cont’d)
“Surplus-log” parallel algorithm for Merging/Ranking
for 1 ≤ i ≤ n pardo
Compute RANK(i,B) using standard binary search
Compute RANK(i,A) using binary search
Complexity: W=(O(n log n), T=O(log n)
The partitioning paradigm
n: input size for a problem. Design a 2-stage parallel algorithm:
Partition the input into a large number, say p, of independent small jobs AND size of the largest small job is roughly n/p.
Actual work - do the small jobs concurrently, using a separate (possibly serial) algorithm for each.

## Slide 85: Linear work parallel merging: using a single spawn
Stage 1 of algorithm: Partitioning for 1 ≤ i ≤ n/p pardo [p <= n/log and p | n]
b(i):=RANK(p(i-1) + 1),B) using binary search
a(i):=RANK(p(i-1) + 1),A) using binary search
Stage 2 of algorithm: Actual work
Observe Overall ranking task broken into 2p independent “slices”.
Example of a slice
Start at A(p(i-1) +1) and B(b(i)).
Using serial ranking advance till:
Termination condition
Either some A(pi+1) or some B(jp+1) loses
Parallel program 2p concurrent threads
using a single spawn-join for the whole
algorithm
Example Thread of 20: Binary search B.
Rank as 11 (index of 15 in B) + 9 (index of
20 in A). Then: compare 21 to 22 and rank
21; compare 23 to 22 to rank 22; compare 23
to 24 to rank 23; compare 24 to 25, but terminate
since the Thread of 24 will rank 24.

## Slide 86: Linear work parallel merging (cont’d)
Observation 2p slices. None larger than 2n/p.
(not too bad since average is 2n/2p=n/p)
Complexity Partitioning takes W=O(p log n), and T=O(log n) time, or O(n) work and O(log n) time, for p <= n/log n.
Actual work employs 2p serial algorithms, each takes O(n/p) time.
Total W=O(n), and T=O(n/p), for p <= n/log n.
IMPORTANT: Correctness & complexity of parallel program
Same as for algorithm.
This is a big deal. Other parallel programming approaches do not have a simple concurrency model, and need to reason w.r.t. the program.